## COUNTY OF HENRICO

VIRGINIA

INTER-OFFICE MEMORANDUM

| TO: | Planning Office | SUBJECT: | LP/POD2006-00012: South River Compounding Pharmacy |
| --- | --- | --- | --- |
| FROM: | Division of Police, Community Policing Unit | DATE: | May 9, 2007 |

### LP/POD2006-00012		South River Compounding Pharmacy		POD-15-06

The Division of Police recommends approval with the below requirements addressed or met.

The Division of Police can’t recommend approval.  Address the items in Section I in order to receive endorsement from this agency.

Based on the information provided at this time, the Division of Police will require the following security measures for this plan prior to receiving an endorsement from this agency.

SECTION I.   ADDRESS THE FOLLOWING ITEMS IN ORDER FOR THE DIVISION OF POLICE TO ENDORSE THIS PLAN:

- Increase the light level within the parking area.  The foot-candle level falls below 0.5 foot-candles in some areas.  The minimum maintained light level should be no lower than 1.0 foot-candles throughout the parking areas, walkways, building entrance and building edge.  Address this item.

- The Illuminating Engineer Society of North America (IESNA) has created standards on security lighting.  The below chart is from the Guidelines for Security Lighting for People, Property, and Public Spaces, IESNA G-1-03.

| Security Locations and Tasks | Illuminance, (Lux)/FC (Horizontal) - Average | Illuminance Lux/FC (Vertical) | Footnotes on special considerations | Ratios (avg to minimum) |
| --- | --- | --- | --- | --- |
| Supermarket, Major Retail Parking |  |  |  |  |
| Parking lot | (30)/ 3.0 | (a) | -- | 4:1 |
| Low activity – close in parking | (50)/ 5.0 | (a) | (k) | 4:1 |

Footnotes: (a) Vertical illuminance of 5-8 lux or values that produce a uniformity ratio of no more than 4:1 (25% of horizontal illuminance; (k)  Size of parking area determined by estimated customer count.

SECTION II.  IMPLEMENT THE FOLLOWING SECURITY STANDARDS:

### Landscaping –  It appears the landscape plan meets the below standards:

- All shrubs and trees should be trimmed to allow for maximum visibility to and from the site and from within the site.

- Shrubs should have a natural growth height of no more than 2 ½ to 3 feet, or be maintained at this height, especially when located along an entrance, walkway or parking area.

- Trees should have a natural growth with limbs at least 4 feet off the ground, or be maintained with the canopy raised, especially when located along a building entrance, walkway or parking area.

- The location of light poles and their relationship to the trees throughout the parking lot and along the building edge needs to be considered.  The two should not be located in the same area, as illumination will be reduced as the tree matures.

Lighting – It appears the lighting plan meets the below standards:

- The lights throughout the site should be the same.  The emphasis is to have the same color of light (white or orange/yellow) throughout.  This will provide good color rendition, help with visibility and reduce contrasts.  Metal Halide is preferred.

- All light fixtures need to be full cut-off.

- The type of light fixture the Division of Police requires is one that puts the light down on the ground, versus horizontally and up in the air.  Many of the decorative light fixtures put the light everywhere but where you want it, which is on the ground.  If decorative fixtures are installed, they should have the bulb in the top casing of the fixture so that the light will be directed towards the ground (see photo).  This will also avoid glare because you don’t actually see the bulb.

- Lighting is one of the most economical and effective forms of crime prevention available.  Lighting must be even and uniform and not produce dark areas or sharp contrasts for concealment.

- In creating uniform lighting, consider:

- type of fixture				c)  the direction of the light

- the height of poles			d)  spacing of fixtures

While our requirements for the endorsement of the plan does not guarantee a crime-free environment, it is our experience that the application of the concepts of Crime Prevention Through Environmental Design (CPTED) will reduce the opportunity for crime to occur and will enhance the quality of life.  Should you have any questions or comments, contact me at (804) 501-5370 or van06@co.henrico.va.us.

Kim Vann

Planner III - CPTED

Crime Prevention Specialist

# Text boxes

The white globe visible to the eye in this post top fixture is decorative; the light bulb is in the top of the fixture.