COUNTY OF HENRICO

VIRGINIA

INTER-OFFICE MEMORANDUM

| TO: | Planning Office | SUBJECT: | POD2007-00113: Poplar Springs Baptist |
| --- | --- | --- | --- |
| FROM: | Division of Police, Community Policing Unit | DATE: | July 2, 2007 |

POD2007-00113	Poplar Springs Baptist		POD-52-07

The Division of Police recommends approval with the below requirements addressed or met in Section I.  Written compliance or new plans with details shown/stated will meet our requirements.

The Division of Police can’t recommend approval at this time.

___________________________________________________________

SECTION I.

ADDRESS THE FOLLOWING ITEMS IN ORDER FOR THE DIVISION OF POLICE TO ENDORSE THIS PLAN:

- Access into the new building should be limited to the main entrance only.  On all days other than Sunday, all exterior doors should be locked.

- Provide a reinforced window or vision panel on the exterior stairwell door (stairwell #2) to provide visibility to or from this space.

SECTION II.  Implement the following security standards:

### Landscaping:  No schematic plan was submitted

- The landscape plan should show the light pole locations as well.

- The location of light poles and their relationship to the trees throughout the parking lot and along the building edge needs to be considered.  The two should not be located in the same area, as illumination will be reduced as the tree matures.

- All shrubs and trees should be trimmed to allow for maximum visibility to and from the site and from within the site.  Shrubs should have a natural growth height of no more than 2 ½ to 3 feet, or be maintained at this height, especially when located along an entrance, walkway or parking area.

- Trees located around buildings, walkways and parking areas should have a natural growth habit that is a tree-form, non-pyramidal shape tree.  If this can’t be done in various areas, the canopy of the trees should then be raised at least 4 feet from the ground as they mature.

## Lighting – no lighting plan submitted

- The lighting plan should be submitted with the plan of development.

- The minimum maintained light level should be no lower than 1.0 foot-candles throughout the parking areas, walkways, building entrance and building edge.

- The lamps throughout the site should be the same.  The emphasis is to have the same color of light (white or orange/yellow) throughout.  This will provide good color rendition, help with visibility and reduce contrasts.  Metal Halide is preferred.

- All light fixtures need to be full cut-off.

- The type of light fixture the Division of Police requires is one that puts the light down on the ground, versus horizontally and up in the air.  Many of the decorative light fixtures put the light everywhere but where you want it, which is on the ground.  If decorative fixtures are installed, they should have the lamp in the top casing of the fixture so that the light will be directed towards the ground (see photo).  This will also avoid glare because you don’t actually see the lamp.

- Lighting is one of the most economical and effective forms of crime prevention available.  Lighting must be even and uniform and not produce dark areas or sharp contrasts for concealment.

- In creating uniform lighting, consider:

- type of fixture				c)  the direction of the light

- the height of poles			d)  spacing of fixtures

## INTERIOR

- Provide access control (physical security) on all exterior doors.  Consideration should be given to alarming the building.

- Install a wide-angle peephole or one-way window on the rear doors, employee entrance doors and delivery doors.

- The following measures should be in place to increase the security for side, rear or storage doors:

  - Metal or solid core			c)  Deadbolt locks

  - Metal frames				d)  Reinforced strike plates

- Equip the doors with self-locking devices that will engage immediately when the door has been closed.

- The glass on all entrance doors should be free of tinting for added visibility into and out of the building.

____________________________________________________________________________________

The Division of Police supports and implements Crime Prevention Through Environmental Design (CPTED), which is the theory that the proper design and effective use of the built environment can lead to a reduction in the incidence and fear of crime and an improvement in the quality of life.

The following characteristics need to be in place at this site.

- Natural Surveillance.  Provide natural surveillance throughout the site, especially to parking areas, buildings, building entrances, walkways, etc.  Natural surveillance is the placement of physical features, activities and people in such a way as to maximize visibility.

- Natural Access Control. Provide natural access control throughout the site.  Natural access control is the physical guidance of people coming and going from a space by the judicial placement of entrances, exits, fencing, landscaping and lighting.   The goal is to guide people where you want them to go and how you want them to get there.

- Territorial reinforcement.  Territorial reinforcement is the use of physical attributes that express ownership, such as fences, pavement treatments, art, signage and landscaping.  The goal is to promote ownership and pride in where you live and work.

- Maintenance.  Allows for the continued use of space for its intended purpose.  It also serves as an additional expression of ownership.

For more information log on to www.henricopolice.org and click on CPTED

While our requirements for the endorsement of the plan does not guarantee a crime-free environment, it is our experience that the application of the concepts of Crime Prevention Through Environmental Design (CPTED) will reduce the opportunity for crime to occur and will enhance the quality of life.  Should you have any questions or comments, contact me at (804) 501-5370 or van06@co.henrico.va.us.

Kim Vann

Planner III - CPTED

Crime Prevention Specialist

# Text boxes

The white globe visible to the eye in this post top fixture is decorative; the lamp is in the top of the fixture.