## COUNTY OF HENRICO

VIRGINIA

INTER-OFFICE MEMORANDUM

| TO: | Planning Office | SUBJECT: | POD2007-00154: East Area Middle School |
| --- | --- | --- | --- |
| FROM: | Division of Police, Community Policing Unit | DATE: | September 5, 2007 |

POD2007-00154		East Area Middle School		POD-65-05

The Division of Police recommends approval with the below requirements addressed or met.

The Division of Police can’t recommend approval at this time.

Implement the following security standards:

- The landscape plan shows the proposed locations of light poles within the drives, parking lots and bus loop.  This helps as both conduit is planned, as well as the location of trees within the property.  This addresses the comment below.

The location of light poles and their relationship to the trees throughout the parking lot and along the building edge needs to be considered.  The two should not be located in the same area, as illumination will be reduced as the tree matures.

- Visibility throughout the site is one aspect of what the landscape materials should be providing.  The following should be in place:

- All shrubs and trees should be trimmed to allow for maximum visibility.

- Trim bushes and shrubs away from buildings, especially by doors or windows, to increase visibility.

c)  Shrubs should have a natural growth height of no more than 2 ½ to 3 feet.

d)  Trees should have a natural growth with limbs at least 4 feet off the ground.

Lighting – not provided at this time, but consideration should be given to the following:

- The minimum maintained light level should be no lower than 1.0 foot-candles throughout the parking areas, walkways, building entrance and building edge.

- The Illuminating Engineer Society of North America (IESNA) has created standards on security lighting. The below chart is from the Guidelines for Security Lighting for People, Property, and Public Spaces, IESNA G-1-03.

| Security Locations and Tasks | Illuminance, Lux/FC (Horizontal) - Average | Illuminance, Lux/FC (Vertical) | Footnotes on special considerations | Ratios (avg to minimum) |
| --- | --- | --- | --- | --- |
| Schools and Institutions |  |  |  |  |
| General parking | 30/ 3.0 | (a) | (l) | 4:1 |
| Sidewalks & footpaths | 10/ 1.0 | (a) | (l) | 4:1 |

Footnotes:  (a)  Vertical illuminance of 5-8 lux or values that produce a uniformity ratio of no more than 4:1 (25% of horizontal illuminance);  (l) For special events, parking lots and grounds should be lighted 2 hours prior to 2 hours after the event

- The lamps throughout the site should be the same.  The emphasis is to have the same color of light (white or orange/yellow) throughout.  This will provide good color rendition, help with visibility and reduce contrasts.  Metal Halide is preferred.

- All light fixtures need to be full cut-off.

- The type of light fixture the Division of Police requires is one that puts the light down on the ground, versus horizontally and up in the air.  Many of the decorative light fixtures put the light everywhere but where you want it, which is on the ground.  If decorative fixtures are installed, they should have the lamp in the top casing of the fixture so that the light will be directed towards the ground (see photo).  This will also avoid glare because you don’t actually see the lamp.

- Lighting is one of the most economical and effective forms of crime prevention available.  Lighting must be even and uniform and not produce dark areas or sharp contrasts for concealment.

- In creating uniform lighting, consider:

- type of fixture				c)  the direction of the light

- the height of poles			d)  spacing of fixtures

While our requirements for the endorsement of the plan does not guarantee a crime-free environment, it is our experience that the application of the concepts of Crime Prevention Through Environmental Design (CPTED) will reduce the opportunity for crime to occur and will enhance the quality of life.  Should you have any questions or comments, contact me at (804) 501-5370 or van06@co.henrico.va.us.

Kim Vann

Planner III - CPTED

Crime Prevention Specialist

# Text boxes

The white globe visible to the eye in this post top fixture is decorative; the lamp is in the top of the fixture.