## COUNTY OF HENRICO

VIRGINIA

INTER-OFFICE MEMORANDUM

| TO: | Planning Office | SUBJECT: | POD2007-00168: Southall at Crossridge |
| --- | --- | --- | --- |
| FROM: | Division of Police, Community Policing Unit | DATE: | September 5, 2007 |

POD2007-00168		Southall at Crossridge			POD-4-06

The Division of Police recommends approval with the below requirements addressed or met in Section I.

The Division of Police can’t recommend approval at this time.  Provide written compliance or new plans with details shown/stated to address or meet the items in Section I for an endorsement of this plan.

SECTION I.

ADDRESS THE FOLLOWING ITEMS IN ORDER FOR THE DIVISION OF POLICE TO ENDORSE THIS PLAN:

- Lighting cut sheets were provided but no photometric plan was submitted.  Provide this plan.

- Lighting should meet the following:

- Parking lot lighting should be at a minimum-maintained level of 1.0 foot-candles.  This lighting should also spill over to the front yards of the units.

- Pedestrian level lighting would be provided along any walkways or paths, especially where the parking lot lighting is not available.

  - Clarify where the security fence will be on the site.  It appears that it is just sections of a fence and not a continuous fence line.

4.  Landscaping should meet the below standards.

SECTION II.  Implement the following security standards:

Lighting – no lighting plan submitted

- Parking lot lighting should be at a minimum-maintained level of 1.0 foot-candles.  This lighting should also spill over to the front yards of the units.

- Pedestrian level lighting would be provided along any walkways or paths, especially where the parking lot lighting is not available.

- Consideration should be given to the location of the light poles and tree canopy’s so there is no conflict between the two.  The two should not be located in the same area, as illumination will be reduced as the tree matures.

- The lights throughout the complex should be the same.  The emphasis is to have the same color of light (white or orange/yellow) throughout.  This will provide good color rendition, help with visibility and reduce contrasts.  Metal Halide lighting is preferred.  The white light of this bulb will complement the likely incandescent bulb property owners will install in the porch lights.

- The following areas need to have lighting provided:

  - Walkways in front of the units

  - Front of the units

    - Rear loading garages – the drive and rear of these units must have increased lighting

- The rear loading garages create alleys within this complex.  Effectively illuminating these areas is a concern for the Division of Police.

Lighting must be provided, as this will be the main way in and out of the units for most residents.  Consider the following:

  - Utilize full cut off fixtures for poles or wall-mounted lights.

  - Install light poles whenever possible.

  - If light poles can’t be used due to the design of the drive, install wall mounted light fixtures that are full cut-off.  This will help in providing effective lighting, while not putting light in the bedrooms of the units facing the alley.

- The type of light fixture we require is one that puts the light down on the ground, versus horizontally and up in the air.  Many of the decorative light fixtures put the light everywhere but where you want it, which is on the ground.  If you install fixtures that are decorative in design, install the type of fixture where the bulb is in the top of the ‘globe’. (see photo) This will place the light down and avoid glare because you don’t actually see the bulb.

- Lighting is one of the most economical and effective forms of crime prevention available.  Lighting must be even and uniform and not produce dark areas or sharp contrasts for concealment.

- In creating uniform lighting, consider:

- type of fixture				c)  the direction of the light

- the height of poles			d)  spacing of fixtures

Landscape plan

1.   Maintain shrubs away from buildings, especially by doors or windows to increase visibility. Maintain the recommended heights for shrubs and trees to allow for maximum visibility to and from the site and from within the site.

- Trees located around buildings, walkways and parking areas should have a natural growth habit that is a tree-form, non-pyramidal shape tree.  If this can’t be done in various areas, the canopy of the trees should then be raised at least 5 feet from the ground as they mature.

- Shrubs should have a natural growth height of no more than 2 ½ to 3 feet, or be maintained at this height, especially when located along an entrance, walkway or parking area.

While our requirements for the endorsement of the plan does not guarantee a crime-free environment, it is our experience that the application of the concepts of Crime Prevention Through Environmental Design (CPTED) will reduce the opportunity for crime to occur and will enhance the quality of life.  Should you have any questions or comments, contact me at (804) 501-5370 or van06@co.henrico.va.us.

Kim Vann

Planner III - CPTED

Crime Prevention Specialist

# Text boxes

The white globe visible to the eye in this post top fixture is decorative; the lamp is in the top of the fixture.