The Engineering Division has completed its review of the above referenced project and has the following comments:

1.	Your previous submission showed disturbance under 2500 square feet.  With the addition of sidewalk and additional land grading, your area of disturbance is now greater than 2500 square feet.  Full design requirements are now in effect, including water quality and 50/10 detention.  I have attached separately our general Engineering review checklist for you to consult as a guide to see what information you will need to show on your plans.

2.	Looking at your plans, you will be eligible to contribute to the Environmental Fund if your removal requirement is less that 0.5 lbs.  You need to update your sheets from your first submission however, as you have added additional impervious area that is not reflected in your water quality calculations.  You will also need to include worksheet 3.6 – with at note at the bottom that compliance is met with a contribution to the Environmental Fund.

3.	Your previous plan submittal, while showing 50/10 calculations, does not indicate that the 50/10 requirement is met.  Unless waived by Public Works, you must show that the additional runoff is detained to 10-year pre conditions.

4.  Additional comments may follow upon review of a subsequent submittal.

Reviewed by:	John Woodburn

Date Reviewed:	16 October 2007

Phone Number:	501-5851		Revised 1/2/07