# GENERAL COMMENTS:

- Plans must be prepared by a licensed engineer or surveyor.

- Provide the engineer’s/surveyor’s/landscape architect’s name, address, e-mail address, telephone number, and fax number on the plan.

- Provide the owner’s and/or developer’s name, address, e-mail address, telephone number, and fax number on the plan.

- The minimum size lettering allowable on construction plans is 1/8”.

- Reference the source of all topography on the cover sheet.

- The latest copy of the Standard Construction Notes/Details Sheet (revised 4/14/06) must be included with the plans.

- Provide a complete drainage area map, in acres, including all off-site drainage areas, supported by an outlined contour map.

- Provide an itemized list of all subdivision bond quantities, to include the following:

All of the following

Linear feet of storm sewer by diameter			Number of flared end sections

Number of inlets			Number of manholes

Linear feet of road by road classification			Linear feet of curb and gutter by type

Number of monuments			Number of street signs

Number of headwalls			Linear feet of guardrail

Linear feet of sidewalk			Drainage area to basin (not site area)

BMP outlet structure size			Guardrail end treatment

Underdrains

ADDITIONAL COMMENTS:

ROAD DESIGN:

- Provide classifications for all roads.

Include the projected vehicles per day (VPD) for all roads.

Provide the typical section for all roads as provide in the Design Manual

Provide pavement sections for all roads that match the road classification.

- Provide a minimum 50’ vertical curve to tie the proposed road grade into the existing edge of pavement at intersections.

- Provide K-values for all vertical curves in accordance with the Design Manual.  Also, show the design speed for all roadways.

- A six (6) feet wide pedestrian shelf is required behind all curb and gutter in the County right-of-way.

- Curb and gutter, pavement widening, and related drainage items are required along all frontage on public rights-of-way.

- Show the full typical section for pavement widening on the plans, showing the centerline of pavement, right-of-way limits, proposed pavement width, elevations, grade percentage, and underdrains.

- Provide cross-sections, at a minimum of 25 feet intervals, showing the existing and proposed pavement elevations throughout the limits of all pavement widening.  Show existing and proposed cross-slopes, as well as profiles for the edge of pavement, top of curb, the centerline of roads, pavement overlays, and milling (1”:1’ vertical;  1”:10’ horizontal).

- Pavement cross-sections for road widening must meet the following criteria:

Minimum proposed cross slope is 1.5%

Maximum proposed cross slope is 3.0%

There can be no more 1.0% difference between the existing and proposed pavement cross slopes

- Pavement overlays, pavement buildup, and/or milling, must be clearly shown on the plans.  When overlays are required in curb and gutter sections, the curb lanes must be edge milled prior to the overlay to eliminate pavement build-up at the edge of pavement and to provide a smooth tie-in to the edge of gutter.  In ditch sections, shoulders and driveways must be tied into the finished elevation of the pavement overlay.

- Provide cross-sections of the roadway showing the limits of pavement, curb and gutter, guard rail, end treatments, fill slopes, easement limits, and any drainage structures at all locations where Traffic Engineering is requiring guard rail.

- UD-4 underdrains are required along the entire length of all proposed roads and/or road widening within the public right-of-way unless waived by the Director of Public Works.

- UD-2 underdrains are required in all raised grass medians and islands located in the public right-of-way.

- CD-1 underdrains are required for all vertical sags located within the public right-of-way.

- Show the location of all underdrains on the plans.

- Private roads and driveways within multi-family developments should be constructed in accordance with County roadway pavement standards.  Provide projected vehicles per day and pavement sections for all private roads and driveways.

ADDITIONAL COMMENTS:

  - Re-evaluate whether a CG-11 is necessary into the Wellness Center / Disco Sports.

  - Clarify the type of curb and gutter on the interior sides of the islands closest to the fuel center.

GRADING:

- The following issues must be addressed regarding lot grading:

An overall (one page) lot drainage map must be included in all subdivision plans at a minimum scale of 1”=200’, and must include the following:

Flow direction arrows for each lot

Show the minimum finished floor elevation (MFF) for each lot based on the required grading to ensure proper drainage.  House locations must be shown for all lots with grading plans.  The MFF must be at least 3.0 feet above finished grade.

Lots which have special building permits requirements must be identified on the construction plans as follows:  NBP1, NBP2, NBP3.

NBP1 – All areas of required grading (including low-lying areas and wetlands to be impacted) and drainage swales, as indicated on the plans, shall be constructed concurrently with the road construction.  Certification of the construction by the engineer of record is required prior to issuance of Building Permits for lots identified as NBP1.  The required certification must be attached to the Building Permits for these lots.  This applies to lots      .

NBP2 – All lots that include storm sewer.  A certified plat identifying the storm sewer easement and the location of the installed drainage improvements must be submitted by the engineer of record prior to the issuance of a Building Permit for those lots identified as NBP2.  (NOTE:  Lots not built on by the time of road acceptance must have the easements staked and flagged for review prior to road acceptance). The required certification must be attached to the Building Permits for these lots.  This applies to lots      .

NBP3 – All lots that contain or are adjacent to lots that contain sediment basins/traps.  Building permits will be delayed until the sediment basins/traps are removed.

Add a note to the plans stating that all lots are to be graded at the time of road construction.

Provide the Building Permit Special Requirements table (a summary of the above information) on the cover sheet.

- Show all  existing and  proposed contours at a maximum interval of two feet (i.e.:  road fill/cut, lot grading, wetland/WOUS grading, etc.).

ADDITIONAL COMMENTS:

CURB AND GUTTER / STORM SEWER:

- Curb and gutter is required on both sides of each road in the subdivision if any of the following apply:

There is less than 0.5% grade within any block of any road in the subdivision.

25% of the roads within a subdivision have 1.0% or flatter grade.

25% of the lots within a subdivision have less than 80 feet of road frontage.

- Henrico County Curb and Gutter is required around all temporary cul-de-sacs.

- Roll-faced curb is only allowed on roadways that are Class I-IV (0-1000 VPD).  The pavement width must be at least 32’ (36’ f/c-f/c).

- If roll-faced curb is used, two (2) inlets with 100% collection efficiency must be provided on both sides of the road on descending grades before all cul-de-sacs with descending grades.

- Provide CG-12 curb ramps at all intersections where there is existing or proposed sidewalk.  Provide depressed curb at intersections if no sidewalk is proposed.

- Provide top of curb elevations around:   all cul-de-sacs   all curb returns

- All entrances must be CG-9D and labeled as such on the plans.

- Roll-faced curb is not allowed for parking areas.

- The maximum depth of flow along roll-faced curb is four inches.

- Curb cuts are not permitted along drive aisles.

- All medians less than six feet wide must be VDOT Std. MS-1.  For turn lanes being constructed on existing roads, the old median must be removed entirely and the solid raised median poured on the asphalt base course in accordance with the standards for MS-1 Median.  Standard MS-1A or variations of the same are not be permitted.

- Valley gutters are not allowed in the public right-of-way.

- Provide profiles based on field-run elevations for all storm sewers located outside of the right-of-way limits.

- Provide an itemized list (including descriptions) of all drainage structures on the plan.

- Stormwater must be collected on-site in curb drop inlets.

- Provide the following information for all curb and gutter/storm sewer systems:

Depth and spread in all gutters based on a two-year storm.

Length of inlet throats (sized for 10-year storm)

Inlet placement based on the maximum allowable spread during a 2-year storm

Type of material (RCP Class III or better in County easements or right-of-way)

Diameter (minimum 15 inches)

Velocity (minimum allowable of 2 fps for 2-year storm)(maximum of 15 fps for 10-year storm)

Capacity (based on 10-year storm event)

Hydraulic grade line computations noting elevations at key points (drop inlets, manholes, etc.)(indicate where inlet shaping is to take place) including details showing how the starting water surface elevation was obtained

Concrete flume transition details from curb to ditch

Details of non-standard structures

Longitudinal slope (minimum allowable is 0.3%)

Maximum length between structures is 300 feet for pipes less than 48” diameter

Indicate whether inlet shaping, steps, and/or O-ring pipe are proposed

Provide storm sewer information/calculations in tabular format on the plans.

- Provide adequate cover for all storm sewers.  The minimum allowable cover is:

Nine (9) inches for storm sewer in the right-of-way

Six (6) inches for storm sewer in easements

- Provide the following information for all culverts:

Inverts based on field-run elevations

Lengths

Type (RCP Class III or better in County easements or right-of-way)

Headwater calculations

Inlet and outlet protection

Outlet velocity (10-year storm)

Diameter

Design cover

Provide the completed VDOT standard culvert form

- DI-3 series inlets must be designed so that the minimum depth of the inlets is equal to or greater than the diameter of the pipe plus 2.67’ (32”).

- DI-4 series inlets are required for all storm sewers greater than 30” diameter.

- The maximum throat length for curb drop inlets in cul-de-sacs is six feet.

- Drop inlets are not allowed in the radius of intersections.

- No more than 0.5 cfs may be directed onto a public right-of-way during a 10-year storm.

- Provide details for JB-1 and any non-standard VDOT inlets.

- All outlet protection must be designed in accordance with Std. & Spec. 3.18 of the Virginia Erosion and Sediment Control Handbook, Third Edition, 1992.

- Show the dimensions for all outlet protection (length, width, and depth, including filter fabric lining).

ADDITIONAL COMMENTS:

  - Comment No. 30 is in regard to the entrances off of Starling Drive.

  - Comment No. 35 is in regard to curb cuts in island near STM-211.

  - Comment No. 41 is in regard to P-202 a 36” pipe with a length of 368 feet.

  - Show access points/manholes at the inlets and outlets of Raintank # 1 & 2.  STM-104 is acceptable for one of the inlets into Raintank # 1.

  - Provide pre and post development Q10 values that drain off-site to Greenbrier Hills.  Demonstrate that not increasing.

  - Provide a detail of trench drain.  Provide a concrete structure where trench drain in loading dock and 15" RCP meet.

  - Provide a detail on plan showing Henrico County 1.5’ wide gutter pan transitioning to a grate that is 2’ wide.

  - Clarify where STM-101A and STM-101B are in plan view.  They are referenced on Sheet C8.03.  Are they STM-102 and STM-103 in plan view?  Make the appropriate changes for consistency.

ON-SITE CHANNELS / WETLANDS:

- All channels with less than 100 acres of contributing drainage area must be piped or otherwise eliminated.  If the environmental regulatory agencies will not issue a permit to impact jurisdictional channels that fall under this policy, the standard form letter attached to the September 12, 2005 policy letter must be completed and submitted and copies sent to the appropriate environmental regulatory agency.

- Open channels, except for roadside ditches, are not permitted unless specifically mandated by local, state and/or federal requirements.

- Provide a typical yard swale detail.  All yard swales must meet the following criteria:

Longitudinal slope must be at least 1%

Minimum side slope ratio is 3:1

Maximum depth is 18 inches

No longer than 150 feet without a drop inlet

- Provide a cross-section for all channels (existing and proposed, natural and man-made) used for stormwater conveyance.  Additional cross-sections will be required where channel characteristics change.  The following information must accompany each cross-section:

Depth

Side slopes (no steeper than 3:1 for proposed channels)

Channel Lining (with Mannings “n” value)

Flow elevations for the 2-year, 10-year and 100-year (if applicable) storm events

The limits of wetlands on both sides of the channel

Longitudinal slope (minimum 1.0% for proposed non-paved channels, minimum 0.3% for proposed paved channels)

Scale must be 1”:1’ Vertical, 1”:5’ Horizontal

- The following information and supporting calculations must be provided for each cross-section provided for all channels (existing and proposed, natural and man-made) used for stormwater conveyance:

Q2		Q10		Q100		Qcapacity

V2		d10

- The minimum allowable V2 for paved channels is 2 fps.

- Provide a profile based on field-run elevations for all channels used for stormwater conveyance.

- The following information and supporting calculations must be provided for all wetland systems:

Q10		Qcapacity (within the limits of the wetlands)		V2		Vallowable

The limits of the 10-year storm must be delineated on the plan view in relation of the limits of the wetlands.

Demonstrate that the wetland system has an outlet and will not act as an impoundment.

Provide a profile based on field-run elevations for all wetland systems used for stormwater conveyance.

- Provide a profile of the roadside ditches on the Road Profile Sheet.

ADDITIONAL COMMENTS:

OFF-SITE OUTFALLS/ADEQUACY:

- Complete the “Receiving System Adequacy” table on the ESC/ESA sheet.

- For all existing channels, wetland systems, and/or culverts used as an outfall, provide the following information:

A profile based on field-run elevations beginning at the project’s discharge location and extending no less than 150 feet in length downstream of the property boundary.  The profile may need to be extended to include all identified channel/wetland/culvert constrictions beyond 150 feet.

Cross-sections every 50 feet along the required length of the profile at the most constricted locations.

Identification of the size, material and type of all structures along the profile

Scale must be 1”:1’ Vertical, 1”:5’ Horizontal

- For all existing storm sewer systems used as an outfall, provide the following information:

A profile based on field-run elevations beginning at the project’s discharge location and including the existing pipe to the first structure (inlet, manhole, etc.) downstream of the project boundary.

Identification of the size, material and type of all structures along the profile

- To verify the adequacy of a channel used as an outfall, the following information must be provided:

Q2		Q10		Qcapacity		V2		Vallowable

The 10-year storm flow is not contained within the channel.  Therefore, the channel is not adequate.

The velocity associated with the 2-year storm flow exceeds the allowable velocity. Therefore, the channel is not adequate.

- To verify adequacy of a wetland system used as an outfall, the following information must be provided:

Q10		Qcapacity (within the limits of the wetlands)		V2		Vallowable

The 10-year storm flow is not contained within the limits of the wetland system.  Therefore, the wetland system is not adequate.

The velocity associated with the 2-year storm flow exceeds the allowable velocity.  Therefore, the wetland system is not adequate.

The wetland system does not appear to have an outlet and will act as an impoundment. Therefore, the wetland system is not adequate.

- To verify adequacy of a storm sewer system or culvert used as an outfall, the following information and supporting calculations must be provided:

Q10		Qcapacity

Submit the storm sewer design spreadsheets

Hydraulic gradeline calculations for the 10-year storm

Culvert analysis for the 10-year storm using standard VDOT form

The existing storm sewer or culvert does not have adequate capacity for the 10-year storm flow.  Therefore, the existing storm sewer or culvert is not adequate.

- In order to use the floodplain as an outfall, the following information must be provided:

Stormwater must be discharged at the limits of the floodplain using an energy dissipator in accordance with Minimum Standard 9.01 of the Henrico County Environmental Program Manual, OR an adequate channel must be provided from the project’s discharge location to the existing channel in the floodplain.  The following information must be provided:

Q10		Qcapacity		V2		Vallowable

The 10-year storm flow is not contained within the channel.  Therefore, the outfall is not adequate.

The velocity associated with the 2-year storm flow exceeds the allowable velocity. Therefore, the channel is not adequate.

The stormwater does not enter the floodplain in a sheet flow manner.  Therefore, the outfall is not adequate.

- Energy Dissipators in accordance with Minimum Standard 9.01 of the Henrico County Environmental Program Manual must be provided where concentrated runoff enters the SPA.

- Proposed level spreading devices must be in accordance with Minimum Standard 9.01 of the Henrico County Environmental Program Manual.

- The plan must include appropriate details of the Energy Dissipators in accordance with Minimum Standard 9.01 of the Henrico County Environmental Program Manual.

ADDITIONAL COMMENTS:

- Comment Nos. 61, 63 & 66 are in regard to the existing pipes for outfalls STM-301 and STM-100 to the first structure downstream of property boundary.  Include profiles, calculations, show in plan view and update RSA table accordingly.

STORMWATER MANAGEMENT:

- The following worksheets (if checked) must be corrected/completed and submitted to the Department of Public Works and also included in the plans.

Worksheet 2.1 – Program Implementation		Worksheet 3.01 – Situation One,

Worksheet 2.2 – Urban Management Area Opt In		Worksheet 3.02 – Situation Two,

Worksheet 2.3 – Environmental Fund Contribution			Worksheet 3.03 – Situation Three,

Worksheet 3.04 – Situation Four, or

Worksheet 3.06 – Compliance		Worksheet 3.05 – Situation Five

BMP design worksheet

- Provide an overall/master plan showing the phasing of sections and proposed BMP locations with supporting calculations.

- The appropriate Stormwater Pollutant Removal worksheet is needed to determine whether the calculated pollutant removal requirement must be achieved through 1) a contribution to the Environmental Fund or participation in a regional BMP or 2) must be achieved in an on-site BMP or a regional BMP.

- The plan must demonstrate that the calculated pollutant removal requirement is achieved in an on-site BMP or a regional BMP.

- The calculated pollutant removal requirement must be achieved through a contribution to the Environmental Fund or participation in a regional BMP.

- Contributions to the Environmental Fund must be made prior to plan approval.

- Contributions to the Environmental Fund must be made prior to recordation of the subdivision.

- This project falls within the limits of a 50/10 detention area.  Provide supporting calculations to show that the post-developed peak flow from the site for a 50-year storm event does not exceed the pre-developed peak flow rate for a 10-year storm event.

- Complete the 50/10 detention requirements summary table on the ESC/ESA sheet.

- Provide the following information for all 50/10 detention basins:

Construction details for the basin, embankment, and outlet devices

Storm routings for the 10-, 50-, and 100-year storm

Delineate the normal pool and 100-year storm elevations

Delineate the 50-year storm elevation for all 50/10 detention basins

Contributing drainage areas

Calculations for time of concentration, curve number, and/or runoff coefficients

Complete input for hydrograph generation

Stage/storage table

Stage/discharge for each component of the outlet structure

Composite stage/discharge table

Outlet control analysis

Provide evidence that the 50-year storm will remain on the site until it reaches the basin

Side slopes must be clearly labeled on the plans.

- Provide the following information for all BMP basins:

Construction details for the basin, embankment, and outlet devices

Delineate the normal pool and 100-year storm elevations

Contributing drainage areas

Stage/storage table

Side slopes must be clearly labeled on the plans.

- Existing wet ponds in single-family residential subdivisions are permitted to remain, however, the subdivision must be designed in such a manner that the existing pond(s) meet each of the following criteria (checked items must be addressed):

The pond(s) must be located in common area.

There must be at least 50 feet between the normal pool elevation of the pond(s) and any buildable area.

A 20’ wide access easement must be provided to the pond(s).  The easement must be completely on one property (it can not straddle a property line).  The access easement must provide access to all inlet and outlet structures in the pond(s).

Show the normal pool elevation in the pond(s).

A 16’ wide drainage easement is required from all inlets to the outlet(s) if the pond contains public water.

Provide the 10-year, and 100-year elevations in the pond(s).

Show that the pond has an adequate outfall in accordance with MS-19.

Provide a dam break analysis if the dam is constructed of fill.

- All BMPs must be designed in accordance with the minimum standards set forth in the Henrico County Environmental Program Manual.

- The BMP/SWM facility must be located as follows:

The highest continuous contour on the inside of the basin must be located at least 25’ from the right-of-way limits for commercial projects.

The highest continuous contour on the inside of the basin must be located outside of the front yard setback for subdivisions and must be at least 25’ from the right-of-way in the side yard.

Structural BMPs that are visible from the right-of-way must be located at least 25’ from the right-of-way limits.

- Provide a maintenance schedule for all manufactured BMP structures on the plans.

- Clearly label the dimensions of all BMPs on the plans.

- A BMP maintenance fee of $100.00 per lot is required prior to recordation for subdivisions that drain to a BMP that will be maintained by a Homeowners Association.  This does not apply to wet ponds since the County assumes no maintenance responsibility for wet ponds.

- To evaluate whether or not dams/impoundments are subject to the Virginia Dam Safety Act, Article 2, Chapter 6, Title 10.1 of the Code of Virginia and Dam Safety Regulations, the following information must be provided:

dam height (vertical distance from the streambed at the downstream toe to the top of dam)

the impoundment capacity (the volume capable of being impounded at the top of the dam)

- The dam/impoundment appears to be exempt from the Virginia Dam Safety Act, Article 2, Chapter 6, Title 10.1 of the Code of Virginia and Dam Safety Regulations because:

the dam height is less than 6 feet, or

the capacity is less than 50 acre-feet and the dam height is less than 25 feet, or

the capacity is less than 15 acre-feet and the dam height is more than 25 feet

- The dam/impoundment appears to be subject to the Virginia Dam Safety Act, Article 2, Chapter 6, Title 10.1 of the Code of Virginia and Dam Safety Regulations.  Regulated dams/impounding structures cannot be constructed or altered prior to issuance of a Virginia Soil and Water Conservation Board construction permit. Contact the Virginia Department of Conservation and Recreation at (804) 371-6095.

- If the dam height is greater than three (3), a geotechnical certification must be submitted in accordance with Section 3-14 of the Henrico County Design Manual stating that construction compaction requirements have been achieved.  This must be submitted as part of the BMP as-built certification prior to ESC bond release.

ADDITIONAL COMMENTS:

  - Regarding Comment Nos. 78 & 79, re-evaluate the table and 50/10 calculations.  The Q-10pre calculations are based on 11.0 acres while the water quality worksheets and cover sheet claim a 12.53 acre site.  The Q10-PRE needs to be based on a site area of 12.53 acres not 11.0 acres.  Need to account for the on-site acreage adjacent to Greenbrier Hills that bypasses 50/10 detention structures.  Make the appropriate changes.

  - Provide a cross-section detail of the Raintank showing the slope.

  - On Sheet C8.04, under the proposed condition heading update ANEW.  The bypass drainage area is not 0.86 acres.

  - On Sheet C8.04 update the drainage area to UDS # 1 to include the southwest corner of proposed parking.  It should be consistent with Sheets C3.01 and C5.03.

FLOODPLAIN:

- This site contains a 100-year floodplain as designated by:

FEMA as Zone A

Comprehensive Drainage Study (CDS)

- This site contains a 100-year floodplain associated with a stream that has at least 100 acres of drainage area.  The presence of this stream indicates a portion of this site is subject to flooding during a 100-year storm event.  Therefore, the associated floodplain and flood elevation must be reflected in the design of this development.

- The elevation for the  FEMA;   CDS;  100-acre floodplain has not been established for the proposed project area.  A floodplain study must be submitted and approved to establish the 100-year floodplain elevation.  Studies for the FEMA floodplain must be approved/confirmed/verified by FEMA and appropriate documentation must be submitted to the County.

- The project site contains or is adjacent to a 100-year floodplain shown in the Henrico County Preliminary Floodplain Study.  We recommend this draft delineation be honored in the design and layout of this project.  Specifically, proposed lots should contain adequate buildable area outside the draft floodplain, proposed structures should be outside the draft floodplain, and minimum finished floor elevations should be one foot higher than the adjacent draft floodplain elevation.

This draft study will be / has been submitted to FEMA for review and will eventually be adopted by the County.  Failure to consider this floodplain in the design and layout of the project may result in lots that will require flood insurance, lots that may be rendered unbuildable, or structures that may be within the floodplain once the study is adopted.

- All applicable floodplain designations must be shown on the plans.  The most restrictive limitations/elevations of combination of the floodplains will govern.

- Provide the elevations of all applicable 100-year floodplains within the project limits.

- Delineate and provide the 100-year backwater elevation at all roadway culvert crossings on the plans.

- The 100-year storm may not overtop the centerline of the road by more than six inches.

- All revisions to the FEMA floodplain must be submitted to the Federal Emergency Management Agency.  Confirmation of FEMA approval must be submitted to the Department of Public Works prior to plan approval.

- Provide the following for all proposed fill to be placed within the 100-year floodplain:

Adequate compensating cut

Cross-sections every 25 feet throughout the limits of cut and fill

Cut and fill volumes

Limits of cut and fill

Evidence that FEMA has approved or conditionally approved any placement of fill within the FEMA floodplain limits

Evidence that the proposed fill will not cause the 100-year floodplain elevation to increase

- Label the limits of the 100-year floodplain as “variable width drainage and utility easement”.

ADDITIONAL COMMENTS:

SURVEY:

- Provide four (4) reference coordinate points tied to the Geodetic Control Network (GCN) with coordinates in the Virginia State Plane Coordinate System (distributed near the corners of the site).  All features must be tied to the four reference points (if floating on the site, they must be tied to a property corner or property line in two different locations).  All County GIS monuments within the site must be identified on the plans.

- A minimum of two benchmarks must be established and shown on the construction plans in areas that will not be disturbed during construction.  For linear projects such as road widening, benchmarks must be placed no farther apart than 500 feet and tied into the survey base line.

- Right-of-way and baseline must be established in the field by the consultant and clearly shown on the plans.  They must be clearly tied to monuments/benchmarks.

- Provide stations at the centerline of all drainage structures located within the right-of-way limits.

- All utility poles, fire hydrants, and other above ground obstacles located within the public right-of-way and in conflict with the proposed sidewalk shelf, curb and gutter and/or the pavement widening shall be relocated at the developer’s expense prior to Henrico County staking the curb and gutter.

ADDITIONAL COMMENTS:

EASEMENTS / AGREEMENTS:

- Show the location, width, and recordation information for all existing drainage easements.

- All proposed drainage easements must be a minimum of 16 feet wide.

- The Deed Book and Page Number must be provided for all proposed off-site drainage easements prior to plan approval.

- For commercial/multi-family projects, only runoff that is considered “public” can be contained in a County maintained drainage easement.  Stormwater from off-site drainage areas that do not contain “public” water must be contained in private drainage easements.

- Provide a drainage easement through all lakes, ponds, and/or BMP basins that will contain public water.  The easement must be at least 16 feet wide and must take the most direct route from the inlet(s) to the outlet(s).

- Provide a BMP/SWM Maintenance Agreement.  This agreement can be found on the Department of Public Works web page at:  http://www.co.henrico.va.us/works/newdpwweb/Forms2/AdobeForms/BMP-SWM-form.pdf.

- A maintenance agreement must be provided between the developer and the County of Henrico prior to plan approval for irrigation, landscaping, lighting, stamped pavers, etc. within the County right-of-way.  This agreement can be found on the Department of Public Works web page at: http://www.co.henrico.va.us/works/newdpwweb/RWMaintenanceAgreement.pdf.

- Provide documentation from all private utility companies (power, gas, etc.) that authorizes land disturbance within their easements.

- Provide evidence (copies of certified letters) that property owners have been notified that work is/will be conducted in the off-site drainage easement located on their property.

ADDITIONAL COMMENTS:

MISCELLANEOUS:

- Show the size and location of all existing drainage structures, pipes, roof drains, swales, ditches, curbs, and channels and the direction of flow in each.

- Show the location of all roof drains and pipes conveying runoff from roof areas and landscape areas.

- The drainage system conveying runoff from roof areas and landscape areas in the vicinity of the building must be designed in accordance with the current edition of the International Plumbing Code.  The following statement must be added to the plans:

The roof / landscape drainage system has been designed in accordance with the current edition of the International Plumbing Code.

- Provide material type, size and elevations for all pipes and structures in the roof / landscape drainage system.

- The drainage system conveying runoff from roof areas and landscape areas in the vicinity of the building must tie into the storm sewer system at a structure (inlet, manhole, junction box, etc.).

- Provide details for all retaining walls.  Add the following note to the plans:  “Plan approval does not include approval of the retaining wall design.  Contact the Department of Building Inspections for approval requirements of the retaining wall.   Building Inspections will determine the retaining wall design approval”.  A professional seal is required if the retaining wall is in the right-of-way.

- Provide evidence that VDOT has reviewed the current scope of work shown on the plan and has no comments regarding the proposed work.

- Additional comments may follow upon review of a subsequent submittal.

ADDITIONAL COMMENTS:

- The existing condition plan needs to show outfall pipe until next off-site structure that goes towards Blue Jay Lane.  Also, that portion of Skylark Drive has been vacated.  Update existing conditions plan of land accordingly.

The Engineering Section has completed its review and has no comments at this time.

OTHER REVIEW AGENCIES:

Please see the attached comments from the Environmental Division.

Please see the attached comments from the Traffic Engineering Division

Reviewed by:	Sharon Smidler

Date Reviewed:	10-30-07

Phone Number:	501-7505	Revised 1/2/07