## COUNTY OF HENRICO

VIRGINIA

INTER-OFFICE MEMORANDUM

| TO: | Planning Office | SUBJECT: | POD2007-00122: Panera Bread Retail Shops |
| --- | --- | --- | --- |
| FROM: | Division of Police, Community Policing Unit | DATE: | July 13, 2007 |

POD2007-00122		Panera Bread Retail Shops		POD-2-07

The Division of Police recommends approval. Provide information to address or met the items in Section I.  Written compliance or new plans with details shown/stated will meet our requirements.

The Division of Police can’t recommend approval at this time

SECTION I.

ADDRESS THE FOLLOWING ITEMS IN ORDER FOR THE DIVISION OF POLICE TO ENDORSE THIS PLAN:

- Provide details showing height, type of fence and location for the fence around outdoor dining area.  Not addressed from July 2007 comments.  Will a barrier be in place here?

- Provide foot-candle levels along the building edge, to include the outdoor dining area. This same information was requested in July 2007 and is not shown.  The minimum maintained light level should be no lower than 1.0 foot-candles throughout the parking areas, walkways, building entrance and building edge.

SECTION II.  Implement the following security standards:

### Landscaping

  - All shrubs and trees should be trimmed to allow for maximum visibility to and from the site and from within the site.  Shrubs should have a natural growth height of no more than 2 ½ to 3 feet, or be maintained at this height, especially when located along an entrance, walkway or parking area.

  - Trees should have a natural growth with limbs at least 4 feet off the ground, or be maintained with the canopy raised, especially when located along a building entrance, walkway or parking area.

## Lighting

  - The lights throughout the site should be the same.  The emphasis is to have the same color of light (white or orange/yellow) throughout.  This will provide good color rendition, help with visibility and reduce contrasts.  Metal Halide is preferred.

  - All light fixtures need to be full cut-off.

  - The type of light fixture the Division of Police requires is one that puts the light down on the ground, versus horizontally and up in the air.  Many of the decorative light fixtures put the light everywhere but where you want it, which is on the ground.  If decorative fixtures are installed, they should have the bulb in the top casing of the fixture so that the light will be directed towards the ground (see photo).  This will also avoid glare because you don’t actually see the bulb.

While our requirements for the endorsement of the plan does not guarantee a crime-free environment, it is our experience that the application of the concepts of Crime Prevention Through Environmental Design (CPTED) will reduce the opportunity for crime to occur and will enhance the quality of life.  Should you have any questions or comments, contact me at (804) 501-5370 or van06@co.henrico.va.us.

Kim Vann

Planner III - CPTED

Crime Prevention Specialist

# Text boxes

The white globe visible to the eye in this post top fixture is decorative; the light bulb is in the top of the fixture.