# PLANNING COMMISSION RECOMMENDATION:

The Traffic Engineering Section:

can recommend approval of this project to the Planning Commission.

cannot recommend approval of this project to the Planning Commission because right-of-way

dedication to 8 feet from face of curb is required along Staples Mill Road.

# ROAD IMPROVEMENT COMMENTS:

- Road improvements and/or right-of-way dedication is required.

Right-of-way dedication to 8 feet from face of curb is required along Staples Mill Road.

Road widening to a Class V road section is required along …………. with 2:1 tapers back to existing at the property lines to the north and south.

Road widening to ... feet from centerline and a --- feet wide shoulder is required along .....................

Minimum improvements may be required, including road widening to 12 feet from centerline,

4’ stabilized shoulders, and associated ditch work for adequate drainage along …………...

- Show dimensions, curb return radius, and right-of-way widths of all new roads and intersections on the plans.

- The minimum allowable centerline radius for curves is 300 feet.

# STANDARD PLAN COMMENTS:

- Henrico County standard curb and gutter is required around all interior driveways and around all parking areas.

- Raised, landscaped islands with a minimum width of 9 feet are required at the ends of all rows of parking to separate parking areas from driveways.

- Label driveway widths, curb radii, and typical parking space dimensions on the plans.

- There may be no more than 50 single-family lots on a single point of access.

- There may be no more than 82 multi-family units on a single point of access.

- Guardrail or other accepted vehicular protection is required along drive aisles, parking or internal roads adjacent to the BMP. The approximate locations of the guardrail or other accepted vehicular protection need to be shown on the plans.

- Show guardrail with proper end treatments where needed.

- All guardrail must be located within right-of-way or an easement.

- Per Public Works policy, standard VDOT 5 feet wide sidewalk with a 2 feet wide utility strip is required along Staples Mill Road for the entire frontage of the property.

- All sidewalks must be located within right-of-way.

- Pedestrian passing areas are needed in sidewalk.

- The maximum length of road segment is 1250 feet.

- Show standard Henrico County end of road barricades.

- A standard R1-1 Stop Sign and 24 inch white stop bar are required at all points of egress from this development.

- Recommend standard R1-1 Stop Sign and 24 inch white stop at all internal intersections within the proposed development.

- No on-street parking will be permitted for this development on the adjacent public roads now or in the future.

- Provide sight distances and sight lines on the plan for all access points onto public right-of-way.  Adequate sight distance must be demonstrated prior to Public Works’ approval of this plan.

- A minimum of 30 feet to the first point of conflict is required at the proposed entrances from a public street.

- All two-way drive aisles need to be a minimum of 24 feet wide and a maximum of 30 feet wide.

- All one-way drive aisles need to be a minimum of 18 feet wide.  Henrico County Division of Fire may require 20 feet.

- Improvements along Staples Mill Road (State Route 33) must be approved by the Department of Transportation.

- A note needs to be included on the plans indicating: “ A traffic signal exists at the intersection of 			 and 		           	. The contractor shall contact the Traffic Engineer at (804) 727-8282 to field locate traffic control equipment and cables at least 48 hours prior to beginning work on or adjacent to the right-of-way within 250 feet of the intersection. The contractor or developer will be responsible for the cost of repair or replacement of any damaged traffic control equipment.”

- The developer is responsible for all costs associated with modifying any existing traffic signal adjacent to the site.

- Provide evidence that VDOT has reviewed the current scope of work shown on the plan and has no comments regarding the proposed work.

The Traffic Engineering Section has completed its review and has no comments at this time.

ADDITIONAL PLAN COMMENT:

- Proposed entrances onto Staples Mill Road need to be a minimum of 150 feet apart unless otherwise approved by VDOT.

- A right turn lane into the site entrances may be required by VDOT.

- Smooth out the southern curb-line at the proposed southern entrance from Staples Mill Road.

- Raised islands with a radius a minimum of 4.5 feet for adequate back-out room and dedicated turnaround spaces need to be provided in the northern ends of the three proposed drive aisles that run north/south.

- Raised islands with a radius a minimum of 4.5 feet for adequate back-out room need to be provided in the southern ends of the three proposed drive aisles that run north/south.

- Proposed sidewalks that run along the ends of parking spaces need to be a minimum of 5 feet in width.  They are not labeled on the plans.

- Bumper blocks are required in all the proposed handicap parking spaces and any regular parking spaces adjacent to the ramps or flush curb.

Michael A. Jennings

Traffic Engineer

Phone (804) 501-4238

Fax:  (804) 501-7470

jen06@co.henrico.va.us