The Engineering Division has completed its review of the above referenced project and has the following comments:

NO COMMENTS

(note that the following comments to submitted plan were address by pdfs submitted 5/11/10)

1.	Sheet C4.2 – Demolition Legend – Add to note 1 – (Covert to Manhole).

2.	Sheet C4.2 – Fix Number 2 and corresponding arrow on plan – This stormdrain is not being removed.

3.	Sheet C5.0 – Add a note to bottom of plan that baseline shown follows the existing EP .

4.	Sheet C5.0 – You have still not provided information to tie down ends of your baseline.  What are your control points?  What is the distance (and bearing if necessary) from your control point to the ends of your baseline (station 10+00 and 15+30 – or other stations at the beginning and end of baseline).  County survey crew will need this information to lay down your baseline in the field when they stake improvements in ROW.

5.	Sheet C6.0 – note at bottom of sheet regarding GNC points – Make this note larger and bold.  Add to cover sheet as well

6.	Sheet C6.0 – call out on the plan view spot shots for the top back curb at 100 foot stations (10+00, 11+00, 12+00, 13+00, and 14+00).  These elevations should correspond to the TC elevations shown for corresponding profiles on sheet C9.0.

7.	Sheet C6.0 – Structure Schedule – remove stationing in schedule, since it doesn’t correspond to baseline stationing called out on plan.

8.	Sheet C9.0 – Add a note to upper right hand corner above cross section 11+25 – “Public Works Director granted exception for 4’ Pedestrian Shelf by phone conversation with Draper-Aden on April 8, 2010.”

9.	Sheet C9.0 – Cross Sections 10+00 – 11+50 – show and label the E/P of the west bound River Road left lane  (these are cross sections where there is a concrete or concrete and grass median)

10.	Sheet C9.0 – Cross Sections 11+75 – 14+00 – Show and label the C/L of River Road

Reviewed by:	John Woodburn

Date Reviewed:      	 12 May 2010

Phone Number:	501-5851		Revised 8/11/08