The Engineering Division has completed its review of the above referenced project and has the following comments:

Contributions to the Environmental Fund ($1440.00) must be made prior to:

Final plan approval

Recordation of final plat

ADDITIONAL COMMENTS

1.	I am concerned about standing water in the western portion of the parking area.  Add a 211 contour around the existing grated top inlet, and show some spot elevations in the parking area between the 212 contour and the grated inlet.  (In particular there is an existing low in the area indicated by a closed 211 contour that I want to make sure is eliminated.)

2.	I am concerned about standing water in the parking area directly to the east of the new 4 bay addition.  Call out the EP elevation at the south east corner of the parking area.  Show spot elevations across parking area to show the south east corner will drain to the EP 212.97 at the corner of the concrete pad in front of the bays.  Also show spot elevation callouts along the edge of the concrete pad between the EP 213.57 and the EP 212.97.

Reviewed by:	John Woodburn

Date Reviewed:	10 May 2012

Phone Number:	501-5851		Revised 8/11/08