The Traffic Engineering Division has reviewed the final construction plans for POD – 12 – 12 – Sears Auto Center Store #2928 and has the following additional/outstanding comments that need to be addressed prior to the signature process:

- “Do Not Enter” signs are needed along the proposed one-way drive aisles.

- Eliminate the proposed striped island and adjust the proposed island to the south to accommodate adequate striping for the parking spaces.

- All two-way drive aisles need to be a minimum of 24 feet wide and a maximum of 30 feet wide.

- Recommend bollards at the corners of the proposed addition to protect the building from vehicular traffic.

- Access management standards require entrances to be a minimum of 150 feet from intersections. A waiver has not been submitted for this request.

- Raised, landscaped islands with a minimum width of 9 feet are required at the ends of all rows of parking to separate parking areas from driveways.

Let me know if you have any questions.

Tommy Catlett

Assistant Traffic Engineer

Phone (804) 501-4661

Fax:  (804) 501-7470

cat@co.henrico.va.us