# PLANNING COMMISSION RECOMMENDATION:

The Traffic Engineering Section:

can recommend approval of this project to the Planning Commission.

cannot recommend approval of this project to the Planning Commission because right-of-way dedication to 50 feet from centerline is required for the property frontage along New Market Road, Route 5 and a minimum of 25 feet from centerline is required along Gregg Road.  Label the centerlines and provide appropriate dimensions.

# ROAD IMPROVEMENT COMMENTS:

- Road improvements and/or right-of-way dedication is required.

Right-of-way dedication to 50 feet from centerline is required for property frontage along New Market Road, Route 5 and a minimum of 25 feet from centerline is required along Gregg Road.  Label the centerlines and provide appropriate dimensions.

Road widening with C&G to 33.5 feet from centerline is required along New Market Road, Route 5.  Road widening with C&G to 18 feet from centerline to face of curb is required along Gregg Road.  Label the centerline

Road widening to ... feet from centerline and a --- feet wide shoulder is required along .....................

Minimum improvements required, including 4’ stabilized shoulders and associated ditch

work for adequate drainage along ............................

- Show dimensions, curb return radius, and right-of-way widths of all new roads and intersections on the plans.

- The minimum allowable centerline radius for curves is 300 feet.

# STANDARD PLAN COMMENTS:

- Henrico County standard curb and gutter is required around all interior driveways and around all parking areas.

- Henrico County standard independent curb is required.

- Raised, landscaped islands with a minimum width of 9 feet are required at the ends of all rows of parking to separate parking areas from driveways.

- Label driveway widths, curb radii, and typical parking space dimensions on the plans.

- Curb radii adjacent to parking spaces need to be a minimum of 4.5 feet.

- There may be no more than 50 single-family lots on a single point of access.

- There may be no more than 82 multi-family units on a single point of access.

- Guardrail or other accepted vehicular protection is required along drive aisles, parking lots or internal roads adjacent to the BMP, or where a 7.5 feet wide graded 6:1 or flatter shelf from face of curb is not provided. The approximate locations of the guardrail or other accepted vehicular protection need to be shown on the plans.

- Show guardrail with proper end treatments where needed.

- All guardrail must be located within right-of-way or an easement.

- Per Public Works policy, a standard Henrico County sidewalk with a 2 feet wide utility strip is required along ……………. for the entire frontage of the property.

- All sidewalks must be located within right-of-way.

- Pedestrian passing areas are needed in sidewalk.

- The maximum length of road segment is 1250 feet.

- Show standard Henrico County end of road barricades.

- A standard R1-1 Stop Sign and 24 inch white stop bar are required at all points of egress from this development.

- Recommend standard R1-1 Stop Sign and 24 inch white stop at all internal intersections within the proposed development.

- No on-street parking will be permitted for this development on the adjacent public roads now or in the future.

- Provide sight distances and sight lines on the plan for all access points onto public right-of-way.  Show sight distance 12 feet from edge of travel lane.  Adequate sight distance must be demonstrated prior to Public Works’ approval of this plan.

- Sight Distance easements will be required for the proposed access points where the sight distance line is outside the proposed right-of-way. All easements need to be shown and identified on the plans.

- Sight Distance easements shall remain free of all structures, trees, shrubbery, and signs that are higher than 30” above the ground where the sight distance originates, except utility poles, fire hydrants, and traffic control signs.

- A minimum of 30 feet to the first point of conflict is required at the proposed entrances from a public street.

- All two-way drive aisles need to be a minimum of 24 feet wide and a maximum of 30 feet wide.

- All one-way drive aisles need to be a minimum of 18 feet wide.  Henrico County Division of Fire may require 20 feet.

- Improvements along New Market Road (State Route 5) must be approved by the Department of Transportation.

- A note needs to be included on the plans indicating: “A traffic signal exists at the intersection of 			 and 		           	. The contractor shall contact the Traffic Engineering Signal Shop at (804) 727-8303 with any questions pertaining to the signal. A Miss Utility ticket shall be called in to field locate traffic control equipment and cables at least 72 hours prior to beginning work on or adjacent to the right-of-way within 500 feet of the intersection. The contractor or developer will be responsible for the cost of repair or replacement of any damaged traffic control equipment.”

- A note needs to be included on the plans indicating: “If there are any Henrico County maintained signs within the construction limits that the contractor feels are in the way, please contact Traffic Engineering at (804) 727-8296 for removal and re-installation.”

- The developer is responsible for all costs associated with modifying any existing traffic signal adjacent to the site.

- A note needs to be included on the plans indicating: “The contractor is responsible for installing all stop signs, directional signs, and striping shown on the plans.”

- Provide evidence that VDOT has reviewed the current scope of work shown on the plan and has no comments regarding the proposed work.

ADDITIONAL PLAN COMMENTS:

- Provide wheel stops at handicap parking spaces.

- Clarify that independent curb will be provided between parking spaces and sidewalk adjacent to proposed building.

- Show truck movements.

- Prefer the turnaround space at the northwest corner of parking lot to be located at the northeast corner of the parking lot to allow for easier maneuvering.

- Consider reducing drive aisles from 38 feet to 24 feet to have more green space or is it needed for truck unloading?

- Consider a 4 foot sidewalk and 2 foot utility strip along Gregg Road.

- Provide a 35 foot radii at Gregg Road and New Market Road.

- Light poles need to be located 3 feett from face of curb to center of light pole.

- Provide a 4 inch white edge line on Route 5 from the gutter pan near the southeast corner of the bike trail on Route 5, to the proposed/existing edge of pavement line 100 feet west of Gregg Road.  Continue the white edge line to tie into the existing white edge line west of the paved taper.

- Provide 4 object markers behind the edge of pavement along the proposed pavement taper.

- Confirm that VDOT has no comments regarding the proposed Capital Trail along the property frontage on New Market Road, Route 5.  Please coordinate with David Steele with VDOT regarding the Capital Trail.  His e-mail address is david.steele@vdot.virginia.gov

- A sight distance of 282 feet is required along Gregg Road.

- Provide the sight distance information on southbound Gregg Road at New Market Road.

- The stop bar on Gregg Road needs to be located 4 feet behind the bike trail.

- Clarify that the sidewalk leading from the bike trail to the parking lot will meet ADA requirements.

- Provide a maintenance of traffic plan for work in the public right-of-way.

- Additional comments may follow upon review of a subsequent submittal.

Sharon Smidler, P.E.

Assistant Traffic Engineer

Phone (804) 501-4661

Fax (804) 501-7470

smi20@co.henrico.va.us