LAND-DISTURBANCE TYPE DETERMINATION AND APPLICABLE REQUIREMENTS

Using the Land-Disturbance Type Determination Worksheet (attached) found in Chapter 3 of the Henrico County Environmental Compliance Manual (Manual), this project has been determined to be (one of the following):

only a Virginia Erosion and Sediment Control Program (VESCP) land-disturbing activity

only a Virginia Stormwater Management Program (VSMP) land-disturbing activity

only a Chesapeake Bay Preservation Act (CBPA) land-disturbing activity

both a VESCP land-disturbing activity and a VSMP land-disturbing activity

both a VESCP land-disturbing activity and a CBPA land-disturbing activity

none of the above – NO COMMENTS - an Environmental Compliance Plan (ECP) is not required

Based on Table 5.1 in Chapter 5 of the Environmental Compliance Manual and the land-disturbance determination made above, an ECP must be developed that contains the following components:

General information in accordance with Section 5.3 of the Manual

CBPA requirements in accordance with Chapter 6 of the Manual

an Environmental Site Assessment in accordance with Chapter 7 of the Manual

an Erosion and Sediment Control (ESC) plan in accordance with Chapter 8 of the Manual

a Stormwater Management (SWM) plan in accordance with Chapter 9 of the Manual

a Pollution Prevention Plan in accordance with Chapter 10 of the Manual

TMDL information in accordance with Chapter 11 of the Manual

a Stormwater Pollution Prevention Plan (SWPPP) in accordance with Chapter 13 of the Manual

Municipal Separate Storm Sewer System (MS4) Program requirements in accordance with Chapter 15 of the Manual

This project has been determined to be a VSMP land-disturbing activity.  Therefore, a General Construction Permit (GCP) must be obtained prior to commencement of land-disturbance in accordance with Chapter 12 of the Manual.

ADDITIONAL COMMENTS:

CHESAPEAKE BAY PRESERVATION AREAS AND STREAM PROTECTION AREAS (Chapter 6)

- The following land features are present on the site and must be accurately shown on the plans:

Resource Protection Area (RPA)

Resource Management Area (RMA)

Stream Protection Area (SPA) (non-RPA and 100 acres or more of drainage)

- A RPA appears to exist on the site associated with a perennial stream that has not been previously identified as such.  In accordance with County Code, RPA rules apply to the stream.  Under this circumstance, appropriate evidence will need to be provided to claim that the stream is not perennial and that RPA rules do not apply.

- The RPA buffer must be forested/reforested.

- The SPA must be forested/reforested.

- The plan must include reforestation details consistent with Minimum Standard 14.10 of the Environmental Compliance Manual.

- The Resource Protection Area (RPA) limits are shown incorrectly.

- The Resource Management Area (RMA) limits are shown incorrectly.  (If the entire site is considered RMA, question #10 on the ESA must be answered as “yes”.)

- The Stream Protection Area (SPA) limits are shown incorrectly.

- Orange safety fence or non-tearable yellow and black barricade tape is required at the limits of the RPA/SPA buffer.  It must also be installed around the limits of disturbance for all encroachments/impacts within these areas.  Show the location of fence/barricade tape on the plans.  The fence/tape must be installed prior to the pre-construction meeting (clearly note this in the ESC narrative).

- There must be a separation equal to or greater than the minimum rear yard setback between the RPA/SPA limits and the rear of the buildable area.

- There must be a separation between the side yard buildable area and the RPA/SPA limits of at least 25 feet, even if the buffer is not located on the lot (common areas, etc.).

- Lots that contain a RPA and/or SPA must be identified with appropriate asterisks ( * ) and notes as stated on page 6-4 of the Henrico County Environmental Compliance Manual.

- A maintenance agreement for the SPA must be provided.  A copy of the required maintenance agreement is available from the Department of Public Works.  Information and forms for the SPA maintenance agreement can be found at:  http://henrico.us/works/forms/  (near the bottom of the page under SPA (Stream Protection Area) Agreement.

- Environmental Protection Area signs are required on all lots containing RPA/SPA.  Sign locations must be accurately shown on the plans in accordance with the Sign Spacing, Location, and Installation Guidelines found in section 6.3.3 of the Environmental Compliance Manual.

- The sequence of construction must clarify that the Environmental Protection Area signs must be installed prior to the pre-construction meeting and must be maintained throughout construction.

ADDITIONAL COMMENTS:

  - Regarding comment #4, Sheet C4.02 (Grading) shows a level spreader with grading in the RPA.  A note should be added to the plans that the graded areas next to the spreader are to be reforested in accordance with the requirements of Section 6.7 of the Henrico County Environmental Manual.

ENVIRONMENTAL SITE ASSESSMENT (Chapter 7)

- The completed Environmental Site Assessment (ESA) must be included with the plans.  (A complete plan review cannot be accomplished until this information has been provided.  Once this information has been received, additional comments may follow.)

- ESA number(s)           was (were) answered incorrectly.

- All components list as being present on the site must be accurately shown on the plans.

- ESA number(s)           have not been accurately shown on the plans.

- The current version of the two standard Erosion and Sediment Control sheets entitled “Standard Notes” and Standard Details/Calcs.”, revised 5/27/14, must be included the plans.

- The owner must sign the Acknowledgments on the Minimum Design Standards for ESC sheet.

ADDITIONAL COMMENTS:

  - You need to update the ESC notes sheet  (At the end of the seeding notes section, it includes a new note on nutrients management not on the older version you are using.)

EROSION AND SEDIMENT CONTROL (ESC) PLAN REQUIREMENTS (Chapter 8)

- Submit an ESC plan in accordance with Chapter 10 of the County Code.  A complete plan review cannot be provided until this information has been submitted.  Once this information has been submitted, additional comments may follow.

- The preliminary limits of disturbance necessary for installation of the initial ESC measures must be clearly indicated on the plans.  This area of disturbance must be the minimum necessary to allow installation of the initial ESC measures and should include all areas necessary for installing the initial ESC measures, including stockpiles, borrow areas, staging areas, etc.

- The ultimate limits of disturbance must be clearly indicated on the plans.

- Silt fence is required and must be shown on the plans.

- Silt fence is needed in additional areas, as noted in the Additional Comments section below.

- Temporary sediment trap(s) is (are) required and must be shown on the plans.

- Temporary sediment basin(s) is (are) required and must be shown on the plans.

- The sediment basin/trap design details information table on the ESA sheet must be completed.

- All sediment basins/traps must be designed so that the wet storage volume elevation does not back water into the permanent storm sewer.

- Baffles are required for all sediment basins/traps that do not meet the required 2:1 flow length to width ratio.

- Stockpiles and appropriate ESC measures must be shown on the plans or the narrative must state that no stockpiles will be located on the site.

- ESC blanket/matting (B/M) is required for all proposed slopes that are steeper than 3:1.

- All concentrated flow down fill slopes must be contained within an adequate temporary or permanent channel, flume, or slope drain structure.

- An ESC narrative/sequence of construction must be included on the plans and must appropriately sequence the installation and maintenance of ESC measures throughout construction.

- The ESC sequence of construction must state that a pre-construction meeting with the Environmental Inspector must occur prior to any land disturbance on the site.

- The ESC sequence of construction must state that if construction does not commence for 180 days following the pre-construction meeting or if the project is dormant for 180 days during the construction phase, a new pre-construction meeting is required before construction can re-start.

- The ESC sequence of construction must clearly indicate that land disturbance outside the preliminary limits of disturbance may not occur until the initial ESC measures installation has been approved by the Environmental Inspector.

- The ESC sequence of construction must clearly indicate that all diversions, sediment basins/traps, and stockpiles must be seeded and mulched immediately upon construction.

- The ESC sequence of construction must include a statement that no erosion and sediment control measures can be removed without approval of the Environmental Inspector for the project.

- The ESC plan/sequence of construction must clearly show how runoff will be diverted into sediment basin(s) or trap(s) during all phases of construction (storm sewer, diversions, channels, etc.).

- Lots adjacent to or containing a sediment basin or trap that will not be converted to a BMP must be identified on the cover sheet, the plan sheet, and with notes stating that building permits will not be issued for these lots until the basins or traps have been removed.

- ESC measures must be shown for all lots adjacent to or containing WOUS/wetlands, SPA, and/or RPA.  Add a note to the ESC plan sheet stating that these measures will be installed prior to dwelling construction.

- All land disturbance associated with utility construction, including appropriate ESC measures, must be clearly indicated on the plans.

- Provide a construction entrance at all access points to the site.

- A vehicle wash rack(s) is required at all locations where construction vehicles will leave the site.

- A water supply is required for the wash rack.  Clearly show how the water will be provided.

- The wash area for the wash rack must drain to a sediment basin/trap.

- Provide inlet protection for all inlets.

- Clearly label all areas of Temporary Seeding (TS) and Permanent Seeding (PS) on the plans.

- A variance request must be submitted in writing because Minimum Standard (MS)       is not being met      .

ADDITIONAL COMMENTS:

- Show all outlet structures for sediment traps and basins and clearly indicate to where they drain.  Sediment trap outlet berms should be shown at scale.

- Phase 2 plans - label the limits of disturbance for  the northern sector and the southern sector.  Add a note that land disturbance outside the preliminary limits in each sector cannot occur without approval of ESC inspector.

- Add notes on ESC sheets referencing grading and drainage sheets for detailed grading of sediment basins.

- Provide a profile view of each basin and trap listed in your basin and trap design table.  Indicate all relevant elevations indicated in Sediment Trap/Basin design table  (bottom elevation, wet storage elevation, dry storage elevation, riser crest elevation, 25-year storm elevation, emergency spillway elevation, top of berm elevation, side slopes of basin, riser diameter, barrel pipe diameter with inverts.  For a project of this complexity, these details are essential.

- I am concerned about how sediment trap 1 will be converted to sediment basin-7.  While sediment trap 1 is fine for the initial clearing of its drainage area. it will quickly become inadequate as the grade of the entire drainage area to it (with increasing drainage area) is being raised.  Perhaps it should initially be located further south outside of the proposed grading, with sediment basin 7 being constructed as the area is brought up to proposed grade.  It would probably be good to go ahead and show sediment basin on the Phase 3 ESC plan so it can be related to sediment basin 8, which will ultimately replace basin 7

- I had asked in previous comments for ESC sheets at the scale of the grading and drainage sheets.  Since you have not provided that, the grading and drainage sheets are providing the detailed plan view grading information for the construction of the basins and traps.  As such, sediment basins 4 and 7 are not shown in detailed plan views, since they are not included in the final plans.  Therefore, provide enlarged plan views of these basins, with contours labeled and appropriate items located (riser, drainage pipes, emergency spillways shown,etc.

- Sheets C4.01-4.04 - label the sideslopes of the basins and traps (looks like most are 2:1).  Note that slopes greater than 3:1 require blanket and matting, so include B/M note on plans and in narrative as part of sideslope stabilization.  Make sure all basins and traps shown have a clear label corresponding to their call out in the tables on sheet C2.11

- Sheet C4.01 - Sediment Trap #4- show the location of the outfall at scale.  The elevations shown should match those in the table on C2.11  (for instance, your drawing shows a bottom elevation of 197, but the table shows 201.  Are you planning to raise the bottom by 4 feet?  This would basically necessitate the reconstruction of the trap.

- Sheet C4.01 - SB-6 - grading indicates bottom elevation of 189, but the table indicates 186.  Please check  (in general- check for consistency between elevations depicted in plans and those shown in table.)

- Sheet C4.03-  SB-5 - riser crest elevation indicated is 214.70, but  table indicates 213.75.

- Sheet C4.03 - label sediment trap 5 and show outlet location.

- Sheet C4.04 - show location and grading for emergency spillway for SB-0.

- Phase 2 ESC sheets - Clearly label the limits of disturbance of the Northern Sector of Land Disturbance and the Southern Sector of Land Disturbance.

- Clarify in your ESC sequence that the land disturbance of the overall site is being divided into a northern sector and a southern sector.  Discuss which sector is to go first, and whether land disturbance in one area will follow the other area.  (in other words - how they coordinate).  You discussion should make clear why you are splitting the overall land disturbance into a northern sector and a southern sector.

- You need to include a callout for a cattle guard washrack at the interior end of your construction entrance, and show that it drains to a sediment basin on trap.   This needs to be shown on the Phase 1 ESC plan for the northern sector as well as the southern sector.

- Given the amount of earthwork to be performed on the site, include a second stone area (like a construction entrance) at the entrance to the northern sector where trucks can be cleaned of loose dirt prior to their driving down hill to Broad Street construction entrance.  A second wash rack can be included as well if it drains to a basin or trap, or the vehicles can be washed off at Broad Street entrance.

POLLUTION PREVENTION PLAN (PPP) REQUIREMENTS (Chapter 10)

- The standard Pollution Prevention Plan sheet must be included with the plan set.

- All appropriate information on the standard PPP sheet must be completed.

- Any other plans referenced in the plans must be identified on the PPP sheet.

- The locations of control measures to address the following items (as identified on the standard PPP sheet) must be clearly indicated on the plans (Not applicable is an acceptable response):

Leaks, spills, and other releases

Equipment/vehicle washing

Vehicle fueling and maintenance

Discharge from storage, handling, and disposal of construction products, materials, and waste

Discharges from other potential pollutant sources

Discharges from concrete related wash activities

Discharges of soaps, detergents, solvents, and wash water from construction activities such as cleanup of stucco, paint, form release oils, and curing compounds

Discharges of hazardous, toxic, and sanitary waste (portable toilets)

ADDITIONAL COMMENTS:

  - Regarding comment #55, you can't just describe the location and indicate a sheet.  You need to show the items symbolically on the sheet, with adequate room for the practices.  Note that some practices need to be 50 feet from inlets or basins, such as washouts and fueling.  Given that most of the initial activities will be in the rear of the site, the PPP items should probably be shown near where the main access route for construction traffic enters the northern portion of the property.  The area allotted for ppp items should be included in the preliminary limits.

MS4 PROGRAM REQUIREMENTS (Chapter 15)

- The dumpster pad must be located so that it does not drain directly into the storm sewer.  In accordance with the County’s NPDES permit, only rainwater may enter the storm sewer system.

- Trash racks are required on storm sewer inlets.  Rebar must be located to provide a two-inch maximum clear space and must be either galvanized or epoxy coated.  Trash racks must be noted in the list of drainage descriptions and details must be provided on the plans.

- An Oil/Water Separator (OWS) is required for this project.  The following comments will apply if the wastewater will be diverted to the storm sewer system:

The OWS must be designed according to the American Petroleum Institute (API) standards.

If the engineer will design the OWS, the design calculations and details must be submitted for review.

If a pre-manufactured OWS will be used, the following information must be submitted for review:

The design calculations for sizing the OWS

Q = A x I

Where:	Q = the design flow to the OWS

A = the area draining to the OWS

I = the amount of rainfall 	(1.6 in/hr under the canopy)

(2.8 in/hr outside of the canopy)

A statement from the manufacturer indicating the OWS is designed per the API standards.

A detail drawing of the OWS must be shown on the plans.

A trench drain system must be installed to divert the wastewater to the OWS.

The trench drain must fully encompass the area that produces wastewater.

The area that produces wastewater must be covered.  The canopy must be labeled and the trench drain must be located inside the drip edge of the canopy.

The area that produces wastewater must be graded so that the runoff from the surrounding area will not enter the trench drain.  Spot grades around the fueling pad must be shown on the plans.

- The plans must include a note on the plan cover sheet stating how the storage of bulk waste fat/oil/grease (FOG) will be addressed – either by using bins/barrels for storage or by using an indoor grease extraction unit.

- If barrels/bins are used for FOG storage, the plans must clearly show the location of the barrels/bins.

- The barrels/bins must be stored “under roof” to eliminate rainfall intrusion.

- A floor drain is required where the barrels/bins are located.  The floor drain must discharge to the sanitary sewer.

- Provide a detailed grading plan for the FOG storage area showing that the area “under roof” will drain to the floor drain and that the area that is not “under roof” will drain away from the storage area.

ADDITIONAL COMMENTS:

  - comments 56-63 will apply to subsequent development plans for the project.

ENVIRONMENTAL COMPLIANCE BOND (Chapter 16)

- Provide an Environmental Compliance bond and two copies of the standard Environmental Compliance Agreement.  All Bonds must be cash, letter of credit, or certificate of deposit.  Information and the forms for the Environmental Compliance Agreement can be found at: http://henrico.us/pdfs/works/revisederosionandsedimentcontrolagreement08.pdf

- Provide an itemized list, including quantities, of all ESC devices on the plans.  The list must include the total amount of land disturbance and the approximate volume of any stockpiles.

- The Environmental Compliance bond amount is set at  $525,000.00.

ADDITIONAL COMMENTS:

  - See EESD webpage for updated forms for Environmental Compliance Bond (This replaces the ESC bond).

WETLANDS/WATERS OF THE UNITED STATES (Chapter 21)

- Provide evidence that all applicable U.S. Army Corps of Engineers and state permits needed for activities in state waters and wetlands or appropriate waivers of jurisdiction have been obtained.

- Jurisdictional wetlands and/or other waters of the U.S. (WOUS) appear to exist on this site (Henrico County representatives do not have the authority to declare a site void of jurisdictional WOUS, including wetlands).

- We were unable to check the wetlands/WOUS delineation because the wetlands/WOUS were not accurately flagged in the field.  Please contact the Henrico County Water Quality Research Analyst at 727-8325 once the wetlands have been accurately flagged.  Final plans must reflect all such boundaries.

- Orange safety fence or non-tearable yellow and black barricade tape is required for all WOUS/wetlands to remain.  It must also be installed around the limits of disturbance for all encroachments/impacts within these areas.  Show the location of fence/barricade tape on the plans.  The fence/tape must be installed prior to the pre-construction meeting (clearly note this in the ESC narrative).

- This activity has been determined to require Federal (U.S. Army Corps of Engineers) and/or State (Department of Environmental Quality (DEQ)) authorization for impacts to WOUS, including wetlands.  Please submit all applicable permits and associated maps or a certification from a principal in the engineering firm (with a copy sent to the Corps) that the proposed impacts are authorized by law.  Additional comments may be generated once the permits have been submitted; therefore, we recommend that all applicable permits be submitted as soon as possible.

- All wetland areas and WOUS must be accurately shown on the plans.

- All wetlands to be impacted (including WOUS) must be clearly identified and quantified on the plans.

- We disagree with the wetland delineation as currently shown.  We feel that there are additional wetlands located      .  If you disagree with this assessment, please contact Robin Wilder at 727-8325.

- There must be a setback equal to or greater than the minimum rear yard setback between wetlands/WOUS to remain and the buildable area.  The separation between the side yard buildable area and areas of wetlands/WOUS, including wetlands/WOUS in common areas, must be at least 25 feet.

- All wetlands/WOUS in front and side yards must be indicated as wetland impacts.

- Lots that contain non-impacted wetlands/WOUS must be identified with appropriate asterisks ( ** ) and notes as stated on page 21-2 of the Henrico County Environmental Compliance Manual.

- A 25 feet wide buffer measured from the streambank is required on both sides of the channel.  The buffer must remain undisturbed, delineated on the construction plans, and clearly marked in the field.

- There must be a setback equal to the front, rear, or side yard setback between the 25 feet buffer limits and the buildable area.

- Unless temporary construction limits are shown on the plans, land disturbance within wetlands/WOUS, SPAs, and/or RPAs will be restricted to the permanent easement width.

ADDITIONAL COMMENTS:

  - ESA checklist indicates wetlands impacts.  These must be clearly labeled and quantified on the plans (acres or square feet).

The Environmental Section has completed its review and has no comments at this time.

PLANNING COMMISSION RECOMMENDATION

The Environmental Section:

can recommend approval of this project to the Planning Commission

cannot recommend approval of this project to the Planning Commission because:

.

Reviewed by:	John Woodburn

Date Reviewed:	7 November 2014

Phone Number:	501-5851

JULY 2014