The Traffic Engineering Division has reviewed the final construction plans for POD – 2014 - 00256 – West Broad Marketplace – Infrastructure and has the following additional/outstanding comments that need to be addressed prior to the signature process.

- Remove the end of road barricade at the eastern end of the Spine Road.  Provide a large arrow (2 directions), W1-7 sign behind the cul-de-sac of the Spine Road.  Object markers, OM 4-1 signs can also be used to mark the end the end of the road.

- Specify the GR-2 guardrail length and GR-9 end treatment length along the end of the cul-de-sac.  The end treatments needs to each have a minimum 50 foot length.

- Dry curb and gutter is not a Henrico County standard.  Remove the “Henrico County Standard” from the dry curb and gutter labels.

- Locate pavement arrows at least 50 feet back from the edge of pavement of the intersections into Cabelas.

- Label the Spine Road and Entrance Road dimensions from face of curb to face of curb on Sheet C3.01.

- Provide a left turn lane with a width of 10 feet and a 4 foot median on the spine road into the northeastern most access point.

- Per the Manual on Uniform Traffic Control Devices (MUTCD) Section 2B.07 there is criteria to be considered for a multi-way stop sign installation.   Clarify whether these conditions are met.

- Provide evidence that VDOT has reviewed the current scope of work shown on the plan and has no comments regarding the proposed work.

- Additional comments may follow upon review of a subsequent submittal.

Please let me know if you have any questions.

Sharon Smidler, P.E.

Assistant Traffic Engineer

Phone (804) 501-4661

smi20@henrico.us