LAND-DISTURBANCE TYPE DETERMINATION AND APPLICABLE REQUIREMENTS

Using the Land-Disturbance Type Determination Worksheet (attached) found in Chapter 3 of the Henrico County Environmental Compliance Manual (Manual), this project has been determined to be (one of the following):

only a Virginia Erosion and Sediment Control Program (VESCP) land-disturbing activity

only a Virginia Stormwater Management Program (VSMP) land-disturbing activity

only a Chesapeake Bay Preservation Act (CBPA) land-disturbing activity

both a VESCP land-disturbing activity and a VSMP land-disturbing activity

both a VESCP land-disturbing activity and a CBPA land-disturbing activity

none of the above – NO COMMENTS - an Environmental Compliance Plan (ECP) is not required

Based on Table 5.1 in Chapter 5 of the Environmental Compliance Manual and the land-disturbance determination made above, an ECP must be developed that contains the following components:

General information in accordance with Section 5.3 of the Manual

CBPA requirements in accordance with Chapter 6 of the Manual

An Environmental Site Assessment in accordance with Chapter 7 of the Manual

An Erosion and Sediment Control (ESC) plan in accordance with Chapter 8 of the Manual

A Stormwater Management (SWM) plan in accordance with Chapter 9 of the Manual

A Pollution Prevention Plan in accordance with Chapter 10 of the Manual

Total Maximum Daily Load (TMDL) information in accordance with Chapter 11 of the Manual

A Stormwater Pollution Prevention Plan (SWPPP) in accordance with Chapter 13 of the Manual

Municipal Separate Storm Sewer System (MS4) Program requirements in accordance with Chapter 15 of the Manual

This project has been determined to be a VSMP land-disturbing activity.  Therefore, a General Construction Permit (GCP) must be obtained prior to commencement of land-disturbance in accordance with Chapter 12 of the Manual.

ADDITIONAL COMMENTS:

GRANDFATHERED AND  PREVIOUSLY PERMITTED PROJECTS

This project is neither grandfathered nor previously permitted.

Application of the Technical Criteria found in Chapter 14 of the Manual (old Technical Criteria) is only allowed on grandfathered projects or projects that obtained initial GCP coverage prior to July 1, 2014 as described in Chapter 4 of the Manual.  However, the Technical Criteria found in Section 9.3 of the Manual (new Technical Criteria) may be applied at the applicant’s discretion in lieu of those in Chapter 14.

This project has claimed grandfathered status.

Before grandfathered status can be confirmed, information verifying compliance with the following conditions must be provided:

For local, state, and federal projects:

There has been an obligation of funding, either in whole, or in part, prior to July 1, 2012, or a stormwater management plan for the project was approved by the Department or the Administrator prior to July 1, 2012.

No General Construction Permit (GCP) was issued prior to July 1, 2014.

Land-disturbance did not commence prior to July 1, 2014.

For private projects:

A currently valid proffered or conditional zoning plan, a preliminary or final subdivision plat, a preliminary or final site plan, zoning plan with a plan of development, a comprehensive stormwater management master plan;  or any document determined to be equivalent to one of the above was approved by the Administrator by July 1, 2012.

The approved document provides for a layout.

The resulting activity will be compliant with the technical stormwater management requirements in Chapter 14 of the Manual.

No General Construction Permit (GCP) was issued prior to July 1, 2014.

Land-disturbance did not commence prior to July 1, 2014.

The project has claimed initial GCP coverage was obtained prior to July 1, 2014.

Provide evidence of the previously issued GCP, including project limits.

This status has been confirmed based on information provided verifying compliance with the applicable conditions described in Chapter 4 of the Manual.

Project status (grandfathered, previously permitted, etc.) must be identified on the cover sheet.

ADDITIONAL COMMENTS:

- All outlet protection must be designed in accordance with Std. & Spec. 3.18 of the Virginia Erosion and Sediment Control Handbook, Third Edition, 1992. Provide at Outfall – 99 & 200

- Show the dimensions for all outlet protection (length, width, and depth, including filter fabric lining). Provide at Outfall – 99 & 200

- Label the limits of the 100-year floodplain as “variable width drainage and utility easement” and “Special Flood Hazard Area”.

TECHNICAL CRITERIA FOR GRANDFATHERED & PREVIOUSLY PERMITTED PROJECTS (Chapter 14)

- The following worksheets (if checked) must be corrected/completed and submitted to the Department of Public Works and also included in the plans.

Worksheet 14.09 – Program Implementation		Worksheet 14.01 – Situation One,

Worksheet 14.06 – Urban Management Area Opt In		Worksheet 14.02 – Situation Two,

Worksheet 14.08 – Environmental Fund Contribution		Worksheet 14.03 – Situation Three,

Worksheet 14.04 – Situation Four, or

Worksheet 14.07 – Compliance		Worksheet 14.05 – Situation Five

BMP design worksheet

Provide Water Quality Calculations for this Phase showing that the site is under 16% and No BMP’s are required.  Keep the overall Water Quality Calculations in the plan.

- Complete the “Outfall Adequacy” table on the ESC/ESA sheet. This plan is under the “old regs”; therefore use the old Outfall Adequacy Table.  You were told in error to use the new outfall tables.

- Additional comments may follow upon review of a subsequent submittal.

ADDITIONAL COMMENTS:

  - All work in West Broad Street R/W is under VDOT purview and not part of these comments.

- Profile the outfalls down to the center of the RPA creek to show it drains, or at a minimum to the Flood Plain on the final storm sewer profiles.

- Show the level spreaders in the profile to show they fit into the area. Show they will fit now instead of later.

- How is Level Spreader at OF-450 to be accessed and constructed once the retaining wall is built if the level spreader is not to be constructed with these plans?

- 20-feet is the max depth for “BB” series inlets per VDOT Guidelines.  You might want to consult with a structural engineer for inlet design. Inlets 300, 452 & 460 exceed 20-ft.

- Consider including the 3 &4 BB Series inlet details on the plans.

- Page C10.04 – In the “Convergence Point Narrative”, it appears the narrative abruptly ends.  Is there something missing? Page C10.04 was not part of the plan set.

- What Q’s were the Outlet Protection for the erosion control measures based on?

- I was informed that no work is to take place in the VDOT R/W until the Signal Plan is approved.  How is Sediment Basin #3 to be connected?

- On Pages C4.02, C2.19 & C6.02; MH-402 is missing.

- Page C2.19 in the plan view the pipe from SB-7 goes through the proposed retaining wall.  In the profile view the pipe stops at the wall.  Which is correct?

- Page C2.14 shows the outfall from SB-0 as Outlet Protection.  Page C4.04 et al shows the outfall as a Level Spreader.  Which is correct?

- Page C6.02 shows pipes 101-99 in a VDOT Drainage Easement.  Be aware Public Works has had a problem in the past with VDOT accepting these off site drainage easements even though it is their pipe system.

- Pages C8.03 & C8.04; provide the details of the level spreaders, outlet protection [dimensions], and profiles to the centerline of the RPA Channel or 100-yr FP in the pipe profiles.

- Page C10.03; for channel section 3F-3G, what is the allowable V2 velocity?  Is 5.93 ft/sec erodible based on soil type?

- Page C11.05 & C11.06; Provide details/elevations/hatch and underdrain dimensions, slopes, etc. on the sand filter drawings.  Sand filters must be designed in accordance with Chapter 14.07 in the Henrico Environmental Compliance Manual.

- The few factory dimensions provided on the sand filter details are too small to read.  Please enlarge.

- On Page MU – Conceptual Master Utility Plan; show the proposed sand filter and piping to the outfall on the northeast corner of the Wegman’s site.

The Engineering Section has completed its review and has no comments at this time.

OTHER REVIEW AGENCIES

Please see the attached comments from the Environmental Division

Please see the attached comments from the Traffic Engineering Division

PLANNING COMMISSION RECOMMENDATION

The Engineering Section:

can recommend approval of this project to the Planning Commission

cannot recommend approval of this project to the Planning Commission because:

.

Reviewed by:	Steve Bandura

Date Reviewed:	23nov14

Phone Number:	804-501-4616

JULY 2014