The Environmental Division has completed its review of the above referenced project and has the following comments:

A pre-construction meeting is required for this project.

RECEIVED WITH EARLY LAND DISTURBANCE PLAN - Provide two copies of the standard Environmental Compliance Agreement and an Environmental Compliance Bond.  All Bonds must be cash, letter of credit, or certificate of deposit.  Information and the forms for the E and S agreement can be found at http://henrico.us/pdfs/works/ECPAgreement.pdf

RECEIVED WITH EARLY LAND DISTURBANCE PLAN - The ECB (Environmental Compliance Bond) amount is set at $525,000.00.

ADDITIONAL COMMENTS

- Level Spreaders draining sediment basins 0, 6 and 8.   I am concerned that these level spreaders, if installed while basins are in place, may fill with sediment during construction phase.  While they will be ultimately required for the outfalls, this plan should probably call for outlet protection to be installed now at these locations, with the level spreaders to be installed when the basins are removed.

- Alternately, the plan can proceed forth with installing the level spreaders, but the developer will be responsible for cleaning accumulated sediment out of the spreaders prior to the release of ESC bond.

- Does your plan allow for access to the level spreaders once the retaining wall is built for maintenance and repair of the level spreaders?

- Sheet 2.02 – show the outfall pipe for Sediment Basin 7

- Sheet 2.02 – I am concerned that Sediment Basin 7 will interfere with the grading uphill of the road and installation of storm drain necessary for ultimately installing Sediment Basin 8.  Is there enough clearance between Sediment Basin 7 and proposed grading for the road and installation of associated storm drain, or should sediment basin 7 be shifted south a little or reconfigured so as to not be so close to the road bed?

- Sheet 2.02 – Discuss in narrative when riser and outfall pipe for Sediment Basin 7 will be installed.  Are you planning to install the pipe as the retaining wall is being constructed?  You are proposing the outfall pipe to be corrugated metal pipe.  Are you planning to run CMP through the retaining wall?  What about when sediment basin 7 is closed out.  Are you planning to leave the CMP pipe in place through the wall and grout/seal it?  Or is it possible to modify the outfall for Sediment Basin 8 (the level spreader) so that you could tie the outfall for sediment Basin 7 into it.  (Make it like what you have done for Sediment Basin 6.)

- Sheet 2.04 and 4.02– How are you planning to join the temporary piping from Sediment Basin 6 to the permanent piping (RCP) leading through the retaining wall to the level spreader.

- Sheet 2.05  - Show storm drain and outfalls on the plan sheet.

- Sheet 2.05 – You should continue to show sediment basin 7 as a ghosted image.  Storm drain draining the Spine Road in the vicinity of sediment basin 7 and 8 will need to continue draining into a sediment basin 7  until the Spine Road in the area is stabilized.  Right now it appears that when basin 7 is removed, the spine road will not drain to basin 8, but will instead just drain to the outfall through the retaining wall at the end of the Spine Road.  This is not acceptable unless the Spine Road is stabilized.

- Discuss in your ESC sequence the steps in transitioning from Sediment Basin 7 to Sediment Basin 8.

Reviewed by:	John Woodburn

Date Reviewed:	15 December 2014

Phone Number:	501-5851		Revised 1/14/08