# ROAD IMPROVEMENT COMMENTS:

- Road improvements and/or right-of-way dedication is required.

Right-of-way dedication to ... feet from centerline is required for property frontage along ...

Road widening with C&G to ... feet from centerline is required along ...

Road widening to ... feet from centerline and a --- feet wide shoulder is required along .....................

Minimum improvements required, including 4’ stabilized shoulders and associated ditch

work for adequate drainage along ............................

- Show dimensions, curb return radius, and right-of-way widths of all new roads and intersections on the plans.

- The minimum allowable centerline radius for curves is 300 feet.

# STANDARD PLAN COMMENTS:

- Henrico County standard curb and gutter is required around all interior driveways and around all parking areas.

- Henrico County standard independent curb is required.

- Raised, landscaped islands with a minimum width of 9 feet are required at the ends of all rows of parking to separate parking areas from driveways.

- Label driveway widths, curb radii, and typical parking space dimensions on the plans.

- Curb radii adjacent to parking spaces need to be a minimum of 4.5 feet.

- There may be no more than 50 single-family lots on a single point of access.

- There may be no more than 82 multi-family units on a single point of access.

- Final grading details need to be shown in order to determine if guardrail or other accepted vehicular protection is necessary.

- Guardrail or other accepted vehicular protection is required along drive aisles, parking lots or internal roads adjacent to the BMP, or where a 7.5 feet wide graded 6:1 or flatter shelf from face of curb is not provided. The approximate locations of the guardrail or other accepted vehicular protection need to be shown on the plans.

- Show guardrail with proper end treatments where needed.

- All guardrail must be located within right-of-way or an easement.

- Per Public Works policy, a standard Henrico County sidewalk with a 2 feet wide utility strip is required along ……………. for the entire frontage of the property.

- All sidewalks must be located within right-of-way.

- Pedestrian passing areas are needed in sidewalk.

- Sidewalks that run along the end of parking spaces are required to be 5 feet wide.

- Wheel stops are required in any proposed handicap parking spaces and any regular parking spaces adjacent to the ramps.  Provide handicap parking signs, R7-8, in front of handicap parking spaces.

- The maximum length of road segment is 1250 feet.

- Show standard Henrico County end of road barricades.

- A standard R1-1 Stop Sign and 24 inch white stop bar are required at all points of egress from this development.

- Recommend standard R1-1 Stop Sign and 24 inch white stop at all internal intersections within the proposed development.

- No on-street parking will be permitted for this development on the adjacent public roads now or in the future.

- Provide sight distances and sight lines on the plan for all access points onto public right-of-way.  Show sight distance 12 feet from edge of travel lane.  Adequate sight distance must be demonstrated prior to Public Works’ approval of this plan.

- Sight Distance easements will be required for the proposed access points where the sight distance line is outside the proposed right-of-way. All easements need to be shown and identified on the plans.

- Sight Distance easements shall remain free of all structures, trees, shrubbery, and signs that are higher than 30” above the ground where the sight distance originates, except utility poles, fire hydrants, and traffic control signs.

- A minimum of 30 feet to the first point of conflict is required at the proposed entrances from a public street.

- All two-way drive aisles need to be a minimum of 24 feet wide and a maximum of 30 feet wide.

- All one-way drive aisles need to be a minimum of 18 feet wide.  Henrico County Division of Fire may require 20 feet.

- Dedicated turn around spaces with adequate back-out room are required in any dead end of rows of parking.  Label the striped out turn around space on the plan.

- Bollards are needed for vehicular protection for any proposed doors that swing into the proposed drive aisles around the proposed building.  Details for the bollards need to be shown on the plans.

- Provide a maintenance of traffic plan for all work proposed in the public right-of-way.

- Improvements along Brook Road (State Route 1) must be approved by the Department of Transportation.

- A note needs to be included on the plans indicating: “A traffic signal exists at the intersection of 			 and 		           	. The contractor shall contact the Traffic Engineering Signal Shop at (804) 727-8303 with any questions pertaining to the signal. A Miss Utility ticket shall be called in to field locate traffic control equipment and cables at least 72 hours prior to beginning work on or adjacent to the right-of-way within 500 feet of the intersection. The contractor or developer will be responsible for the cost of repair or replacement of any damaged traffic control equipment.”

- A note needs to be included on the plans indicating: “If there are any Henrico County maintained signs within the construction limits that the contractor feels are in the way, please contact Traffic Engineering at (804) 727-8296 for removal and re-installation.”

- The developer is responsible for all costs associated with modifying any existing traffic signal adjacent to the site.

- A note needs to be included on the plans indicating: “The contractor is responsible for installing all stop signs, directional signs, and striping shown on the plans.”

- A note needs to be included on the plans indicating: “Coordinate in the field with Henrico County Traffic Engineering at 804-727-8282 regarding the striping and arrows on 		  before installation."

- Show proposed striping and arrows on the plan for the widening of Virginia Center Parkway and Battlefield Road.

- Provide evidence that VDOT has reviewed the current scope of work shown on the plan and has no comments regarding the proposed work.

ADDITIONAL PLAN COMMENTS:

- Show truck movements for dumpsters and deliveries.

- Clarify how will protect dumpster door from hitting cars parked in the adjacent spot.  Specifically, west of Building B and adjacent to 2 parking spaces.

- Clarify whether the existing retaining wall adjacent to Virginia Center Parkway is to be removed.  The existing retaining wall appears to be in conflict with Drive B access point.  Clarify limits of existing retaining wall and top & bottom of wall elevations.

- Demonstrate adequate sight distance at southbound Battlefield Road looking right onto Francis Road.  Provide sight distance easement as necessary.

- Proposed egress striping needs to be shown and labeled on the plans.

- Label the type, color, width of striping near drive thru.

- Specify the width, length, color, spacing for the proposed striping on Virginia Center Parkway.

- Update the RG-1R label to reflect R6-1R sign in the median across from the proposed right in / right out.

- A Keep Right, R4-7 sign is needed on the proposed median end on Virginia Center Parkway.

- Provide right-of-way dedication or pedestrian access easement to get pedestrians from the sidewalk parallel to Virginia Center Parkway to the curb ramp.

- On Sheet 17, specify the type of AASHTO truck turning left from the site onto westbound Virginia Center Parkway.

- Remove the 639 sight distance line from Drive B looking right onto Virginia Center Parkway since there is a median.

- Show 280 feet sight distance line from Drive B looking left onto the modified Virginia Center Parkway right turn lane.  Provide sight distance easement as necessary.

- The end of road barricade comment is in regard to the proposed stub road off of Battlefield Rd and Drive B.

- Show R1-1 stop sign at the end of SB Bundle of Joy Lane.

- On Sheet C24, remove temp CG-2 label.

- Dimension and label the width of the proposed sidewalks.

- Install 3 object markers, OM 4-1 behind the curb south of main entrance A.

- Provide guardrail adjacent to Virginia Center Parkway near the permanent BMP.

- Label right-of-way dedication dimensions from centerline along Virginia Center Parkway, Battlefield Road and Francis Road.

- On Virginia Center Parkway and Battlefield Road, label the dimensions from the centerline to the proposed face of curb.

- Additional comments may follow upon review of a subsequent submittal.

Sharon Smidler, P.E.

Assistant Traffic Engineer

Phone (804) 501-4661

smi20@henrico.us