The Traffic Engineering Division has reviewed the final construction plans for POD 37-11 – Stuart’s Crossing – and has the following additional/outstanding comments that need to be addressed prior to the signature process.

- Provide sight distance on northbound Battlefield Road looking left onto Virginia Center Parkway.

- Sidewalk that runs along the end of parking spaces are required to be 5 feet wide.  Evalute Sheet 24 behind Building A.

- Provide a Henrico County end of road barricade off Drive B on Sheet 20.

- Update Sheet 15 to reflect Stonewall Glen Section 6 name instead of proposed subdivision.

- On Sheet 19, extend the right-of-way to the back of the sidewalk to the limits of the CG-12 near Main Entrance A.

- On Virginia Center Parkway and Battlefield Road, label the centerline to the proposed face of curb dimensions.

- Why is there a 2.5 foot utility strip.  Henrico’s typical utility strip is a 2 foot utility strip, 4 foot sidewalk and 0.5 foot maintenance strip within the right-of-way.  We need to have a 0.5 foot maintenance strip in the right-of-way behind the sidewalk.  Label the maintenance strip on the plan.

- Evaluate extending the Virginia Center Parkway median from 5+75 to 5+90.  Show WB-50 movements from outside left turn lane on Main Entrance A.

- Show striping, arrows and signs on the plan for the widening of Virginia Center Parkway and Battlefield Road.  Update the plan to reflect the mark-ups e-mailed to Byron with E.D. Lewis on 4/17/15.

- Provide a copy of the signal plan to Henrico Traffic Engineering prior to POD approval.

- Provide evidence that VDOT has reviewed the current scope of the work shown on the plan and has no comments regarding the proposed work.

Please let me know if you have any questions.

Sharon Smidler, P.E.

Assistant Traffic Engineer

Phone (804) 501-4661

smi20@henrico.us