The Department of Public Works has completed its review of the above referenced plat and has the following comments (checked items apply):

The construction plans have not been approved.  Once the construction plans are approved, the plat must address all applicable items listed below.

A revision to the approved construction plans is required that will impact the plat.  Once the revision is approved, the plat must address all applicable items listed below.

No Comments.  DPW can recommend approval of the plat.

EASEMENTS / FLOODPLAIN

- The onsite drainage easements must match those shown on the approved construction plans.

- The sight distance easements must match those shown on the approved construction plans.

- All off-site drainage easements must be recorded.

- The temporary cul-de-sac easements must match those shown on the approved construction plans.

- The limits of the floodplain must match that shown on the approved construction plans and be labeled as a Limits of Special Flood Hazard Area.

- The Special Flood Hazard Area must be labeled as a Variable Width Drainage and Utility Easement.

BONDS / FUND CONTRIBUTIONS

- A performance bond for the road and drainage improvements shown on the approved construction plans must be submitted prior to recordation of the subdivision.  The bond amount for the road and drainage improvements must be determined using the bond calculation worksheet provided by the County of Henrico Department of Public Works.

- Submit the completed bond calculation worksheet provided by the County of Henrico Department of Public Works for the road and drainage improvements.

- The road and drainage performance bond amount has been estimated to be $      and has been forwarded to Planning.

- An Environmental Fund contribution of $      must be submitted prior to recordation.

- A SWM Facility Maintenance Fund contribution of $      ($100 per SWM facility per lot) must be submitted prior to recordation.

ENVIRONMENTAL FEATURES

- Lots containing wetlands must be labeled with ** and be identified with the following note:

Lots marked with ** may contain waters and/or wetlands as determined at the time of recordation of the plat.  Disturbance outside of designated water and wetland impact areas will require approval from the U.S. Army Corps of Engineers and/or the Virginia Department of Environmental Quality.  Additional requirements may be imposed on these lots prior to the issuance of building permit.  See construction plans on file in the Planning Office for additional details.

The identified lots must match those shown on the approved construction plans.

- Wetlands/WOUS are to be shown only if required by USCOE or DEQ permit conditions.

- The RPA must be shown on the plat and match that shown on the approved construction plans.

- The SPA must be shown on the plat and match that shown on the approved construction plans.

- Lots containing RPA and/or SPA must be labeled with *** and be identified with the following note:

Lots marked with *** contain RPA and/or SPA.  These areas are to remain undisturbed and are to be protected from all construction or land disturbing activities.  See construction plans on file in the Planning Office for additional details.

OTHER

- Four (4) GIS points must be provided on each page of the plat.

- The radius of the cul-de-sacs must match those shown on the approved construction plans.

- The horizontal curves of the right-of-way must match those shown on the approved construction plans.

- Remove NBP designations and minimum finished floor elevations from the plat.

Additional Comments:

NO COMMENTS

Reviewer / Reviewer Phone: 	Alex Gruendl / 804-501-4033

Date:		8 October 2018

Revised 1/21/16