# PLANNING COMMISSION RECOMMENDATION:

The Traffic Engineering Section:

can recommend approval of this project to the Planning Commission.

cannot recommend approval of this project to the Planning Commission because further road widening of Concept Road 143 (Magellan Pkwy) is required. See comment #1 below.

# ROAD IMPROVEMENT COMMENTS:

- Road improvements and/or right-of-way dedication is required.

Right-of-way dedication to 50 feet from centerline of right-of-way is required on both sides of Concept Road 143 (Magellan Pkwy)

Road widening with Henrico County curb & gutter to 33.5 feet from centerline is required along both sides of Concept Road 143 (Magellan Pkwy). Per Proffer #15 of Rezoning Case REZ2019-00025: “..the entrance into the development over and across the Concept Road will be constructed with four lanes to public road standards to its ultimate width from Brook Road east past Telegraph Rd to the first road crossing within the property, as shown on the Concept Plan.”

Road widening to ... feet from centerline and a --- feet wide shoulder is required along .....................

Minimum improvements required, including 4’ stabilized shoulders and associated ditch

work for adequate drainage along ............................

- Show dimensions, right-of-way centerlines, curb return radii, and right-of-way widths of all roads (both sides) and intersections on the plans.

- The minimum allowable centerline radii for curves is … feet along ...

- The minimum access point spacing is … feet along …

# STANDARD PLAN COMMENTS:

- Provide the vehicle trips per weekday, AM peak hour weekday trip generation (enter/exit) and PM peak hour weekday trip generation (enter/exit) on the plan cover sheet. There is a newer POD cover sheet that needs to be used that is available at http://henrico.us/works/design/.

- Show the minimum queue length for drive thru lanes.

- Henrico County standard curb and gutter is required around all interior driveways and around all parking areas. Clarify parallel parking space dimensions relative to spaces at curb returns 22’ from pavement marking to EP curb and gutter; 24’ long from pavement marking to pavement marking. Are the spaces at the curb returns 23.5’ long (given 1.5’ gutter pan)?

- Henrico County standard independent curb is required.

- Raised, landscaped islands with a minimum width of 9 feet are required at the ends of all rows of parking to separate parking areas from driveways. Please label widths of islands (ex. Sheet C13, Keswick Dr, two spaces between buildings 1, 2, 3, and a 2nd 3 [mistake? 4?])

- Label driveway widths, curb radii, and typical parking space dimensions on the plans. Some curb radii dimensions are not labelled on plan.

- Curb radii adjacent to parking spaces need to be a minimum of 4.5 feet.

- There may be no more than 50 single-family lots on a single point of access.

- There may be no more than 82 multi-family units on a single point of access.

- Final grading details need to be shown in order to determine the need for guardrail or other accepted vehicular protection.

- Guardrail and proper end treatments are required along public roadways where the appropriate clear zone is not provided.  The approximate locations of the guardrail and end treatments need to be shown on the plan within the right-of-way or an easement.

- In private developments, guardrail or other accepted vehicular protection is required along drive aisles, parking lots or internal private roads adjacent to a BMP, or where a 7.5 feet wide clear zone having a graded 6:1 or flatter shelf from face of curb or near edge of pavement is not provided. When there is a water hazard with a depth of 2 feet or more, the minimum clear zone increases to 10 feet.  The approximate locations of the guardrail or other accepted vehicular protection need to be shown on the plans.

- Per Public Works policy, a standard Henrico County sidewalk with a 2 feet wide utility strip is required along ……………. for the entire frontage of the property.

- All sidewalks must be located within right-of-way.

- Pedestrian passing areas are needed in sidewalk.

- Sidewalks that run along the end of parking spaces are required to be 5 feet wide.

- Wheel stops are required in any proposed handicap parking spaces and any regular parking spaces adjacent to the ramps.  Provide handicap parking signs, R7-8, in front of handicap parking spaces.

- The maximum length of road segment is 1320 feet.

- Show standard Henrico County end of road barricades.

- A standard R1-1 Stop Sign and 24 inch white stop bar are required at all points of egress from this development. Please include on Magellan Pkwy access.

- Recommend standard R1-1 Stop Sign and 24 inch white stop at all internal intersections within the proposed development.

- Provide and show the locations of the subdivision street name signs.  The street name signs must meet the specifications in the Department of Public Works Design Manual.

- Provide and show the locations of the public speed limit signs and Stop signs.

- Specify the proposed type of posts for subdivision street name signs, stop signs, speed limit signs, etc. in the public right-of-way.  If not using the standard green u-channel, square wood or square metal posts in the public right-of-way, provide a Henrico County Right-of-Way Maintenance Agreement prior to plan approval. Any non-standard sign post must be approved by the Traffic Engineer prior to plan approval.  Provide a catalog cut of any proposed non-standard sign post.

- Within subdivisions, bump-outs are required on public residential roadways with a speed limit of 25 mph or less. Bump-outs are curb extensions that reduce the travel lanes along a roadway. They are predominantly located at intersections to reduce pedestrian crossing distances but may be installed at a mid-block section of roadway. Bump-outs are also used as a traffic calming measure. Locations of bump-outs should be coordinated with Traffic Engineering. Traffic Engineering will provide an example of bump-outs upon request.

- No on-street parking will be permitted for this development on the adjacent public roads now or in the future.

- Provide intersection sight distance lines to scale on the plan for all access points onto the public right-of-way.  Provide a profile of the roadway along with the driver’s line of sight.  Show sight distance 14.5 feet from edge of travel lane.  Adequate sight distance must be demonstrated prior to Public Works’ approval of this plan.

- Sight Distance easements will be required for the proposed access points where the sight distance line is outside the proposed right-of-way. All easements need to be shown and identified on the plans.

- Sight Distance easements shall remain free of all structures, trees, shrubbery, and signs that are higher than 30” above the ground where the sight distance originates, except utility poles, fire hydrants, and traffic control signs.

- A minimum of 30 feet to the first point of conflict is required at the proposed entrances from a public street.

- All two-way drive aisles need to be a minimum of 24 feet wide and a maximum of 30 feet wide.

- All one-way drive aisles need to be a minimum of 18 feet wide.  Henrico County Division of Fire may require 20 feet.

- Dedicated turn around spaces with adequate back-out room are required in any dead end of rows of parking.  Label the striped out turn around space on the plan.

- Bollards are needed for vehicular protection for any proposed doors that swing into the proposed drive aisles around the proposed building.  Details for the bollards need to be shown on the plans.

- Show trash truck movements moving throughout site.

- Provide a detailed maintenance of traffic plan for all work proposed in the public right-of-way. TTC-23.2 on sheet 40 acknowledged, but insufficient for whole site. Please provide a maintenance of traffic narrative to go with construction sequencing.

- Improvements along Brook Road (State Route 1) must be approved by the Department of Transportation.

- A note needs to be included on the plans indicating: “A traffic signal exists at the intersection of 			 and 		           	. The contractor shall contact the Traffic Engineering Signal Shop at (804) 727-8303 with any questions pertaining to the signal. A Miss Utility ticket shall be called in to field locate traffic control equipment and cables at least 72 hours prior to beginning work on or adjacent to the right-of-way within 500 feet of the intersection. The contractor or developer will be responsible for the cost of repair or replacement of any damaged traffic control equipment.”

- A note needs to be included on the plans indicating: “If there are any Henrico County maintained signs within the construction limits that the contractor feels are in the way, please contact Traffic Engineering at (804) 727-8296 for removal and re-installation.”

- The developer is responsible for all costs associated with modifying any existing traffic signal adjacent to the site.

- A note needs to be included on the plans indicating: “The contractor is responsible for installing all stop signs, directional signs, and striping shown on the plans.”

- A note needs to be included on the plans indicating: “Coordinate in the field with Henrico County Traffic Engineering at 804-727-8282 regarding the striping and arrows on Telegraph Rd & Concept Road 143 (Magellan Pkwy)  before installation."

- Show proposed striping and arrows on the plan for the widening of Telegraph Rd & construction of Concept Road 143 (Magellan Pkwy). Recommend providing a separate striping plan

- Provide evidence that VDOT has reviewed the current scope of work shown on the plan and has no comments regarding the proposed work.

- All roads intersecting another road shall do so at an angle of 90 degrees for a minimum distance of 75’ from the centerline of each roadway in all directions. "Road" shall mean public road, private road, multifamily access, and commercial access. Comment made in reference to private road intersections.

- Additional comments may follow upon review of a subsequent submittal.

ADDITIONAL PLAN COMMENTS:

  - Chord right-of-way dedication at each public intersection.

  - Consult with VDOT about possibility of sidewalk along Brook Rd. Additional right-of-way may need to be attained for this.

  - Remove access to DMV nearest to intersection of Brook Rd and Magellan Pkwy.

  - Clarify how contractor will “maintain uninterrupted access during construction activities to DMV site”.

  - Provide MUTCD standard NO LEFT TURN sign be set in median across from eastern DMV access.

  - For sight distance, cut back concrete medians at intersection of Magellan Pkwy and Telegraph Rd. Shift back turn lanes & tapers accordingly.

  - Clarify function of Magellan Pkwy and Telegraph Rd intersection. As shown, through Traffic on Telegraph Rd will have to watch 7 lanes of traffic to cross. (four through lanes, two left turn lanes, and one right turn lane. Consider redesign.

  - Clarify limits of Section 1 work. Eastern half of Telegraph Rd widening (north) is cut off on sheet C12. Accesses on western half of Telegraph Rd are to be built too?

  - Provide more detail of Magellan Pkwy’s alignment to the shopping center across the street, off Brook Rd.

  - Include R4-7c signs at the ends of proposed medians.

  - Per comment #27, specify speed for Magellan Pkwy.

  - On sheet C20, the proposed 50-foot sags (STA 9+00 to 9+50 and STA 10+50 to 11+00) are inadequate for Telegraph Rd’s speed.

  - On sheet C21, the proposed 150’ sag (from STA 10+50 to 12+00) looks to be inadequate for Magellan Pkwy’s expected road speed.

  - Call out pedestrian access easements for sidewalk.

  - On sheet C15, provide a taper from the widened portion to the existing portion of Telegraph Rd SB.

  - Consider curb ramp and stop sign placement for proposed pedestrian crossings. On sheet C15, relocate meandering sidewalk (running along Telegraph Rd) and ramps on McCormick Farm Dr back toward Telegraph Rd, between stop bar and CG-9D.

  - Are any barricades proposed for the ends of private roads that are to be continued in future phases?

  - Provide slope easements off BOTH sides of Magellan Pkwy Right-of-way, approaching I-95.

  - Provide typical cross-section of Magellan Pkwy. Provide x-sections for road widening along Telegraph Rd and Magellan Pkwy, per EESD Engineer’s requirements.

Brandon House, E.I.T.

Traffic Review Engineer

County of Henrico - Department of Public Works
P.O. Box 90775 Henrico, VA 23273-0775

804.501.4661 phone | 804.501.7470 fax

hou018@henrico.us | www.henrico.us/works/traffic/