The Traffic Engineering Division has reviewed the plans for POD2020-00410 and has the following additional/outstanding comments:

# REMAINING STANDARD PLAN COMMENTS:

- Provide the vehicle trips per weekday, AM peak hour weekday trip generation (enter/exit) and PM peak hour weekday trip generation (enter/exit) on the plan cover sheet. There is a newer POD cover sheet that needs to be used that is available at http://henrico.us/works/design/. (10/16/20): Clarify and provide vehicle trip numbers as “enter/exit” rather than “enter” only.

- Sidewalks that run along the end of parking spaces are required to be 5 feet wide. The continuous width of the sidewalk should exclude the width of the curb.

- [REPEAT] Show vehicle movements on the plan; specifically, how traffic approaches the DROPOFF Area.

- A standard R1-1 Stop Sign and 24 inch white stop bar are required at all points of egress from this development.

ADDITIONAL PLAN COMMENTS:

Sheet C3.0 (Layout Plan):

- Provide VDOT standard terminals for proposed GR-2 guardrail. Call out on the plans. Add VDOT standard guardrail detail(s) among plan notes and details.

Sheet C3.4 (Maintenance of Traffic Plan):

- Update Figure-TTCs to latest revision of VWAPM (2011 VWAPM, Revision 2: September 1, 2019).

- Add following notes to Maintenance of Traffic Plan:

  - Except for emergencies, no lane closures or other traffic restrictions shall be erected during periods of inclement weather.

  - The Contractor shall coordinate all lane closures with Henrico Police/Fire (501-5000) and Pupil Transportation/ Schools (226-5570).

  - The Contractor is responsible for the maintenance of all signs and posts in the work zone.  This includes, but is not limited to, stop, yield, street name and speed limit signs.  Any sign or post damaged during construction or missing shall be replaced by the Contractor at his expense.

  - The Traffic Engineer (804-727-8282) reserves the right to modify the traffic control as necessary in the interests of public safety and/or convenience.

  - Unless otherwise approved, no equipment or materials are to be left in the county right-of-way after work hours.  Should permission be given to allow equipment and materials in the right-of-way after work hours, group II channelizing devices (plastic barrels with prismatic sheeting) shall be used to delineator the obstacles.  Equipment and materials shall be placed in areas that would have no adverse impact to the property owners and shall not obstruct any sight distances or create any other safety issues.

  - All employees exposed to vehicular traffic shall be provided with and instructed to wear warning vests marked with or made of reflectorized or high visibility materials meeting Class III standards.

Upon additional submittals, further comments may be generated.

Brandon House, E.I.T.

Traffic Review Engineer

County of Henrico - Department of Public Works
P.O. Box 90775 Henrico, VA 23273-0775

804.501.4661 phone | 804.501.7470 fax

hou018@henrico.us | www.henrico.us/works/traffic/