The Department of Public Works has completed its review of the above referenced project and has the following comments:

- Trees and/or shrubs cannot be planted in any County maintained drainage easement.  Show the storm sewers and drainage easements on the landscape plan.

- No plantings above 30 inches in height above the curb line are allowed in the public right-of-way.

- A maintenance agreement must be provided from the developer to the County for any plantings, irrigation work, lighting work, etc. located in the right-of-way.

- Henrico County is not liable or responsible for any damage or destruction of plantings, lighting, irrigation systems, etc. in the right-of-way or public easement resulting from maintenance of the drainage systems, right-of-way, and/or roadway.

- Provide underdrains along the rear of the curb and gutter any public right-of-way or in any islands/medians in the public right-of-way if an irrigation system is proposed.

- Provide sight distance information at all entrances and intersections.  See Additional Comments as well.

- Lighting poles/fixtures are not permitted over any storm sewer (public or private) or in public drainage easements.  Show the proposed lights on the grading plan with the storm sewer.  Make sure lights are not located on top of the Stormtech systems or other storm sewer.

- Trees/shrubs cannot be planted below the water quality volume elevation in the BMP.

- Trees/shrubs cannot be planted on the fill section of any dams.

- Mulch cannot be placed below the water quality volume elevation in the BMP.

- Plantings, lighting poles/fixtures, and/or fences around BMPs must be placed so that access is not blocked to any inlet/outlet structures.

- NO COMMENTS

ADDITIONAL COMMENTS:

- Per County policy, "no landscape plantings which obstruct visions between a height of 30 inches and eight feet above the ground level where the sight distance originates shall be permitted within the sight distance line nor within 5 feet of the sight distance line."  Trees within this area must be limbed up to 8'.  Shrubs should not grow taller than 30".

Reviewed by:	Sarah Briggs

Date:	02/26/21

Email……………………………………………………………………………………….bri114@henrico.us

Phone……………………………………………………………………………………………...804-501-4616