# ROAD IMPROVEMENT COMMENTS:

- Road improvements and/or right-of-way dedication is required.

Right-of-way dedication to _ feet from centerline of right-of-way is required for property frontage along _.

Road widening with Henrico County curb & gutter to ... feet from centerline is required along ...

Road widening to ... feet from centerline and a --- feet wide shoulder is required along .....................

Minimum improvements required, including 4’ stabilized shoulders and associated ditch

work for adequate drainage along ............................

- Show dimensions, right-of-way centerlines, curb return radii, and right-of-way widths of all roads (both sides) and intersections on the plans. Label centerline of Burning Tree Road. Provide dimensions from centerline to:

  - newly proposed right-of-way line…there appears to be two right-of-way lines shown. Clarify that right-of-way will be 33’ from centerline.

  - proposed face of curbing of widened Burning Tree Road.

- The minimum allowable centerline radii for curves is … feet along ...

- The minimum access point spacing is … feet along …

# STANDARD PLAN COMMENTS:

- Provide the vehicle trips per weekday, AM peak hour weekday trip generation (enter/exit) and PM peak hour weekday trip generation (enter/exit) on the plan cover sheet. There is a newer POD cover sheet that needs to be used that is available at http://henrico.us/works/design/.

- Show the minimum queue length for drive thru lanes.

- Henrico County standard curb and gutter is required around all interior driveways and around all parking areas. Label where proposed.

- Henrico County standard independent curb is required. Label where proposed.

- Raised, landscaped islands with a minimum width of 9 feet are required at the ends of all rows of parking to separate parking areas from driveways.

- Label driveway widths, curb radii, and typical parking space dimensions on the plans.

- Curb radii adjacent to parking spaces need to be a minimum of 4.5 feet.

- There may be no more than 50 single-family lots on a single point of access.

- There may be no more than 82 multi-family units on a single point of access.

- Final grading details need to be shown in order to determine the need for guardrail or other accepted vehicular protection.

- Guardrail and proper end treatments are required along public roadways where the appropriate clear zone is not provided.  The approximate locations of the guardrail and end treatments need to be shown on the plan within the right-of-way or an easement.

- In private developments, guardrail or other accepted vehicular protection is required along drive aisles, parking lots or internal private roads adjacent to a BMP, or where a 7.5 feet wide clear zone having a graded 6:1 or flatter shelf from face of curb or near edge of pavement is not provided. When there is a water hazard with a depth of 2 feet or more, the minimum clear zone increases to 10 feet.  The approximate locations of the guardrail or other accepted vehicular protection need to be shown on the plans.

- Per Public Works policy, a standard Henrico County sidewalk with a 2 feet wide utility strip is required along ……………. for the entire frontage of the property.

- All sidewalks must be located within right-of-way.

- Pedestrian passing areas are needed in sidewalk.

- Sidewalks that run along the end of parking spaces are required to be 5 feet wide.

- Wheel stops are required in any proposed handicap parking spaces and any regular parking spaces adjacent to the ramps.  Provide handicap parking signs, R7-8, in front of handicap parking spaces.

- The maximum length of road segment is 1320 feet.

- Show standard Henrico County end of road barricades.

- A standard R1-1 Stop Sign and 24 inch white stop bar are required at all points of egress from this development.

- Recommend standard R1-1 Stop Sign and 24 inch white stop at all internal intersections within the proposed development.

- Provide and show the locations of the subdivision street name signs. The street name signs must meet the specifications in the Department of Public Works Design Manual (Section 2-38). Signs for public roads shall display a green background with white lettering while signs for private roads shall display a white background with black lettering.

- Provide and show the locations of the subdivision speed limit signs and Stop signs.  What will the road speed limits be?

- Specify the proposed type of posts for subdivision street name signs, stop signs, speed limit signs, etc. in the public right-of-way.  If not using the standard green u-channel, square wood or square metal posts in the public right-of-way, provide a Henrico County Right-of-Way Maintenance Agreement prior to plan approval. Any non-standard sign post must be approved by the Traffic Engineer prior to plan approval.  Provide a catalog cut of any proposed non-standard sign post.

- Within subdivisions, bump-outs are required on public residential roadways with a speed limit of 25 mph or less. Bump-outs are curb extensions that reduce the travel lanes along a roadway. They are predominantly located at intersections to reduce pedestrian crossing distances but may be installed at a mid-block section of roadway. Bump-outs are also used as a traffic calming measure. Locations of bump-outs should be coordinated with Traffic Engineering. Traffic Engineering will provide an example of bump-outs upon request.

- No on-street parking will be permitted for this development on the adjacent public roads now or in the future.

- Provide intersection sight distance lines to scale on the plan for all access points onto the public right-of-way.  Provide a profile of the roadway along with the driver’s line of sight.  Show sight distance 14.5 feet from edge of travel lane.  Adequate sight distance must be demonstrated prior to Public Works’ approval of this plan.

- Sight Distance easements will be required for the proposed access points where the sight distance line is outside the proposed right-of-way. All easements need to be shown and identified on the plans.

- Sight Distance easements shall remain free of all structures, trees, shrubbery, and signs that are higher than 30” above the ground where the sight distance originates, except utility poles, fire hydrants, and traffic control signs.

- A minimum of 30 feet to the first point of conflict is required at the proposed entrances from a public street.

- All two-way drive aisles need to be a minimum of 24 feet wide and a maximum of 30 feet wide.

- All one-way drive aisles need to be a minimum of 18 feet wide.  Henrico County Division of Fire may require 20 feet.

- Dedicated turn around spaces with adequate back-out room are required in any dead end of rows of parking.  Label the striped out turn around space and NO PARKING sign on the plan. No parking sign should be MUTCD standard. Provide a detail of the sign.

- Bollards are needed for vehicular protection for any proposed doors that swing into the proposed drive aisles around the proposed building.  Details for the bollards need to be shown on the plans.

- Show truck movements on the plan.

- Provide a maintenance of traffic plan for all work proposed in the public right-of-way.

- Improvements along ... (State Route ...) must be approved by the Department of Transportation.

- A note needs to be included on the plans indicating: “A traffic signal exists at the intersection of 			 and 		           	. The contractor shall contact the Traffic Engineering Signal Shop at (804) 727-8303 with any questions pertaining to the signal. A Miss Utility ticket shall be called in to field locate traffic control equipment and cables at least 72 hours prior to beginning work on or adjacent to the right-of-way within 500 feet of the intersection. The contractor or developer will be responsible for the cost of repair or replacement of any damaged traffic control equipment.”

- A note needs to be included on the plans indicating: “If there are any Henrico County maintained signs within the construction limits that the contractor feels are in the way, please contact Traffic Engineering at (804) 727-8296 for removal and re-installation.”

- The developer is responsible for all costs associated with modifying any existing traffic signal adjacent to the site.

- A note needs to be included on the plans indicating: “The contractor is responsible for installing all stop signs, directional signs, and striping shown on the plans.”

- A note needs to be included on the plans indicating: “Coordinate in the field with Henrico County Traffic Engineering at 804-727-8282 regarding the striping and arrows on Burning Tree Road before installation."

- Show proposed striping and arrows on the plan for the widening of Burning Tree Road.

- Provide evidence that VDOT has reviewed the current scope of work shown on the plan and has no comments regarding the proposed work.

- All roads intersecting another road shall do so at an angle of 90 degrees for a minimum distance of 75’ from the centerline of each roadway in all directions. "Road" shall mean public road, private road, multifamily access, and commercial access.

- Additional comments may follow upon review of a subsequent submittal.

ADDITIONAL PLAN COMMENTS:

General:

- Provide County Typical Section detail for a Class VII (Burning Tree Road) roadway among construction notes and details. Typical Road Sections can be found in Appendix B of the Henrico Public Works Design Manual. Please visit: https://henrico.us/works/design/manual/.

- Provide stationing along Burning Tree Road.

- Provide VDOT standard detail for proposed CG-9D.

Sheet 1 (Cover):

- Clarify sheet index. Some of the pages noted in the index do not match up with the sheet numbers near the end of the plan.

Sheets 19-21 (Site Plan):

- Provide curb return radii dimensions for the CG-9D access off Burning Tree Road. Minimum allowable curb radius is 15’.

- I see what appears to be labels for details (A, B, C, and D). Lettered labels shown seem to match up with details in legend. Ensure the letters are identified in the legend.

- On sheet 21:

  - Recommend removal of parallel parking spaces parallel to New Settlement Drive, adjacent to raised island by New Settlement Circle.

  - Provide dimensions for the proposed turn-around space (including curb radii)

Brandon House, E.I.T.

Traffic Review Engineer

County of Henrico - Department of Public Works
P.O. Box 90775 Henrico, VA 23273-0775

804.501.4661 phone | 804.501.7470 fax

hou018@henrico.us | www.henrico.us/works/traffic/