The Traffic Engineering Division has reviewed the plans for POD2021-00011 and has the following comments:

# PLANNING COMMISSION RECOMMENDATION:

The Traffic Engineering Section:

can recommend approval of this project to the Planning Commission.

cannot recommend approval of this project to the Planning Commission because ...

General:

- Label ‘existing’ stop signs at intersections near border between section 1 & section 2 to clarify stop conditions.

Sheet C16 (Layout & Utility Plan [West]):

- For new crosswalk (crossing Magellan Pkwy) at intersection of Magellan Pkwy & Telegraph Rd:

  - Provide W11-2 and W16-7P signs to face Magellan Pkwy EB

  - Call out crosswalk marking detail on this sheet (per striping legend on sheet C45).

  - The crosswalks should not have the two longitudinal lines. Only the bars parallel with the flow of traffic should be provided.

  - Add note to the plans: “Coordinate in the field with Henrico County Traffic Engineering at 804-727-8282 (Matthew Mawyer) regarding the crosswalk striping at the intersection of Magellan Pkwy & Telegraph Road before installation.

- For the ‘stub’ access opposite of the new DMV entrance, clarify when a development will come and use the stub to establish a driveway. A cross-access easement will need to be provided to allow access to the parcel at the corner of Magellan Pkwy & Brook Road.

Sheet C20 (Grading & Drainage Plan [West]):

- Provide a detail for proposed “GR3 Timber Bollard Guardrail”.

- The guardrail segment between the 2 (north-facing) parking spaces and SWM Facility #1C (off proposed Birchwood Hill Dr) terminates awfully close to the west side of the parking space. Recommend removing a portion of the guardrail segment nearest to the edge of the space.

Sheets C22 and C23 (Grading and Drainage Plan [South & North]):

- The labelled clear zone along McCormick Farm Dr (by the wetlands) appears to scale at 10’ as opposed to the labelled 7.5’. Revise label.

- In the parking spaces that face SWM Facility #1A, provide additional grading or guardrail behind the sidewalk.

Sheet C46A (Vehicle Movements & Maintenance of Traffic):

- In “Maintenance of Traffic Notes”: Revise note “e” to say: “The Traffic Engineer (804-727-8282) reserves the right to modify the traffic control as necessary in the interests of public safety and/or convenience.” … I apologize for the error in my original comment.

- Provide a legible label for the design vehicle used to demonstrate turning movements.

- For sidewalk work out of right-of-way, add Figure TTC-1.1.

- Provide applicable Figure TTC(s) for installation of the new crosswalks at the intersection of Magellan Pkwy & Telegraph Rd.

Upon additional submittals, further comments may be generated.

Please let me know if you have any questions.

Thanks,

Brandon House, E.I.T.

Traffic Review Engineer

County of Henrico - Department of Public Works
P.O. Box 90775 Henrico, VA 23273-0775

804.501.4661 phone | 804.501.7470 fax

hou018@henrico.us | www.henrico.us/works/traffic/