# PLANNING COMMISSION RECOMMENDATION:

The Traffic Engineering Section:

can recommend approval of this project to the Planning Commission.

cannot recommend approval of this project to the Planning Commission because ...

# ROAD IMPROVEMENT COMMENTS:

- Road improvements and right-of-way dedication is required.

- Refer to Rezoning Case: REZ2020-00015, Proffer 13 for required road improvements. Right-of-way dedication will be based on extent of road improvements.

- New subdivision roads shall meet street width requirements as outlined by County typical road sections I – VI. Typical Road Sections can be found in Appendix B of the Henrico Public Works Design Manual. Please visit: https://henrico.us/works/design/manual/. ROW and pavement design shall be based on projected traffic volume.

- County Standard cul-de-sac dimensions require a 45’ pavement radius (centerline of cul-de-sac to the face of curb) and a 50’ right-of-way radius. Label dimensions.

  - The cul-de-sac at the terminus of Clayman Road will need to be improved to current standards.

- Given the number of lots that will use Turtle Parkway to access and exit their parcels:

  - The Turtle Pkwy approach to its intersection with Drybridge Rd should have one ingress lane and two egress lanes. The road will need to be an adequate width to accommodate 3 lanes of travel at this intersection approach.

  - A right turn lane should be provided for Drybridge Road’s northbound approach to it’s intersection with Turtle Parkway.

- For detached lots 18 & 19 (fronting on Old Williamsburg Road):

  - Right-of-way dedication to 25’ from centerline is required. Please confirm existing right-of-way with dimensions (refer to comment #2, below).

  - Road widening to Henrico County Class I road standards is required. Coordinate with DPW Engineering Reviewer regarding need for curb and gutter.

- Show dimensions, right-of-way centerlines, curb return radii, and right-of-way widths of all roads (both sides) and intersections on the plans.

- The minimum allowable centerline radii for curves is 300 feet along newly proposed subdivision roads. Clarify dimensions.

- The minimum access point spacing is 250 feet along Drybridge Road. The minimum access point spacing is 150 feet along newly proposed public roads.

# STANDARD PLAN COMMENTS:

- Provide the vehicle trips per weekday, AM peak hour weekday trip generation (enter/exit) and PM peak hour weekday trip generation (enter/exit) on the plan cover sheet. There is a newer POD cover sheet that needs to be used that is available at http://henrico.us/works/design/.

- Show the minimum queue length for drive thru lanes. Refer to “Drive thru Lane” standards found at https://henrico.us/works/traffic/traffic-engineering-policies/. Drive thru lanes shall be 10’ wide at minimum with a minimum width 12’ wide bypass provided to allow motorists the opportunity to exit the drive thru and re-enter the parking lot.

- Henrico County standard curb and gutter is required around all interior driveways and around all parking areas.

- Henrico County standard independent curb is required. In private roads/parking lots, please label where proposed.

- Raised, landscaped islands with a minimum width of 9 feet are required at the ends of all rows of parking to separate parking areas from driveways.

- Label driveway widths, curb radii, and typical parking space dimensions on the plans.

- Curb radii adjacent to parking spaces need to be a minimum of 4.5 feet.

- There may be no more than 50 single-family lots on a single point of access.

- There may be no more than 82 multi-family units on a single point of access.

- Final grading details need to be shown in order to determine the need for guardrail or other accepted vehicular protection.

- Guardrail and proper end treatments are required along public roadways where the appropriate clear zone is not provided.  The approximate locations of the guardrail and end treatments need to be shown on the plan within the right-of-way or an easement.

- In private developments, guardrail or other accepted vehicular protection is required along drive aisles, parking lots or internal private roads adjacent to a BMP, or where a 7.5 feet wide clear zone having a graded 6:1 or flatter shelf from face of curb or near edge of pavement is not provided. When there is a water hazard with a depth of 2 feet or more, the minimum clear zone increases to 10 feet.  The approximate locations of the guardrail or other accepted vehicular protection need to be shown on the plans.

- Per Public Works policy, a standard Henrico County sidewalk with a 2 feet wide utility strip is required along Drybridge Road for the entire frontage of the property…Additionally, provide dimensions for all proposed sidewalk.

- All sidewalks must be located within right-of-way.

- Pedestrian passing areas may be needed in sidewalk. More dimensions need to be provided to make determination.

- Sidewalks that run along the end of parking spaces are required to be 5 feet wide.

- Wheel stops are required in any proposed handicap parking spaces and any regular parking spaces adjacent to the ramps.  Provide handicap parking signs, R7-8, in front of handicap parking spaces.

- The maximum length of road segment is 1320 feet.

- Show standard Henrico County end of road barricades.

- A standard R1-1 Stop Sign and 24 inch white stop bar are required at all points of egress from this development.

- Recommend standard R1-1 Stop Sign and 24 inch white stop at all internal intersections within the proposed development.

- Provide and show the locations of the subdivision street name signs. The street name signs must meet the specifications in the Department of Public Works Design Manual (Section 2-38). Signs for public roads shall display a green background with white lettering while signs for private roads shall display a white background with black lettering.

- Provide and show the locations of the subdivision speed limit signs and Stop signs.

- Specify the proposed type of posts for subdivision street name signs, stop signs, speed limit signs, etc. in the public right-of-way.  If not using the standard green u-channel, square wood or square metal posts in the public right-of-way, provide a Henrico County Right-of-Way Maintenance Agreement prior to plan approval. Any non-standard sign post must be approved by the Traffic Engineer prior to plan approval.  Provide a catalog cut of any proposed non-standard sign post.

- Within subdivisions, bump-outs are required on public residential roadways with a speed limit of 25 mph or less. Bump-outs are curb extensions that reduce the travel lanes along a roadway. They are predominantly located at intersections to reduce pedestrian crossing distances but may be installed at a mid-block section of roadway. Bump-outs are also used as a traffic calming measure. Locations of bump-outs should be coordinated with Traffic Engineering. An example of bump-outs is attached at the bottom of this document.

- No on-street parking will be permitted for this development on the adjacent public roads now or in the future.

- Provide intersection sight distance lines to scale on the plan for all public road intersections and access points onto the public right-of-way.  Provide a profile of the roadway along with the driver’s line of sight.  Show sight distance 14.5 feet from edge of travel lane.  Adequate sight distance must be demonstrated prior to Public Works’ approval of this plan.

- Sight Distance easements will be required for the proposed access points where the sight distance line is outside the proposed right-of-way. All easements need to be shown and identified on the plans.

- Sight Distance easements shall remain free of all structures, trees, shrubbery, and signs that are higher than 30” above the ground where the sight distance originates, except utility poles, fire hydrants, and traffic control signs.

- A minimum of 30 feet to the first point of conflict is required at the proposed private entrances from a public street. The spacing increases to 150 feet for developments with more than one business or greater than 82 housing units.

- All private two-way drive aisles need to be a minimum of 24 feet wide and a maximum of 30 feet wide.

- All one-way drive aisles need to be a minimum of 18 feet wide.  Henrico County Division of Fire may require 20 feet.

- Dedicated turn around spaces with adequate back-out room are required in any dead end of rows of parking.  Label the striped out turn around space and MUTCD standard NO PARKING sign on the plan.

- Bollards are needed for vehicular protection for any proposed doors that swing into the proposed drive aisles around the proposed building.  Details for the bollards need to be shown on the plans.

- Show truck movements on the plan.

- Provide a maintenance of traffic plan for all work proposed in the public right-of-way.

- Improvements along Williamsburg Road (State Route 60) must be approved by the Department of Transportation.

- A note needs to be included on the plans indicating: “A traffic signal exists at the intersection of 			 and 		           	. The contractor shall contact the Traffic Engineering Signal Shop at (804) 727-8303 with any questions pertaining to the signal. A Miss Utility ticket shall be called in to field locate traffic control equipment and cables at least 72 hours prior to beginning work on or adjacent to the right-of-way within 500 feet of the intersection. The contractor or developer will be responsible for the cost of repair or replacement of any damaged traffic control equipment.”

- A note needs to be included on the plans indicating: “If there are any Henrico County maintained signs within the construction limits that the contractor feels are in the way (along Drybridge Road, Old Williamsburg Road, and Old Memorial Drive), please contact Traffic Engineering at (804) 727-8296 for removal and re-installation.”

- Subject to VDOT approval, the developer is responsible for all costs associated with construction of a traffic signal at the intersection at the intersection of Dry Bridge Road and Williamsburg Road.

- A note needs to be included on the plans indicating: “The contractor is responsible for installing all stop signs, directional signs, and striping shown on the plans.”

- A note needs to be included on the plans indicating: “Coordinate in the field with Henrico County Traffic Engineering at 804-727-8282 regarding the striping and arrows amongst widened and newly proposed roads before installation. VDOT will oversee new striping on Williamsburg Road."

- Provide a dedicated pavement marking and traffic sign plan for all proposed road widening as indicated in proffer #13 of rezoning case REZ2020-00015. Please include any proposed crosswalk markings as well.

  - Provide a detail for all traffic signs proposed.

- Provide evidence that VDOT has reviewed the current scope of work shown on the plan and has no comments regarding the proposed work.

- All roads intersecting another road shall do so at an angle of 90 degrees for a minimum distance of 75’ from the centerline of each roadway in all directions. "Road" shall mean public road, private road, multifamily access, and commercial access.

- Additional comments will follow upon review of a detailed, subsequent submittal.

ADDITIONAL PLAN COMMENTS:

- Per the rezoning case exhibits for REZ2020-00015, the intersection design of (what is now shown as) Turtle Parkway & Fiddle Leaf Drive needs to be built as a roundabout. Since the Focal Point is close by and is planned to become a place where many pedestrians will be going to/from, a roundabout will slow traffic. I look forward to receiving dimensions and detail of the roundabout as this project progresses. Additionally:

  - The design of the roundabout shall be in accordance with the latest edition of the Federal Highway Administration publication “Roundabouts: An Informational Guide”.

  - No on street parking shall be allowed within 75’ of the outside edge of the roundabout, in any direction.

  - In determining the Intersection sight distance, the length of the approach leg of the sight distance triangle shall be 50 feet from the circulatory roadway.

  - The maintenance costs associated with the landscaping and the illumination in the roundabout shall be borne by the developer or HOA, as applicable.

  - Autoturn movements of larger vehicles will need to be provided per comment #39.

- Regarding townhome units 1-42: Clarify vehicle accessibility to townhome units 1-42. Are they intended to front load along the public road? If so, the townhomes need to have an adequately deep driveway so a car can get off the roadway and not have to wait for a garage door to open before exiting the roadway.

- Regarding townhome units 12-23: The number of units should be dropped in each block.  Remove one unit closest to Dry Bridge and one-two units closest to intersection of Turtle Parkway & Fiddle Leaf Drive.  They are too close to Dry Bridge and footprint of a roundabout.

- Provide a road profile for the proposed public streets.

- Provide stationing along the roads to be improved and the proposed roads.

- Provide cross-sections for the widening of all existing roads to be improved in 25’ intervals.

- Road mill & overlay must be provided for the existing through lane adjacent to any road widening. Provide VDOT WP-2 detail for road widening.

- Add Henrico County standard construction notes & details sheet to the plans. The sheet can be found at https://henrico.us/works/construction/, at the bottom of the page.

- At “DRYBRIDGE EAST COMMERCIAL LOTS”, provide an internal connection between the two.

- Clarify a master plan for the full development of Drybridge Commons. The Rezoning case showed additional development on the west side of Drybridge Road.

- Provide a VDOT standard CG-9D apron for each private access from the public roadway. Provide VDOT standard detail in the plans.

- Provide VDOT standard CG-12 locations and details on the plans for proposed curb ramps.

Brandon House, E.I.T.

Traffic Review Engineer

County of Henrico - Department of Public Works
P.O. Box 90775 Henrico, VA 23273-0775

804.501.4661 phone | 804.501.7470 fax

hou018@henrico.us | www.henrico.us/works/traffic/