LAND-DISTURBANCE TYPE DETERMINATION AND APPLICABLE REQUIREMENTS

Using the Land-Disturbance Type Determination Worksheet (attached) found in Chapter 3 of the Henrico County Environmental Compliance Manual (Manual), this project has been determined to be:

both a VESCP land-disturbing activity and a VSMP land-disturbing activity

CURB AND GUTTER / STORM SEWER:

- Provide profiles for all proposed storm sewers

- Provide an itemized list (including descriptions) of all drainage structures on the plan and indicate whether inlet shaping, steps, and/or O-ring pipe are proposed

- Provide the following information for all curb and gutter/storm sewer systems:

Velocity (minimum allowable of 2 fps for 2-year storm)

Hydraulic grade line computations noting below calculations how starting water surface elevation was obtained

ADDITIONAL COMMENTS:

- Sheet DA-1:  Label drainage area call-out circles with matching storm sewer.

- Sheet DA-1:  Add C value to call-out circles.

- Sheet DA-1:  Show Tc path for drainage areas where 5 minute minimum is not assumed.

- Sheet DA-1:  Darken drainage area delineations relevant to proposed storm sewer.

- Sheet Calc-1:  Add composite runoff coefficient calculations in tabular format for storm 1-25.

Additional comments may follow upon review of a subsequent submittal.

The Engineering Section has completed its review and has no comments at this time.

OTHER REVIEW AGENCIES

Please see the attached comments from the Environmental Division

Please see the attached comments from the Traffic Engineering Division

Please see the attached comments from the Construction Division

Reviewed by:	Doug Young

Date Reviewed:	14 April 2021

Phone Number:	501-5851

E-mail:	you071@henrico.us

OCT. 2018