# PLANNING COMMISSION RECOMMENDATION:

The Traffic Engineering Section:

can recommend approval of this project to the Planning Commission. Recommendation made on the basis that the layout reflects the updated terminus of Waterfront Place as shown on updated sheet C11.04 as received by email on April 23, 2021. Comments for the project otherwise remain as before (save for comment #s 60 and 61, now crossed out).

cannot recommend approval of this project to the Planning Commission because:

# ROAD IMPROVEMENT COMMENTS:

- Road improvements and/or right-of-way dedication is required.

- With the removal of the cul-de-sac at the existing public terminus of Waterfront Place, Public Works requires the extended right-of-way to terminate with an adequate turn around. In the spirit of both providing a turn around and improving the intersection of Waterfront Place & Dominion Boulevard, Public Works will look for the new right-of-way to terminate as a roundabout:

  - The design of the roundabout shall be in accordance with the latest edition of the Federal Highway Administration publication “Roundabouts: An Informational Guide”.

  - Adequate right-of-way must be provided to encompass the entirety of the roundabout.

  - No on street parking shall be allowed within 75’ of the outside edge of the roundabout, in any direction.

  - In determining the Intersection sight distance, the length of the approach leg of the sight distance triangle shall be 50 feet from the circulatory roadway.

  - The maintenance costs associated with the landscaping and the illumination in the roundabout shall be borne by the developer or HOA, as applicable.

  - Autoturn movements for larger vehicles will need to be provided.

- Along the new public extension of Waterfront Place, along the eastbound lane, modify the median to provide a dedicated left turn lane at the intersection of Waterfront Place and Waterfront Drive.

- Show dimensions, right-of-way centerlines, curb return radii, and right-of-way widths of all roads (both sides) and intersections on the plans. Label proposed right-of-way radius at the new end of Waterfront Place.

- The minimum allowable centerline radii for curves is … feet along ...

- The minimum access point spacing is … feet along …

# STANDARD PLAN COMMENTS:

- Provide the vehicle trips per weekday, AM peak hour weekday trip generation (enter/exit) and PM peak hour weekday trip generation (enter/exit) on the plan cover sheet. There is a newer POD cover sheet that needs to be used that is available at http://henrico.us/works/design/.

- Show the minimum queue length for drive thru lanes.

- Henrico County standard curb and gutter is required around all interior driveways and around all parking areas.

- Henrico County standard independent curb is required.

- Raised, landscaped islands with a minimum width of 9 feet are required at the ends of all rows of parking to separate parking areas from driveways.

- Label driveway widths, curb radii, and typical parking space dimensions on the plans. Some driveway width dimensions are not provided on the plans.

- Curb radii adjacent to parking spaces need to be a minimum of 4.5 feet.

- There may be no more than 50 single-family lots on a single point of access.

- There may be no more than 82 multi-family units on a single point of access.

- Final grading details need to be shown in order to determine the need for guardrail or other accepted vehicular protection.

- Guardrail and proper end treatments are required along public roadways where the appropriate clear zone is not provided.  The approximate locations of the guardrail and end treatments need to be shown on the plan within the right-of-way or an easement.

- In private developments, guardrail or other accepted vehicular protection is required along drive aisles, parking lots or internal private roads adjacent to a BMP, or where a 7.5 feet wide clear zone having a graded 6:1 or flatter shelf from face of curb or near edge of pavement is not provided. When there is a water hazard with a depth of 2 feet or more, the minimum clear zone increases to 10 feet.  The approximate locations of the guardrail or other accepted vehicular protection need to be shown on the plans.

- Per Public Works policy, a standard Henrico County sidewalk with a 2 feet wide utility strip is required along Waterfront Place for the entire frontage of the property. Consider carrying sidewalk from Waterfront Place to connect to the site along Dominion Boulevard.

- All sidewalks must be located within right-of-way. Comment only applies for Waterfront Place sidewalk.

- Pedestrian passing areas may be needed in sidewalk. This is dependent on the typical sidewalk width.

- Sidewalks that run along the end of parking spaces are required to be 5 feet wide.

- Wheel stops are required in any proposed handicap parking spaces and any regular parking spaces adjacent to the ramps.  Provide handicap parking signs, R7-8, in front of handicap parking spaces.

- The maximum length of road segment is 1320 feet.

- Show standard Henrico County end of road barricades.

- A standard R1-1 Stop Sign and 24 inch white stop bar are required at all points of egress from this development.

- Recommend standard R1-1 Stop Sign and 24 inch white stop at all internal intersections within the proposed development.

- Provide and show the locations of the subdivision street name signs. The street name signs must meet the specifications in the Department of Public Works Design Manual (Section 2-38). Signs for public roads shall display a green background with white lettering while signs for private roads shall display a white background with black lettering.

- Provide and show the locations of the subdivision speed limit signs and Stop signs.

- Specify the proposed type of posts for subdivision street name signs, stop signs, speed limit signs, etc. in the public right-of-way.  If not using the standard green u-channel, square wood or square metal posts in the public right-of-way, provide a Henrico County Right-of-Way Maintenance Agreement prior to plan approval. Any non-standard sign post must be approved by the Traffic Engineer prior to plan approval.  Provide a catalog cut of any proposed non-standard sign post.

- Within subdivisions, bump-outs are required on public residential roadways with a speed limit of 25 mph or less. Bump-outs are curb extensions that reduce the travel lanes along a roadway. They are predominantly located at intersections to reduce pedestrian crossing distances but may be installed at a mid-block section of roadway. Bump-outs are also used as a traffic calming measure. Locations of bump-outs should be coordinated with Traffic Engineering. Traffic Engineering will provide an example of bump-outs upon request.

- No on-street parking will be permitted for this development on the adjacent public roads now or in the future.

- Provide intersection sight distance lines to scale on the plan for all access points onto the public right-of-way.  Provide a profile of the roadway along with the driver’s line of sight.  Show sight distance 14.5 feet from edge of travel lane.  Adequate sight distance must be demonstrated prior to Public Works’ approval of this plan.

- Sight Distance easements will be required for the proposed access points where the sight distance line is outside the proposed right-of-way. All easements need to be shown and identified on the plans.

- Sight Distance easements shall remain free of all structures, trees, shrubbery, and signs that are higher than 30” above the ground where the sight distance originates, except utility poles, fire hydrants, and traffic control signs.

- A minimum of 30 feet to the first point of conflict is required at the proposed entrances from a public street.

- All two-way drive aisles need to be a minimum of 24 feet wide and a maximum of 30 feet wide.

- All one-way drive aisles need to be a minimum of 18 feet wide.  Henrico County Division of Fire may require 20 feet.

- Dedicated turn around spaces with adequate back-out room are required in any dead end of rows of parking.  Label the striped out turn around space and MUTCD standard NO PARKING sign on the plan.

- Bollards are needed for vehicular protection for any proposed doors that swing into the proposed drive aisles around the proposed building.  Details for the bollards need to be shown on the plans.

- Show truck movements on the plan.

- Provide a maintenance of traffic plan for all work proposed in the public right-of-way.

- Improvements along ... (State Route ...) must be approved by the Department of Transportation.

- A note needs to be included on the plans indicating: “A traffic signal exists at the intersection of Cox Road and Waterfront Place. The contractor shall contact the Traffic Engineering Signal Shop at (804) 727-8303 with any questions pertaining to the signal. A Miss Utility ticket shall be called in to field locate traffic control equipment and cables at least 72 hours prior to beginning work on or adjacent to the right-of-way within 500 feet of the intersection. The contractor or developer will be responsible for the cost of repair or replacement of any damaged traffic control equipment.”

- A note needs to be included on the plans indicating: “If there are any Henrico County maintained signs within the construction limits that the contractor feels are in the way, please contact Traffic Engineering at (804) 727-8296 for removal and re-installation.”

- The developer is responsible for all costs associated with modifying any existing traffic signal adjacent to the site.

- A note needs to be included on the plans indicating: “The contractor is responsible for installing all stop signs, directional signs, and striping shown on the plans.”

- A note needs to be included on the plans indicating: “Coordinate in the field with Henrico County Traffic Engineering at 804-727-8282 regarding the striping and arrows on Waterfront Place before installation."

- Show proposed striping and arrows on the plan for the improvements of Waterfront Place.

- Provide evidence that VDOT has reviewed the current scope of work shown on the plan and has no comments regarding the proposed work.

- All roads intersecting another road shall do so at an angle of 90 degrees for a minimum distance of 75’ from the centerline of each roadway in all directions. "Road" shall mean public road, private road, multifamily access, and commercial access.

- Additional comments may follow upon review of a subsequent submittal.

ADDITIONAL PLAN COMMENTS:

General:

- Clarify why proffer #10 of rezoning case REZ2020-00044 specifies that the improvements made to private maintained Dominion Boulevard are subject to final approval of the Director of Public Works.

- Is there a master plan for this development? On sheets C8.01 & C8.02 I see annotations calling for future path and driveway connections

Sheet C8.00 (Overall Layout):

- Clarify what the dashed lines behind the buildings represent.

Sheet C8.01 (Layout Plan):

- For the parking spaces in front of apartment building #2, concerned about the proximity of parking spaces nearest to the intersecting drive aisle. Vehicles backing out of the spaces look capable of backing into the intersecting drive aisle. Consider removing 1-2 spaces of each end.

Sheet C11.03 (Roadway Plan):

- Recommend adding W11-2 and W16-7P signs to accompany crosswalk markings.

- Provide details for any proposed traffic signs in the plans.

- Recommend specifying pavement marking material.

- Ensure correct road width dimensions are established between cross-sections and plan view. Some of the dimensions for both the full road widths and lane widths do not match up between.

- For pedestrian safety, crosswalks should be relocated out of turn lanes. They are typically located near intersections.

- Highly recommend removal of shared center turn lanes in favor of turn lanes dedicated for single directions of traffic.

- The center turn lane markings between the proposed point of access on the north side of Dominion Boulevard and the near one on the south side make no sense. Revise.

- Right turn lane widths should be 12’ wide relative to the edge of pavement, not the face of curbing.

- The minimum width of a crosswalk is 6’. Clarify that this is provided.

Sheet C11.04 (Roadway Plan):

- Clarify striping proposed on Waterfront Place. It is not labelled by any letters from the pavement marking legend.

- Provide a note stating: “All striping within the Public right-of-way shall be type B, class I thermoplastic and meet the current requirements of the VDOT road and bridge specifications. Markings shall have a minimum thickness of 90 mil.”

Sheet C12.01 (MOT Plan):

- Label any proposed temporary pavement markings and specify color.

Sheet C12.04 (MOT Notes and Details):

- Add following notes to the MOT plans:

  - Work hours within Waterfront Place are 9:00AM-4:00PM, Monday through Friday.

  - Except for emergencies, no lane closures or other traffic restrictions shall be erected during periods of inclement weather.

  - The Contractor shall coordinate all lane closures with Henrico Police/Fire (804-501-5000) and Pupil Transportation/ Schools (804-226-5570).

  - The Contractor is responsible for the maintenance of all signs and posts in the work zone.  This includes, but is not limited to, stop, yield, street name and speed limit signs.  Any sign or post damaged during construction or missing shall be replaced by the Contractor at his expense.

  - The Traffic Engineer (804-727-8282) reserves the right to modify the traffic control on Waterfront Place as necessary in the interests of public safety and/or convenience.

  - Unless otherwise approved, no equipment or materials are to be left in the county right-of-way after work hours.  Should permission be given to allow equipment and materials in the right-of-way after work hours, group II channelizing devices (plastic barrels with prismatic sheeting) shall be used to delineator the obstacles.  Equipment and materials shall be placed in areas that would have no adverse impact to the property owners and shall not obstruct any sight distances or create any other safety issues.

  - All employees exposed to vehicular traffic shall be provided with and instructed to wear warning vests marked with or made of reflectorized or high visibility materials meeting Class III standards.

  - The Contractor is responsible for maintaining access to all affected property owners within the limits of work.

  - The Contractor is responsible for all notifications made to affected property owners, management groups, and the travelling public.

Please let me know if you have any questions.

Thank you,

Brandon House, E.I.T.

Traffic Review Engineer

County of Henrico - Department of Public Works
P.O. Box 90775 Henrico, VA 23273-0775

804.501.4661 phone | 804.501.7470 fax

hou018@henrico.us | www.henrico.us/works/traffic/