# PLANNING COMMISSION RECOMMENDATION:

The Traffic Engineering Section:

can recommend approval of this project to the Planning Commission.

cannot recommend approval of this project to the Planning Commission because:

# REMAINING STANDARD PLAN COMMENTS:

- A standard R1-1 Stop Sign and 24 inch white stop bar are required at all points of egress from this development. (8/2/21): Thank you for providing the stop sign at the intersection of Brookwood Glen Lane & Terrace. Remove the proposed stop bar here.

- Dedicated turn around spaces with adequate back-out room are required in any dead end of rows of parking.  Label the striped out turn around space and MUTCD standard NO PARKING sign on the plan. (8/2/21): Please relocate this space to be on the left side of the dead end (as you approach the dead end). This allows for easier vehicle maneuvers into the space.

- Additional comments may follow upon review of a subsequent submittal.

ADDITIONAL PLAN COMMENTS:

General:

- Provide dimensions for lane & median widths on the plan. (8/2/21): Per County typical cross-sectional detail (on sheet C39), the median should be 14’ wide when the area is not being used for a left turn lane. Why is it dimensioned 13’?

- Show dimensions for the proposed parallel parking spaces on the plans. (8/2/21): Clarify dimensions. It’s somewhat confusing to have two ‘typical’ dimensions for 3 parking spaces (shown on sheet C10).

- Road mill & overlay must be provided for the existing through lane adjacent to the road widening on Magellan Pkwy.

Sheet C9 (Layout & Utility Plan [North]):

- On Telegraph Road, extend sidewalk to northern property line.

- Clarify sidewalk and utility strip dimensions relative to Telegraph Road curbing where sidewalk is proposed within Telegraph Road right-of-way. A 2’ wide utility strip is typically provided per County standards.

Sheet C10 (Layout & Utility Plan [South]):

- At the intersection of Magellan Pkwy & Telegraph Rd:

  - (At the westbound approach) extend turn lane storage to match up with the labelled 200’ dimension. The turn lane storage appears to scale slightly shorter than 200’.

  - The sidewalk segment at the northeast corner of the intersection, extending east along Magellan Pkwy, should extend from the eastern edge of the curb ramp.

- At approximately STA 18+50, remove the “ex. R3-5r sign”

- Revise location of the meandering sidewalk as it approaches the intersection of Englewood Farms Drive and Magellan Pkwy…Pedestrians (on Magellan Pkwy) may be more inclined to walk across the grass from the intersection to the meandering sidewalk segment in front of building 11.

Sheet C11 (Layout & Utility Plan [East]):

- At the site’s access from public Brookwood Glen Terrace, recommend installing monuments at the access to further denote the exit from public right-of-way to private property. (8/2/21): Though mentioned in the comment/response letter, I was unable to locate the monuments at this access. Please clarify where I find these.

- Add street signs at the intersection of Brookwood Glen Terrace (public) and Brookwood Glen Terrace (private) to differentiate ownership of the roadways.

- At the intersection of Englewood Farms Drive & Magellan Parkway, construct a short portion of public sidewalk extending east from the intersection and parallel with Magellan Parkway to the terminus of the curb and gutter. Sidewalk to reside in public right-of-way. Provide a sidewalk easement as necessary for the CG-9D crossing.

Sheet C42 (Site Details):

- Use TTC-42.2 (Interior Lane Closure on a Multi-Lane Roadway) in lieu of TTC-7.1 for median work.

- Revise sequence of construction:

  - DO NOT INSTALL CENTER MEDIANS UNTIL EAST BOUND WIDENING IS COMPLETE needs to be revised to WEST BOUND.

  - Change ‘stripping’ to ‘striping’

Sheet C43 (Striping Plan and Details):

- In pavement marking legend, provide a means for identifying existing pavement markings versus proposed pavement markings.

- Remove “PROPOSED MINI-SKIPS STA 22+60 to STA 23+43”

- For Magellan Pkwy WB, east of its intersection with Telegraph Road:

  - In the right turn lane, extend single solid white line to match storage length of left turn lane.

- For Magellan Pkwy EB, east of its intersection with Telegraph Road:

  - Leave existing turn arrows in the right turn lane leading to Section 1’s access. No need to remove these.

- Mill and overlay area will need to cover where double solid yellow lines will be removed.

Should you have any questions, please let me know.

Thanks,

Brandon House, E.I.T.

Traffic Review Engineer

County of Henrico - Department of Public Works
P.O. Box 90775 Henrico, VA 23273-0775

804.501.4661 phone | 804.501.7470 fax

hou018@henrico.us | www.henrico.us/works/traffic/