# PLANNING COMMISSION RECOMMENDATION:

The Traffic Engineering Section:

can recommend approval of this project to the Planning Commission.

cannot recommend approval of this project to the Planning Commission because:

- Road Improvements along Dry Bridge Road need to be shown in full extent from Williamsburg Road to northern project limits of phase 1. Improvements need to clearly show dimensions from centerline to face of curbing to demonstrate adequacy. See comment #1.

- Right-of-way dimensions for Dry Bridge Road need to be provided on the plans. See comment #2.

- Dimensions and specifications need to be shown for the roundabout at intersection of Fiddle Leaf Drive and Turtle Parkway. See comment #2.

- Horizontal curves must have a minimum centerline length of curve of 100 feet

- Truck movements need to be provided to show a truck can use the roundabout to make a left turn (maneuvering properly around the roundabout to turn from one street to the intersecting street). See comment #39.

# ROAD IMPROVEMENT COMMENTS:

- Road improvements and/or right-of-way dedication may be required (pending confirmation of existing right-of-way dimensions).

Right-of-way dedication to 45 feet from centerline of right-of-way is required for property frontage along Dry Bridge Road to accommodate the right turn lanes.

Road widening with Henrico County curb & gutter to 26 feet from centerline is required along Dry Bridge Road. Dry Bridge Road shall be widened to 38 feet from centerline (to face of curbing) for the right turn lanes.

Road widening to ... feet from centerline and a --- feet wide shoulder is required along .....................

Minimum improvements required, including 4’ stabilized shoulders and associated ditch

work for adequate drainage along ............................

- Show dimensions, right-of-way centerlines, curb return radii, and right-of-way widths of all roads (both sides) and intersections on the plans. Additionally, the following dimensions need to be shown for the roundabout: inscribed diameter, center island diameter, circulatory lane width, entering and exiting lane widths, truck apron diameter, entry curves, exit curves, and resultant design speed.

- The minimum allowable centerline radii for curves is 300 feet along residential streets. Horizontal curves shall be minimum 100’ long.

- The minimum access point spacing is … feet along …

# STANDARD PLAN COMMENTS:

- Provide the vehicle trips per weekday, AM peak hour weekday trip generation (enter/exit) and PM peak hour weekday trip generation (enter/exit) on the plan cover sheet. There is a newer POD cover sheet that needs to be used that is available at http://henrico.us/works/design/.

- Show the minimum queue length for drive thru lanes.

- Henrico County standard curb and gutter is required around all interior driveways and around all parking areas.

- Henrico County standard independent curb is required.

- Raised, landscaped islands with a minimum width of 9 feet are required at the ends of all rows of parking to separate parking areas from driveways.

- Label driveway widths, curb radii, and typical parking space dimensions on the plans.

- Curb radii adjacent to parking spaces need to be a minimum of 4.5 feet.

- There may be no more than 50 single-family lots on a single point of access.

- There may be no more than 82 multi-family units on a single point of access.

- Final grading details need to be shown to determine the need for guardrail or other accepted vehicular protection… Clarify conflicting grades shown between units 7-12 and Orange Blossom Lane.

- Guardrail and proper end treatments are required along public roadways where the appropriate clear zone is not provided.  The approximate locations of the guardrail and end treatments need to be shown on the plan within the right-of-way or an easement…Area of concern is grading by intersection of Dry Bridge Road and Orange Blossom Lane…Can the 3:1 slopes be graded to 4:1?

- In private developments, guardrail or other accepted vehicular protection is required along drive aisles, parking lots or internal private roads adjacent to a BMP, or where a 7.5 feet wide clear zone having a graded 6:1 or flatter shelf from face of curb or near edge of pavement is not provided. When there is a water hazard with a depth of 2 feet or more, the minimum clear zone increases to 10 feet.  The approximate locations of the guardrail or other accepted vehicular protection need to be shown on the plans.

- Per Public Works policy, a standard Henrico County sidewalk with a 2 feet wide utility strip is required along ……………. for the entire frontage of the property.

- All sidewalks must be located within right-of-way.

- Pedestrian passing areas are needed in sidewalk.

- Sidewalks that run along the end of parking spaces are required to be 5 feet wide.

- Wheel stops are required in any proposed handicap parking spaces and any regular parking spaces adjacent to the ramps.  Provide handicap parking signs, R7-8, in front of handicap parking spaces. Comment made in anticipation of Building Inspections reviewer requiring handicap parking spaces.

- The maximum length of road segment is 1320 feet.

- Show standard Henrico County end of road barricades with road extension signs (as shown on sheet 26).

- A standard R1-1 Stop Sign and 24 inch white stop bar are required at all points of egress onto the public right-of-way

- Recommend standard R1-1 Stop Signs and 24 inch white stop at all internal intersections within the proposed development

- Provide and show the locations of the subdivision street name signs. The street name signs must meet the specifications in the Department of Public Works Design Manual (Section 2-38). Signs for public roads shall display a green background with white lettering while signs for private roads shall display a white background with black lettering.

- Provide and show the locations of the subdivision speed limit signs.

- Specify the proposed type of posts for subdivision street name signs, stop signs, speed limit signs, etc. in the public right-of-way.  If not using the standard green u-channel, square wood or square metal posts in the public right-of-way, provide a Henrico County Right-of-Way Maintenance Agreement prior to plan approval. Any non-standard sign post must be approved by the Traffic Engineer prior to plan approval.  Provide a catalog cut of any proposed non-standard sign post.

- Within subdivisions, bump-outs are required on public residential roadways with a speed limit of 25 mph or less. Bump-outs are curb extensions that reduce the travel lanes along a roadway. They are predominantly located at intersections to reduce pedestrian crossing distances but may be installed at a mid-block section of roadway. Bump-outs are also used as a traffic calming measure. Locations of bump-outs should be coordinated with Traffic Engineering. Traffic Engineering will provide an example of bump-outs upon request.

- No on-street parking will be permitted for this development on the adjacent public roads now or in the future.

- Provide intersection sight distance lines to scale on the plan for all access points onto the public right-of-way.  Provide a profile of the roadway along with the driver’s line of sight.  Show sight distance 14.5 feet from edge of travel lane.  Adequate sight distance must be demonstrated prior to Public Works’ approval of this plan. Roundabout sight distance lines will also need to be shown. In determining the intersection sight distance, the length of the approach leg of the sight distance triangle shall be 50 feet from the circulatory roadway… Adequate sight distance, according to the criteria found in “Roundabouts: In Information Guide”, must be demonstrated prior to Public Works’ approval of this plan. Sight distance lines should be shown on its own plan sheet.

- Sight Distance easements will be required for the proposed access points where the sight distance line is outside the proposed right-of-way. All easements need to be shown and identified on the plans.

- Sight lines and Sight Distance easements shall remain free of all structures, trees, shrubbery, and signs that are higher than 30” above the ground where the sight distance originates, except utility poles, fire hydrants, and traffic control signs.

- A minimum of 30 feet to the first point of conflict is required at the proposed entrances from a public street.

- All two-way drive aisles need to be a minimum of 24 feet wide and a maximum of 30 feet wide.

- All one-way drive aisles need to be a minimum of 18 feet wide.  Henrico County Division of Fire may require 20 feet.

- Dedicated turn around spaces with adequate back-out room are required in any dead end of rows of parking.  Label the striped out turn around space and MUTCD standard NO PARKING sign on the plan…Add fire lane signs at end of Alley #1.

- Bollards are needed for vehicular protection for any proposed doors that swing into the proposed drive aisles around the proposed building.  Details for the bollards need to be shown on the plans.

- Show truck movements on the plan. Truck movements need to be provided to show a truck can use the roundabout to make a left turn (maneuvering properly around the roundabout to turn from one street to the intersecting street)

- Provide a maintenance of traffic plan for all work proposed in the public right-of-way.

- Improvements along Williamsburg Road (U.S. Route 60) must be approved by the Department of Transportation.

- A note needs to be included on the plans indicating: “A traffic signal exists at the intersection of 			 and 		           	. The contractor shall contact the Traffic Engineering Signal Shop at (804) 727-8303 with any questions pertaining to the signal. A Miss Utility ticket shall be called in to field locate traffic control equipment and cables at least 72 hours prior to beginning work on or adjacent to the right-of-way within 500 feet of the intersection. The contractor or developer will be responsible for the cost of repair or replacement of any damaged traffic control equipment.”

- A note needs to be included on the plans indicating: “If there are any Henrico County maintained signs within the construction limits that the contractor feels are in the way, please contact Traffic Engineering at (804) 727-8296 for removal and re-installation.”

- The developer is responsible for all costs associated with modifying any existing traffic signal adjacent to the site.

- A note needs to be included on the plans indicating: “The contractor is responsible for installing all stop signs, directional signs, and striping shown on the plans.”

- A note needs to be included on the plans indicating: “Coordinate in the field with Henrico County Traffic Engineering at 804-727-8282 regarding the striping and arrows on 		  before installation."

- Show proposed striping, arrows, and traffic signs on the plan for the widening of Dry Bridge Road and construction of Turtle Parkway and Orange Blossom Lane.

- Provide evidence that VDOT has reviewed the current scope of work shown on the plan and has no comments regarding the proposed work.

- All roads intersecting another road shall do so at an angle of 90 degrees for a minimum distance of 75’ from the centerline of each roadway in all directions. "Road" shall mean public road, private road, multifamily access, and commercial access.

- Additional comments may follow upon review of a subsequent submittal.

ADDITIONAL PLAN COMMENTS:

Sheet 4 (Layout & Utility Plan):

- CG-9D aprons need to be provided at all accesses onto private property from public right-of-way.

- Label and show all CG-12 ramps.

- CG-12 ramps need to be provided at the intersection of Fiddle Leaf Dr & Orange Blossom Lane

- Re-route sidewalks at the end of Alley #1 (at western end of units 12 and 13) to run toward one another. Recommend providing curb ramps to allow crossing across the drive aisle.

- Clarify where the mailboxes are located. I was unable to locate this detail on the plans.

- Add driveway stub for future restaurant parcel.

Sheet 7 (E&SC Plan Ph. 1):

- In step #7:

  - Revise typo ‘intall’ in first sentence.

  - The third sentence references basins “A & C”. It appears only two basins (“A” & “B”) are proposed.

Sheet 16 (Cross Sections):

- What street(s) are these cross-sections for?

- Provide a vertical and horizontal scale.

- Clarify inclusion of some odd cross-section intervals.

- Are there more cross-sections beyond these?

Sheet 23 (Notes & Details):

- The GENERAL NOTES included need to remove/revise all references from VDOT to Henrico County (as applicable).

Sheet 26 (Standard Construction Notes & Details):

- In the END ROAD BARRICADE detail. Remove the last sentence found under the picture. The County no longer installs these reflectorized signs (OM4-2).

Sheet 27 (MOT & Striping Plan):

- In the MOT Notes:

  - In the first note, revise street name to “Dry Bridge Road”.

  - Delete the second note.

Brandon House, E.I.T.

Traffic Review Engineer

County of Henrico - Department of Public Works
P.O. Box 90775 Henrico, VA 23273-0775

804.501.4661 phone | 804.501.7470 fax

hou018@henrico.us | www.henrico.us/works/traffic/