# PLANNING COMMISSION RECOMMENDATION:

The Traffic Engineering Section:

can recommend approval of this project to the Planning Commission.

cannot recommend approval of this project to the Planning Commission because:

- A right-of-way centerline and right-of-way dimensions (width extending from the centerline to the property frontage) need to be clearly shown to demonstrate dedication is adequate to current standards. See comment #s 1 & 2 below.

# ROAD IMPROVEMENT COMMENTS:

- Road improvements and/or right-of-way dedication is required.

Right-of-way dedication to 57 feet from centerline of right-of-way is required for property frontage along both Pouncey Tract Road & Twin Hickory Lake Drive to accommodate the right turn lanes and sidewalk.

Road widening with Henrico County curb & gutter to ... feet from centerline is required along ...

Road widening to ... feet from centerline and a --- feet wide shoulder is required along .....................

Minimum improvements required, including 4’ stabilized shoulders and associated ditch

work for adequate drainage along ............................

- Show dimensions, right-of-way centerlines, curb return radii, and right-of-way widths of all roads (both sides) and intersections on the plans.

- The minimum allowable centerline radii for curves is … feet along ...

- The minimum access point spacing is … feet along …

# STANDARD PLAN COMMENTS:

- Provide the vehicle trips per weekday, AM peak hour weekday trip generation (enter/exit) and PM peak hour weekday trip generation (enter/exit) on the plan cover sheet. There is a newer POD cover sheet that needs to be used that is available at http://henrico.us/works/design/.

- Show the minimum queue length for drive thru lanes.

- Henrico County standard curb and gutter is required around all interior driveways and around all parking areas and along widened Twin Hickory Lake Drive. Specify.

- Henrico County standard independent curb is required.

- Raised, landscaped islands with a minimum width of 9 feet are required at the ends of all rows of parking to separate parking areas from driveways.

- Label driveway widths, curb radii, and typical parking space dimensions on the plans.

- Curb radii adjacent to parking spaces need to be a minimum of 4.5 feet.

- There may be no more than 50 single-family lots on a single point of access.

- There may be no more than 82 multi-family units on a single point of access.

- Final grading details need to be shown in order to determine the need for guardrail or other accepted vehicular protection.

- Guardrail and proper end treatments are required along public roadways where the appropriate clear zone is not provided.  The approximate locations of the guardrail and end treatments need to be shown on the plan within the right-of-way or an easement.

- In private developments, guardrail or other accepted vehicular protection is required along drive aisles, parking lots or internal private roads adjacent to a BMP, or where a 7.5 feet wide clear zone having a graded 6:1 or flatter shelf from face of curb or near edge of pavement is not provided. When there is a water hazard with a depth of 2 feet or more, the minimum clear zone increases to 10 feet.  The approximate locations of the guardrail or other accepted vehicular protection need to be shown on the plans.

- Per Public Works policy, a standard Henrico County sidewalk with a 2 feet wide utility strip is required along ……………. for the entire frontage of the property.

- All sidewalks must be located within right-of-way or within a permanent easement. Reference made to sidewalk proposed on Pouncey Place.

- Pedestrian passing areas are needed in sidewalk.

- Sidewalks that run along the end of parking spaces are required to be 5 feet wide independent of the width of the curbing.

- Wheel stops are required in any proposed handicap parking spaces and any regular parking spaces adjacent to the ramps.  Specify handicap parking signs as R7-8 in front of handicap parking spaces

- The maximum length of road segment is 1320 feet.

- Show standard Henrico County end of road barricades.

- A standard R1-1 Stop Sign and 24 inch white stop bar are required at all points of egress from this development.

- Recommend standard R1-1 Stop Sign and 24-inch white stop at the easternmost T-intersection found by the match line on sheets C-302 and C-303. Recommend stop condition be placed on the eastbound approach to the intersection.

- Provide and show the locations of the subdivision street name signs. The street name signs must meet the specifications in the Department of Public Works Design Manual (Section 2-38). Signs for public roads shall display a green background with white lettering while signs for private roads shall display a white background with black lettering.

- Provide and show the locations of the subdivision speed limit signs and Stop signs.

- Specify the proposed type of posts for subdivision street name signs, stop signs, speed limit signs, etc. in the public right-of-way.  If not using the standard green u-channel, square wood or square metal posts in the public right-of-way, provide a Henrico County Right-of-Way Maintenance Agreement prior to plan approval. Any non-standard sign post must be approved by the Traffic Engineer prior to plan approval.  Provide a catalog cut of any proposed non-standard sign post.

- Within subdivisions, bump-outs are required on public residential roadways with a speed limit of 25 mph or less. Bump-outs are curb extensions that reduce the travel lanes along a roadway. They are predominantly located at intersections to reduce pedestrian crossing distances but may be installed at a mid-block section of roadway. Bump-outs are also used as a traffic calming measure. Locations of bump-outs should be coordinated with Traffic Engineering. Traffic Engineering will provide an example of bump-outs upon request.

- No on-street parking will be permitted for this development on the adjacent public roads now or in the future.

- Provide intersection sight distance lines to scale on the plan for all access points onto the public right-of-way.  Provide a profile of the roadway along with the driver’s line of sight.  Show sight distance 14.5 feet from edge of travel lane (provide this dimension on the plans).  Adequate sight distance must be demonstrated prior to Public Works’ approval of this plan. Comment made regarding easternmost Twin Hickory Lake Drive access. See comment #33 for more information.

- Sight Distance easements will be required for the proposed access points where the sight distance line is outside the proposed right-of-way. All easements need to be shown and identified on the plans.

- Sight Distance lines and easements shall remain free of all structures, trees, shrubbery, and signs that are higher than 30” above the ground where the sight distance originates, except utility poles, fire hydrants, and traffic control signs. Per the sight distance profile on sheet C-805 the easternmost entrance on Twin Hickory Lake Drive has inadequate clearance (minimum 1’ of clearance over the finished grade) for the sight line looking right. Will any of the existing trees within the median on Twin Hickory Lake Drive remain beyond the new WB left turn lane?

- A minimum of 150 feet to the first point of conflict is required at the proposed entrances from a public street for developments with more than one business or greater than 82 housing units..

- All two-way drive aisles need to be a minimum of 24 feet wide and a maximum of 30 feet wide. Reference made to the reduced with drive aisle widths by the PROP CARRIAGE HOUSEs

- All one-way drive aisles need to be a minimum of 18 feet wide.  Henrico County Division of Fire may require 20 feet.

- Dedicated turn around spaces with adequate back-out room are required in any dead end of rows of parking.  Label the striped out turn around space and MUTCD standard NO PARKING sign on the plan. Please include a detail of the NO PARKING sign proposed.

- Bollards are needed for vehicular protection for any proposed doors that swing into the proposed drive aisles around the proposed building.  Details for the bollards need to be shown on the plans.

- Show truck movements on the plan. How would a trash truck access the enclosure between retail buildings 3 and 4?

- Provide a maintenance of traffic plan for all work proposed in the public right-of-way.

- Improvements along Pouncey Tract Road (State Route 271) must be approved by the Department of Transportation.

- A note needs to be included on the plans indicating: “A traffic signal exists at the intersection of 			 and 		           	. The contractor shall contact the Traffic Engineering Signal Shop at (804) 727-8303 with any questions pertaining to the signal. A Miss Utility ticket shall be called in to field locate traffic control equipment and cables at least 72 hours prior to beginning work on or adjacent to the right-of-way within 500 feet of the intersection. The contractor or developer will be responsible for the cost of repair or replacement of any damaged traffic control equipment.”

- A note needs to be included on the plans indicating: “If there are any Henrico County maintained signs within the construction limits along Twin Hickory Lake Drive and Pouncey Place that the contractor feels are in the way, please contact Traffic Engineering at (804) 727-8296 for removal and re-installation.”

- The developer is responsible for all costs associated with modifying any existing traffic signal adjacent to the site. Per proffer # 13f of rezoning case REZ2021-0000018 requires “A pedestrian crossing with appropriate signalization from the site crossing Twin Hickory Lake Drive from it’s intersection with Pouncey Tract Road.”

- A note needs to be included on the plans indicating: “The contractor is responsible for installing all stop signs, directional signs, and striping shown on the plans.”

- A note needs to be included on the plans indicating: “Coordinate in the field with Henrico County Traffic Engineering at 804-727-8282 regarding the striping and arrows on Twin Hickory Lake Drive before installation."

- Show proposed signs, striping and arrows on the plan for the widening of Twin Hickory Lake Drive. Provide dedicated striping and sign plan sheets that include:

  - All existing and proposed lines (types, colors, widths, and lengths [relative to road stationing]) and arrows.

  - Line type dimensions (i.e. “mini-skip” marking lengths and gaps)

  - Lane widths

  - A note specifying that all pavement markings in the public right-of-way shall be thermoplastic and have a minimum thickness of 90 mil.

  - A note stating: “Any pavement markings disturbed during construction shall be replaced by the developer. If one line of a double yellow centerline is disturbed, both lines shall be reinstalled”.

  - A sign legend specifying sign MUTCD ID, dimensions, and depiction of what the sign looks like.

- Provide evidence that VDOT has reviewed the current scope of work shown on the plan and has no comments regarding the proposed work.

- All roads intersecting another road shall do so at an angle of 90 degrees for a minimum distance of 75’ from the centerline of each roadway in all directions. "Road" shall mean public road, private road, multifamily access, and commercial access.

- Additional comments will follow upon review of a subsequent submittal.

ADDITIONAL PLAN COMMENTS:

General:

- Provide stationing along Twin Hickory Lake Drive.

- Provide cross-sections for all proposed road widening in 25’ intervals.

- Road mill & overlay must be provided for the existing through lane adjacent to the road widening on Twin Hickory Lake Drive. Provide VDOT standard WP-2 detail on the plans. Coordinate with VDOT regarding pavement requirements on Pouncey Tract Road.

- For widening of Twin Hickory Lake Drive, provide County Typical Section detail for a Class VII roadway among construction notes and details. Refer to sheet B-12 found in Appendix B of the County Design Manual (https://henrico.us/assets/DesignMannual_09.01.2021_AppendixB.pdf).

- At accesses onto the public roads, set stop bars to be “behind” curb ramps relative to intersecting public roadway. This is a recommendation for internal intersections as well.

- Provide VDOT standard CG-9D entrances at the accesses along Pouncey Place and Twin Hickory Place Drive. Add standard CG-9D detail to the plans.

Sheet C-301 (Overall Site Plan):

- Concerned about the motorists backing out of garage bays. Motorists will be unable to see down the drive aisles to determine where anyone is coming. Please revise.

- Provide VDOT standard CG-12 ramps within the splitter island proposed at the Pouncey Tract point of access.

- Clarify need for two points of access at Pouncey Place cul-de-sac. Though it’s a cul-de-sac I am concerned about multiple points of conflict created by three commercial driveways located so close to one another. Could an internal connection be made with the neighboring Townes at Pouncey Place development?

- Revise shown median break on Twin Hickory Lake Drive:

  - The western nose should be modified to better accommodate left turns from the site.

  - The eastern nose should be pulled back approximately 10’. Turn lane would need to be modified to maintain storage and taper lengths.

- Specify proposed VDOT median construction within revised Twin Hickory Lake Drive median. Coordinate with Public Works – Construction Division reviewer.

- With the introduction of the splitter island at the Pouncey Tract Road point of access, the center turn lane pavement markings will need to change. Coordinate with VDOT.

- Clarify sidewalk design along Pouncey Place.

- In the area by the dumpster enclosure located between “retail building #1” and “Building #1” concerned about cars parking within striped out area in front of dumpster enclosure. Consider providing raised island buffer(s) between enclosure access and parking spaces.

Sheet C-903 (Maintenance of Traffic):

- Clarify proposed use of shown Figure TTCs.

- Add following notes to maintenance of traffic plan:

  - Work hours within Twin Hickory Lake Drive & Pouncey Place are 9:00AM-3:30PM, Monday through Friday.

  - All lanes of traffic shall be open at the close of each day.

  - Except for emergencies, no lane closures or other traffic restrictions shall be erected during periods of inclement weather.

  - The Contractor shall coordinate all lane closures with Henrico Police/Fire (804-501-5000) and Pupil Transportation/ Schools (804-226-5570).

  - The Contractor is responsible for the maintenance of all signs and posts in the work zone.  This includes, but is not limited to, stop, yield, street name and speed limit signs.  Any sign or post damaged during construction or missing shall be replaced by the Contractor at his expense.

  - The Traffic Engineer (804-727-8282) reserves the right to modify the traffic control as necessary in the interests of public safety and/or convenience.

  - the contractor is responsible for the replacement of any pavement markings disturbed by construction.  the contractor is responsible for installing pavement markings on final pavement overlay within two (2) days of final overlay.  temporary pavement markings may be needed depending on the length of time.

  - The contractor shall replace missing pavement markings with thermoplastic pavement marking material (minimum thickness of 90 mil) during the installation of the final course of asphalt.  Thermoplastic pavement markings shall be reflectorized with glass beads.

  - Unless otherwise approved, no equipment or materials are to be left in the county right-of-way after work hours.  Should permission be given to allow equipment and materials in the right-of-way after work hours, group II channelizing devices (plastic barrels with prismatic sheeting) shall be used to delineator the obstacles.  Equipment and materials shall be placed in areas that would have no adverse impact to the property owners and shall not obstruct any sight distances or create any other safety issues.

  - All employees exposed to vehicular traffic shall be provided with and instructed to wear warning vests marked with or made of reflectorized or high visibility materials meeting Class III standards.

Should you have any questions, please let me know.

Thank you,

Brandon House, E.I.T.

Traffic Review Engineer

County of Henrico - Department of Public Works
P.O. Box 90775 Henrico, VA 23273-0775

804.501.4661 phone | 804.501.7470 fax

hou018@henrico.us | www.henrico.us/works/traffic/