# RECOMMENDATION TO PLANNING DIRECTOR:

The Traffic Engineering Section:

can recommend approval of this project to the Planning Director.

cannot recommend approval of this project to the Planning Director because:

- Various right-of-way dedications/revisions need to take place (comment #1)

- Road improvements along Yahley Mill Road are needed. Turn lane lengths on (relocated) Longbridge Road need to be increased/modified to meet current standards. (comment #1)

- A pedestrian connection (trail/sidewalk) needs to be made to connect the subdivision to the Capital Trail. (comment #18a)

- Given the widening of New Market Road, revisions to the existing Capital Trail along New Market Road will need to be shown and agreed upon by the VDOT. (comment #s 1 and 56)

- Longbridge Road’s existing alignment will need to be removed and shown on the plans (comment #51)

# ROAD IMPROVEMENT COMMENTS:

- Road improvements and/or right-of-way dedication is required.

Right-of-way dedication:

New Market Road: Coordinate with VDOT regarding the relocation of the Capital Trail away from widened New Market Road. Additional dedication may be necessary to accommodate road widening and relocated trail, pending VDOT review.

Longbridge Road: With what appears to be a shoulder and ditch section proposed, additional right-of-way dedication may be needed to accommodate turns lanes and a pedestrian facility (trail or sidewalk) to connect the subdivision back to the Capital Trail.

Yahley Mill Road: Dedicate to 44.5 feet from centerline of right-of-way for a right turn lane into the site. On sheet C0.1, note #9C, among turn lanes to be installed: A SOUTHBOUND RIGHT-TURN LANE ON YAHLEY MILL ROAD AT CASPIAN COURT needs to be provided and accommodated for on the site plan.

Fountain Grove Drive: No dedication. Right-of-way at intersections with private streets should not extend into the private roadways. Revise.

Cul-de-sac streets: For traditional cul-de-sacs, a 55’ R/W radius (with a 48’ pavement radius (to F/C)) is the current County standard. According to the associated plat submittal, a 50’ radius is proposed throughout.

Property/right-of-way lines at roadway intersections shall be a chord/tangent. The beginning and ending points of the right-of-way tangent are determined by measuring back from the right-of-way extended PI (point of intersection). The ends of the tangent line shall be minimum 25 feet from the right-of-way extended PI (in each direction) for residential streets and 30 feet for non-residential streets.

Road widening:

On (relocated) Longbridge Road: provide 8’ wide shoulders off edges of pavement (graded 12:1) and associated ditch work for adequate drainage. Extend turn lanes to meet current Henrico County standard dimensions (100’ long taper, 200’ of storage).

On Yahley Mill Road: widening, meeting Henrico County Class VI standards from centerline, is required for the two lots adjacent to Yahley Mill Road. Refer to Typical sheet B-9 found in Appendix B of the Public Works Design Manual. Consult with EESD engineer for curb and gutter requirements. Please note, the right-of-way dedication figure above (44.5’ from centerline) is based on a curb and gutter section with a right turn lane (road would be widened to 32’ from centerline to F/C). Turn lane to include 200’ of storage with a 100’ long taper. A pavement taper may be installed to tie widened road to existing road width.

Road widening to ... feet from centerline and a --- feet wide shoulder is required along .....................

Minimum improvements required, including 6’ stabilized shoulders and associated ditch

work for adequate drainage along ............................

- Show dimensions, right-of-way centerlines, curb return radii, and right-of-way widths of all roads (both sides) and intersections on the plans. As the plans progress, continue to provide right-of-way dimensions in same manner shown on revised plan sheets received by email on December 15, 2021.

- The minimum allowable centerline radii for curves is … feet along ... Centerline lengths shall be minimum 100’ long.

- All roads intersecting another road shall do so at an angle of 90 degrees for a minimum distance of 60 feet measured from the near edge of pavement/face of curb of the thru lane of the intersecting road in all directions. "Road" shall mean public road, private road, multifamily access, alley, and commercial access.

- The minimum access point spacing (measured from the near edge of pavement of existing road to centerline of new road) is … feet along….

# STANDARD PLAN COMMENTS:

- Provide the vehicle trips per weekday, AM peak hour weekday trip generation (enter/exit) and PM peak hour weekday trip generation (enter/exit) on the plan cover sheet. There is a newer POD cover sheet that needs to be used that is available at Engineering & Environmental Services - Henrico County, Virginia.

- Show the minimum queue length for drive thru lanes.

- Henrico County standard curb and gutter is required around all interior driveways and around all parking areas. Reference made to alley parking sections.

- Henrico County standard independent curb is required.

- Raised, landscaped islands with a minimum width of 9 feet are required at the ends of all rows of parking to separate parking areas from driveways.

- Label driveway widths, curb radii, and typical parking space dimensions on the plans.

- Curb radii adjacent to parking spaces need to be a minimum of 4.5 feet.

- There may be no more than 50 single-family lots on a single point of access.

- There may be no more than 82 multi-family units on a single point of access.

- Final grading details need to be shown to determine the need for guardrail or other accepted vehicular protection.

- MASH (Manual for Assessing Safety Hardware) standard guardrail and proper end treatments are required along public roadways where the appropriate clear zone is not provided. Refer to current VDOT GRIT (Guardrail Installation Training) Manual. The approximate locations of the guardrail and end treatments need to be shown on the plan within the right-of-way or an easement.

- In private developments, guardrail or other accepted vehicular protection is required along drive aisles, parking lots or internal private roads adjacent to a BMP, or where a 7.5 feet wide clear zone having a graded 6:1 or flatter shelf from face of curb or near edge of pavement is not provided. When there is a water hazard with a depth of 2 feet or more, the minimum clear zone increases to 10 feet.  The approximate locations of the guardrail or other accepted vehicular protection need to be shown on the plans.

- Per public works policy, a 5’ wide standard Henrico County sidewalk with a 4 feet wide utility strip (measured between the back of curb and near edge of sidewalk) is required on at least one side of Class I – IV roads. Sidewalk shall include a minimum 1’ shelf beyond the far edge of the sidewalk (from the public roadway).

  - A pedestrian connection (trail/sidewalk) needs to be made to connect the subdivision to the Capital Trail.

  - In addition to the road improvements in comment #1, install sidewalk and curb ramps along the lots adjacent to Yahley Mill Road

  - Since an amenity center is planned for the eastern corner of Fountain Grove Drive & Belcourt Park Drive, sidewalk should be installed on the eastern side of Fountain Grove Drive to connect to the nature trail and sidewalk along Belcourt Park Drive

  - Sidewalk along Fountain Grove Dr will need to continue to northern terminus of road.

  - Provide a sidewalk connection on the eastern side of Fountain Grove Dr to allow pedestrian connectivity to Block S lots (lots by Fountain Grove Place).

  - Provide a sidewalk connection to the nature trail end on Caspian Court.

- All sidewalks must be located within right-of-way. For road classes I-IV (standard 50’ right-of-way), a permanent easement will be needed in addition to the proposed right-of-way to incorporate the entire sidewalk plus a minimum 1’ shelf beyond the far edge of the sidewalk… The 55’ wide R/W rural roads (with curb and gutter) should move the sidewalk back toward the roadway, 4’ behind the back of curbing.

- Pedestrian passing areas are needed in sidewalk.

- Sidewalks that run along the end of parking spaces are required to be 5 feet wide exclusive of the width of curbing.

- Wheel stops are required in any proposed handicap parking spaces and any regular parking spaces adjacent to the ramps.  Provide handicap parking signs, R7-8, in front of handicap parking spaces. Comment made in anticipation of handicap parking spaces being added to the plans.

- The maximum length of road segment is 1320 feet.

- Show standard Henrico County end of road barricades. An end of road barricade is needed for the northern terminus of Fountain Grove Drive.

  - On sheet C7.0 (Henrico County standard Construction Notes), in the END OF ROAD BARRICADE detail:

    - Label the signs as OM4-2

    - Remove the remove the sentence “Reflectorized signs to be installed by the County”. This is an outdated note and out of practice.

- A standard R1-1 Stop Sign and 24 inch white stop bar are required at all points of egress from this development. Specify stop bar widths to be 24”. Add a stop bar at the Caspian Court approach to its intersection with Yahley Mill Road.

- Recommend standard R1-1 Stop Signs and 24 inch white stop at all internal intersections within the proposed development

- Provide and show the locations of the subdivision street name signs. The street name signs must meet the specifications in the Department of Public Works Design Manual (Section 2-38). Signs for public roads shall display a green background with white lettering while signs for private roads shall display a white background with black lettering.

- Provide and show the locations of the subdivision speed limit signs and Stop signs.

- Specify the proposed type of posts for subdivision street name signs, stop signs, speed limit signs, etc. in the public right-of-way.  If not using the standard green u-channel, square wood or square metal posts in the public right-of-way, provide a Henrico County Right-of-Way Maintenance Agreement prior to plan approval. Any non-standard sign post must be approved by the Traffic Engineer prior to plan approval.  Provide a catalog cut of any proposed non-standard sign post.

- Within subdivisions, “bump-outs” are required on public residential roadways with a speed limit of 25 mph or less. Bump-outs are curb extensions that reduce the travel lanes along a roadway. They are predominantly located at intersections to reduce pedestrian crossing distances but may be installed at a mid-block section of roadway. Bump-outs are also used as a traffic calming measure. Locations of bump-outs should be coordinated with Traffic Engineering. For an example of bump-outs, please see sheets B-4 and B-5 of Appendix B in the Public Works Design Manual.

  - In the interest of safety, and according to Section 19-3403 of the County Code of Ordinances: Traffic Engineering is looking for the installation of bump-outs in the following locations:

    - Intersection of Fountain Grove Drive & Kidiron Street (northern leg of intersection)...A sufficiently long lane shift would need to be provided where the boulevard entrance transitions to the bump-out. This may require cutting back the northern end of the median nose back and providing a taper of the road edge and median toward the middle of the road/right-of-way

    - Intersection of Fountain Grove Drive & Andalusian Way (southern leg of intersection)

    - Intersection of Fountain Grove Drive & Belcourt Park Drive (both north and south legs of intersection

        - VDOT standard CG-12 ramps need to be added for a crossing of the northern leg of the intersection

    - A mid-block crossing for the proposed nature trail connection to Fountain Grove Drive. Refer to comment #18c. This will be for the benefit of residents, trail users, and those interested in visiting the amenity center. CG-12 ramps will be needed.

    - Intersection of Fountain Grove Drive & Warriner Downs Drive (southern leg)

    - Intersection of Warriner Downs Drive & Caspian Court (western corner)

- No on-street parking will be permitted for this development on the adjacent public roads now or in the future.

- Provide intersection sight distance lines to scale on the plan for all access points onto the public right-of-way.  Provide a profile of the roadway along with the driver’s line of sight.  Show sight distance 14.5 feet from edge of travel lane (demonstrated with dimensions).  Adequate sight distance must be demonstrated prior to Public Works’ approval of this plan.

- Sight Distance easements will be required for the proposed access points where the sight distance line is outside the proposed right-of-way. All easements need to be shown and identified on the plans.

- Sight Distance lines and easements shall remain free of all structures, trees, shrubbery, and signs that are higher than 30” above the ground where the sight distance originates, except utility poles, fire hydrants, and traffic control signs.

- A minimum of 30 feet to the first point of conflict is required at the proposed entrances from a public street.

- All two-way drive aisles need to be a minimum of 24 feet wide and a maximum of 30 feet wide.  Call out the dimensions on the plans.

- All one-way drive aisles need to be a minimum of 18 feet wide.  Henrico County Division of Fire may require 20 feet.

- Dedicated turn around spaces with adequate back-out room are required in any dead end of rows of parking. Label the striped out turn around space and NO PARKING sign on the plan. Reference made to the dead-end parking lot at the northern corner of Orchard Cottage Loop.

- Bollards are needed for vehicular protection for any proposed doors that swing into the proposed drive aisles around the proposed building.  Details for the bollards need to be shown on the plans.

- Show truck movements on the plan.

- Provide a maintenance of traffic plan for all work proposed in the public right-of-way.

- Improvements along New Market Road (State Route 5) must be approved by the Department of Transportation.

- A note needs to be included on the plans indicating: “A traffic signal exists at the intersection of 			 and 		           	. The contractor shall contact the Traffic Engineering Signal Shop at (804) 727-8303 with any questions pertaining to the signal. A Miss Utility ticket shall be called in to field locate traffic control equipment and cables at least 72 hours prior to beginning work on or adjacent to the right-of-way within 500 feet of the intersection. The contractor or developer will be responsible for the cost of repair or replacement of any damaged traffic control equipment.”

- A note needs to be included on the plans indicating: “If there are any Henrico County maintained signs within the construction limits that the contractor feels are in the way, please contact Traffic Engineering at (804) 727-8296 for removal and re-installation.”

- The developer is responsible for all costs associated with modifying any existing traffic signal adjacent to the site.

- A note needs to be included on the plans indicating: “The contractor is responsible for installing all stop signs, directional signs, and striping shown on the plans.”

- A note needs to be included on the plans indicating: “Coordinate in the field with Henrico County Traffic Engineering at 804-727-8282 regarding the striping and arrows on Longbridge Road, Fountain Grove Drive, and Yahley Mill Road before installation."

- Show proposed traffic signs, striping, and arrows on the plan for the road improvements where applicable. Provide a dedicated pavement marking and traffic sign plan. Details to include:

  - Details of MUTCD standard signs (MUTCD ID, depiction, and dimensions)

  - Within sheet(s), clearly depict and call out

    - All existing and proposed lines (types, colors, widths, and lengths [relative to road stationing]) and arrows.

    - Line type dimensions (as necessary) (i.e. mini skips)

    - Lane widths (both existing and proposed)

    - Striped turn lane lengths

  - Provide a note specifying that all pavement markings in the public right-of-way shall be thermoplastic and have a minimum thickness of 90 mil

  - Provide a note stating: “Any pavement markings disturbed during construction shall be replaced by the developer. If one line of a double yellow centerline is disturbed, both lines shall be reinstalled”.

- Provide evidence that VDOT has reviewed the current scope of work shown on the plan and has no comments regarding the proposed work.

- Additional comments will follow upon review of a subsequent submittal.

ADDITIONAL PLAN COMMENTS:

General:

- The existing Longbridge Road connection to both New Market Road and the alignment east of the project limits shall not remain “as is”. The referenced segment of Longbridge Road will need to be removed.

- On sheet C7.1, typical road section details need to be provided for (relocated) Longbridge Road and the widening of New Market Road.

- To separate private and public roads, CG-9D aprons should be installed at the public connections to private streets.

- There are several “stop conflicts” with the pedestrian crossings throughout this development. In these situations, especially at public road intersections, curb ramps need to be brought closer to the intersection and reside between the stop condition and intersecting roadway. Ramps need to remain “directional”, oriented parallel with the intersecting roadway.

- Provide the locations of speed limit sign(s) on Longbridge Road.

- On many of the 32’ wide, private streets, parking needs to be restricted on one side of the road to maintain sufficient room for 2-way traffic. Please provide NO PARKING signs to enforce this.

Sheet C3.1 (Site & Buildable Area Plan):

- With New Market Road shown to encroach the Capital Trail’s existing location, coordinate with VDOT regarding the trail’s relocation and revised crossing of New Market Road. Will it remain in place or need to be relocated? Details of revised trail crossing are subject to VDOT review and approval.

  - The maintenance of traffic plan will need to consider the trail construction and should provide a means to maintain access to it.

- At the intersections of New Market Rd & (relocated) Longbridge Road AND (relocated) Longbridge Road and Fountain Grove Drive, please provide a W1-7 (double arrow) sign.

Sheet C3.2 (Site & Buildable Area Plan):

- CG-12 ramps need to be “directionally” oriented, to send pedestrians in a straight path from one ramp to the next.

- Label widened right-of-way width of Fountain Grove Drive by its intersection with (relocated) Longbridge Road.

Sheet C3.3 (Site & Buildable Area Plan):

- Recommend providing ramps and a sidewalk connection to the neighborhood park on Sweeney Mill Lane.

Sheet C3.4 (Site & Buildable Area Plan):

- For the one-way alleys, provide MUTCD standard DO NOT ENTER signs at the egress of the drive aisles.

Sheet C3.6 (Site & Buildable Area Plan):

- Recommend providing additional pedestrian (sidewalk and ramp) connections to the neighborhood park on Bassett Hall Place beyond that proposed off Kidiron Street.

Sheet C3.7 (Site & Buildable Area Plan):

- Concerned about the alley intersection proposed in the bottom left corner of the sheet. The intersection angle is so acute and creates a lot of conflict for motorists entering from Andalusian Way. Highly recommend construction a single drive aisle connection from Andalusian Way and creating a T-intersection between the intersecting roads with a stop condition on the “stem” of T.

- Why are Belcourt Park Drive and Andalusian Way slightly shifted in alignment across Fountain Grove Drive? Revise to keep streets in continuous alignment.

- Consider flipping stop conditions at intersection of Andalusian Way & Belcourt Park Drive (since Andalusian Way is expected to carry more traffic)

Sheet C3.11 (Site & Buildable Area Plan):

- At intersection of Yahley Mill Road & Caspian Court, increase curb return radii to 35’.

Please let me know if you have any questions.

Thanks,

Brandon House, E.I.T.

Traffic Review Engineer

County of Henrico - Department of Public Works
P.O. Box 90775 Henrico, VA 23273-0775

804.501.4661 phone | 804.501.7470 fax

hou018@henrico.us | www.henrico.us/works/traffic/