# ROAD IMPROVEMENT COMMENTS:

- Road improvements and/or right-of-way dedication is required. Chord rights-of-way take at intersection of Nine Mile Rd and E Cedar Fork Rd…Set chord to be 30’ from the right-of-way extended point of intersection. Dedication should be made directly to the Commonwealth of Virginia (VDOT).

Existing sidewalk along Nine Mile Rd is outside of right-of-way (as shown on sheets 2 & 3). Since Nine Mile Road is a VDOT right-of-way, confirm with VDOT whether right-of-way must be dedicated to cover existing sidewalk.

Right-of-way dedication to ... feet from centerline of right-of-way is required for property frontage along ...

Road widening with Henrico County curb & gutter to ... feet from centerline is required along ...

Road widening to ... feet from centerline and a --- feet wide shoulder is required along .....................

Minimum improvements required, including 4’ stabilized shoulders and associated ditch

work for adequate drainage along ............................

- Show dimensions, right-of-way centerlines, curb return radii, and right-of-way widths of all roads (both sides) and intersections on the plans.

- The minimum allowable centerline radii for curves is … feet along ...

- The minimum access point spacing is … feet along …

# STANDARD PLAN COMMENTS:

- Provide the vehicle trips per weekday, AM peak hour weekday trip generation (enter/exit) and PM peak hour weekday trip generation (enter/exit) on the plan cover sheet. There is a newer POD cover sheet that needs to be used that is available at http://henrico.us/works/design/.

- Show the minimum queue length for drive thru lanes. Please see “Drive-thru lanes” section of Henrico County Traffic Engineering policies at https://henrico.us/works/traffic/traffic-engineering-policies/. A length dimension still needs to be shown. Queue length must be minimum 100’.

- Henrico County standard curb and gutter is required around all interior driveways and around all parking areas.

- Henrico County standard independent curb is required.

- Raised, landscaped islands with a minimum width of 9 feet are required at the ends of all rows of parking to separate parking areas from driveways. (3/23/22): Consider placing one between the dumpster enclosure and the nearest parking space. Coordinate with Planning otherwise.

  - On sheet 4 of 28, under “LAYOUT GENERAL NOTES”: recommend removing note #11 as it almost never applies here.

  - The face of curbing for the raised islands will need to span the full width of the parking space to offer full protection. The face of curbing for the islands should also be in line with the edge of the sidewalk/building. Two-way drive aisles need to remain at 24’ in width.

- Label driveway widths, curb radii, and typical parking space dimensions on the plans.

- Curb radii adjacent to parking spaces need to be a minimum of 4.5 feet.

- There may be no more than 50 single-family lots on a single point of access.

- There may be no more than 82 multi-family units on a single point of access.

- Final grading details need to be shown in order to determine the need for guardrail or other accepted vehicular protection.

- Guardrail and proper end treatments are required along public roadways where the appropriate clear zone is not provided.  The approximate locations of the guardrail and end treatments need to be shown on the plan within the right-of-way or an easement.

- In private developments, guardrail or other accepted vehicular protection is required along drive aisles, parking lots or internal private roads adjacent to a BMP, or where a 7.5 feet wide clear zone having a graded 6:1 or flatter shelf from face of curb or near edge of pavement is not provided. When there is a water hazard with a depth of 2 feet or more, the minimum clear zone increases to 10 feet.  The approximate locations of the guardrail or other accepted vehicular protection need to be shown on the plans.

- Per Public Works policy, a standard Henrico County sidewalk with a 2 feet wide utility strip is required along ……………. for the entire frontage of the property.

- All sidewalks must be located within right-of-way. Refer to comment #1, above.

- Pedestrian passing areas are needed in sidewalk.

- Sidewalks that run along the end of parking spaces are required to be 5 feet wide (as measured from the back of curb). Label proposed sidewalk width.

- Wheel stops are required in any proposed handicap parking spaces and any regular parking spaces adjacent to the ramps.  Provide handicap parking signs, R7-8, in front of handicap parking spaces. Label R7-8 on “Proposed Geometric Plan”.

  - Clarify whether wheel stop or bollard be used for sign protection. Both can be provided, but only one form of sign protection is necessary. (3/23/22): Show both bollard and wheel stop on the plans for clarity.

- The maximum length of road segment is 1320 feet.

- Show standard Henrico County end of road barricades.

- A standard R1-1 Stop Sign and 24 inch white stop bar are required at all points of egress from this development.

- Recommend standard R1-1 Stop Sign and 24 inch white stop at all internal intersections within the proposed development.

- Provide and show the locations of the subdivision street name signs.  The street name signs must meet the specifications in the Department of Public Works Design Manual.

- Provide and show the locations of the subdivision speed limit signs and Stop signs.

- Specify the proposed type of posts for subdivision street name signs, stop signs, speed limit signs, etc. in the public right-of-way.  If not using the standard green u-channel, square wood or square metal posts in the public right-of-way, provide a Henrico County Right-of-Way Maintenance Agreement prior to plan approval. Any non-standard sign post must be approved by the Traffic Engineer prior to plan approval.  Provide a catalog cut of any proposed non-standard sign post.

- Within subdivisions, bump-outs are required on public residential roadways with a speed limit of 25 mph or less. Bump-outs are curb extensions that reduce the travel lanes along a roadway. They are predominantly located at intersections to reduce pedestrian crossing distances but may be installed at a mid-block section of roadway. Bump-outs are also used as a traffic calming measure. Locations of bump-outs should be coordinated with Traffic Engineering. Traffic Engineering will provide an example of bump-outs upon request.

- No on-street parking will be permitted for this development on the adjacent public roads now or in the future.

- From the southbound approach to the intersection of E Cedar Fork Road & Nine Mile Road, provide intersection sight distance looking left from the right turn lane. Need to confirm sight distance looking left will not be obstructed by proposed landscaping by Nine Mile Road. Adequate sight distance must be demonstrated prior to Public Works’ approval of this plan.

- Sight Distance easements will be required for the proposed access points where the sight distance line is outside the proposed right-of-way. All easements need to be shown and identified on the plans.

- Sight Distance easements shall remain free of all structures, trees, shrubbery, and signs that are higher than 30” above the ground where the sight distance originates, except utility poles, fire hydrants, and traffic control signs.

- A minimum of 30 feet to the first point of conflict is required at the proposed entrances from a public street.

- All two-way drive aisles need to be a minimum of 24 feet wide and a maximum of 30 feet wide. Clarify if/how two-way traffic is to navigate between car wash line and proposed pump nearest to line. This is under the assumption that vehicles are in the car wash queue with another vehicle at the pump. (3/19/21): How would the car wash enforce a limit of two cars in the queuing lane at once? A minimum 100’ queue length must be provided per comment #6 above.

- All one-way drive aisles need to be a minimum of 18 feet wide.  Henrico County Division of Fire may require 20 feet.

- Dedicated turn around spaces with adequate back-out room are required in any dead end of rows of parking.  Label the striped out turn around space on the plan.

- Bollards are needed for vehicular protection for any proposed doors that swing into the proposed drive aisles around the proposed building.  Details for the bollards need to be shown on the plans. Please provide bollard for door on south side of building and for dumpster enclosure (for door that swings toward the car wash egress).

- Show truck movements on the plan. (3/19/21): Specify design vehicle used for truck movements. Is this indicative of the size of tanker trucks that will routinely come to refill the underground storage tanks?... Clarify movements for a trash truck entering the site, accessing the dumpster enclosure, and exiting the site.

- Provide a maintenance of traffic plan for all work proposed in the public right-of-way.

- Improvements along ... (State Route ...) must be approved by the Department of Transportation.

- A note needs to be included on the plans indicating: “A traffic signal exists at the intersection of E Cedar Fork Rd and Nine Mile Rd. The contractor shall contact the Traffic Engineering Signal Shop at (804) 727-8303 with any questions pertaining to the signal. A Miss Utility ticket shall be called in to field locate traffic control equipment and cables at least 72 hours prior to beginning work on or adjacent to the right-of-way within 500 feet of the intersection. The contractor or developer will be responsible for the cost of repair or replacement of any damaged traffic control equipment.”

- A note needs to be included on the plans indicating: “If there are any Henrico County maintained signs within the construction limits that the contractor feels are in the way, please contact Traffic Engineering at (804) 727-8296 for removal and re-installation.”

- The developer is responsible for all costs associated with modifying any existing traffic signal adjacent to the site. This signal is maintained by the Virginia Department of Transportation.

- A note needs to be included on the plans indicating: “The contractor is responsible for installing all stop signs, directional signs, and striping shown on the plans.”

- A note needs to be included on the plans indicating: “Coordinate in the field with Henrico County Traffic Engineering at 804-727-8282 regarding the striping and arrows on 		  before installation."

- Show proposed striping and arrows on the plan for the widening of 		           	.

- Provide evidence that VDOT has reviewed the current scope of work shown on the plan and has no comments regarding the proposed work.

- All roads intersecting another road shall do so at an angle of 90 degrees for a minimum distance of 75’ from the centerline of each roadway in all directions. "Road" shall mean public road, private road, multifamily access, and commercial access.

- Additional comments may follow upon review of a subsequent submittal.

ADDITIONAL PLAN COMMENTS:

Sheet 4 of 28 (Proposed Geometric Plan):

- At intersection of Cedar Fork Rd and private drive aisle, update existing sidewalk connection to CG-9D (at property corner) to meet current ADA standards. (3/23/22): Clarify that this work will be done.

- In “Construction General Notes”, note #8: please label location of DO NOT ENTER signs on plans. (3/23/22): A DO NOT ENTER sign needs to be provided for the egress of the one-way drive aisle adjacent to the car wash building. Recommend installing a 24” wide, solid white bar (spanning will drive aisle width) to accompany DO NOT ENTER sign(s).

- For the entrance further from E Cedar Fork Road, a stop sign will need to be added for the northern leg’s approach to the now 4-way intersection. Remove the stop sign proposed for the westbound approach to the intersection.

- Highly recommend outlining car wash queuing lane with single solid white lines to outline drive thru lane from rest of one-way drive aisle. Drive thru lanes shall be minimum 10’ wide with a 12’ wide bypass available.

- Update annotations to reference relevant sheets. (Ex. “HC PARKING SEE DETAILS SHEET 14” are now found on sheet 15.)

Sheet 16 of 31 (Miscellaneous Details):

- Why are VDOT standard curb and gutter details on this sheet? The plan appears to only propose Henrico County standard curb and gutter.

Sheet 27 of 28 (Truck Turning Movement):

- Concerned about truck movements. As shown, the WB-50 truck would have to drive through a couple of parking spaces and drive the wrong way down a one-way drive aisle.

- Can a tanker truck (WB-50) make a right turn from E Cedar Fork Rd into the shopping center and site?

Please let me know if you have any questions.

Thanks,

Brandon House, E.I.T.

Traffic Review Engineer

County of Henrico - Department of Public Works
P.O. Box 90775 Henrico, VA 23273-0775

804.501.4661 phone | 804.501.7470 fax

hou018@henrico.us | www.henrico.us/works/traffic/