# RECOMMENDATION TO PLANNING DIRECTOR:

The Traffic Engineering Section:

can recommend approval of this project to the Planning Director.

cannot recommend approval of this project to the Planning Director because:

- Additional road widening is needed along Scott Road (Comment #1)

- Upon receipt of the County’s Draft Bike plan, a shared use path is projected along Scott Road. Additional R/W dedication/easements appear to be needed (comment #51)

# ROAD IMPROVEMENT COMMENTS:

- Road improvements and/or right-of-way dedication is required.

Right-of-way dedication to 25 feet from centerline of right-of-way is required for property frontage along Scott Road/Athens Avenue.

Property/right-of-way lines at roadway intersections shall be a chord/tangent. The beginning and ending points of the right-of-way tangent are determined by measuring back from the right-of-way extended PI (point of intersection). The ends of the tangent line shall be minimum 25 feet from the right-of-way extended PI (in each direction) for residential streets and 30 feet for non-residential streets. Reference made to the intersection corner of Scott Rd/Athens Ave & Aberdeen St.

Road widening with Henrico County curb & gutter to 18 feet from centerline is required along Scott Road. The road’s pavement design shall meet Class V standards see (see sheet B-6 in Appendix B of the current public works design manual https://henrico.us/pdfs/works/design/designmanual/2021_DesignManual_AppendixB.pdf). Widening should extend along full Scott Road property frontage.

Road widening to ... feet from centerline and a --- feet wide shoulder is required along .....................

Minimum improvements required, including 6’ stabilized shoulders and associated ditch

work for adequate drainage along ............................

- Show dimensions, right-of-way centerlines, curb return radii, and right-of-way widths of all roads (both sides) and intersections on the plans… The minimum allowable curb return radius for a commercial entrance is 15’. Clarify radii for proposed accesses.

- The minimum allowable centerline radii for curves (superelevated) is 371 feet along 35 MPH Scott Road. Centerline lengths shall be minimum 100’ long.

- All roads intersecting another road shall do so at an angle of 90 degrees for a minimum distance of 60 feet measured from the near edge of pavement/face of curb of the thru lane of the intersecting road in all directions. "Road" shall mean public road, private road, multifamily access, alley, and commercial access.

- The minimum access point spacing (measured from the near edge of pavement of existing road to centerline of new road) is … feet along….

# STANDARD PLAN COMMENTS:

- Provide the vehicle trips per weekday, AM peak hour weekday trip generation (enter/exit) and PM peak hour weekday trip generation (enter/exit) on the plan cover sheet. There is a newer POD cover sheet that needs to be used that is available at Engineering & Environmental Services - Henrico County, Virginia.

- Show the minimum queue length for drive thru lanes.

- Henrico County standard curb and gutter is required around all interior driveways and around all parking areas. Label where proposed.

- Henrico County standard independent curb is required. Label where proposed.

- Raised, landscaped islands with a minimum width of 9 feet are required at the ends of all rows of parking to separate parking areas from driveways.

- Label driveway widths, curb radii, and typical parking space dimensions on the plans.

- Curb radii adjacent to parking spaces need to be a minimum of 4.5 feet.

- There may be no more than 50 single-family lots on a single point of access.

- There may be no more than 82 multi-family units on a single point of access.

- Final grading details need to be shown in order to determine the need for guardrail or other accepted vehicular protection. Reference made to comment #1, regarding additional widening along Scott Road.

- MASH (Manual for Assessing Safety Hardware) standard guardrail and proper end treatments are required along public roadways where the appropriate clear zone is not provided. Refer to current VDOT GRIT (Guardrail Installation Training) Manual. The approximate locations of the guardrail and end treatments need to be shown on the plan within the right-of-way or an easement.

- In private developments, guardrail or other accepted vehicular protection is required along drive aisles, parking lots or internal private roads adjacent to a BMP, or where a 7.5 feet wide clear zone having a graded 6:1 or flatter shelf from face of curb or near edge of pavement is not provided. When there is a water hazard with a depth of 2 feet or more, the minimum clear zone increases to 10 feet.  The approximate locations of the guardrail or other accepted vehicular protection need to be shown on the plans.

- Per Public Works policy, a 5’ wide standard Henrico County sidewalk with a 4 feet wide utility strip (measured between the back of curb and near edge of sidewalk) is required along Scott Road for the entire frontage of the property. Sidewalk shall include a minimum 1’ shelf beyond the far edge of the sidewalk (from the public roadway).

- All sidewalks must be located within right-of-way. For road classes I-IV, a permanent easement will be needed in addition to the proposed right-of-way to incorporate the entire sidewalk plus a minimum 1’ shelf beyond the far edge of the sidewalk.

- Pedestrian passing areas are needed in sidewalk.

- Sidewalks that run along the end of parking spaces are required to be 5 feet wide exclusive of the width of curbing.

- Wheel stops are required in any proposed handicap parking spaces and any regular parking spaces adjacent to the ramps.  Provide handicap parking signs, R7-8, in front of handicap parking spaces

- The maximum length of road segment is 1320 feet.

- Show standard Henrico County end of road barricades.

- A standard R1-1 Stop Sign and 24 inch white stop bar are required at all points of egress from this development.

- Recommend standard R1-1 Stop Signs and 24 inch white stop bar at all internal intersections within the proposed development

- Provide and show the locations of the subdivision street name signs. The street name signs must meet the specifications in the Department of Public Works Design Manual (Section 2-38). Signs for public roads shall display a green background with white lettering while signs for private roads shall display a white background with black lettering.

- Provide and show the locations of the subdivision speed limit signs and Stop signs.

- Specify the proposed type of posts for subdivision street name signs, stop signs, speed limit signs, etc. in the public right-of-way.  If not using the standard green u-channel, square wood or square metal posts in the public right-of-way, provide a Henrico County Right-of-Way Maintenance Agreement prior to plan approval. Any non-standard sign post must be approved by the Traffic Engineer prior to plan approval.  Provide a catalog cut of any proposed non-standard sign post.

- Within subdivisions, bump-outs are required on public residential roadways with a speed limit of 25 mph or less. Bump-outs are curb extensions that reduce the travel lanes along a roadway. They are predominantly located at intersections to reduce pedestrian crossing distances but may be installed at a mid-block section of roadway. Bump-outs are also used as a traffic calming measure. Locations of bump-outs should be coordinated with Traffic Engineering. For an example of bump-outs, please see sheets B-4 and B-5 of Appendix B in the Public Works Design Manual.

- No on-street parking will be permitted for this development on the adjacent public roads now or in the future.

- Provide intersection sight distance lines to scale on the plan for all access points onto the public right-of-way.  Provide a profile of the line of sight.  Show sight distance 14.5 feet (dimensioned on the plans) from edge of travel lane. Adequate sight distance must be demonstrated prior to Public Works’ approval of this plan.

  - Intersection sight distance looking onto Scott Road shall be minimum 400’ long looking both left and right from each point of access

- Sight Distance easements will be required for the proposed access points where the sight distance line is outside the proposed right-of-way. All easements need to be shown and identified on the plans.

- Sight Distance lines and easements shall remain free of all structures, trees, shrubbery, and signs that are higher than 30” above the ground where the sight distance originates, except utility poles, fire hydrants, and traffic control signs.

- A minimum of 30 feet to the first point of conflict is required at the proposed entrances from a public street.

- All two-way drive aisles need to be a minimum of 24 feet wide and a maximum of 30 feet wide.  Call out the dimensions on the plans.

- All one-way drive aisles need to be a minimum of 18 feet wide.  Henrico County Division of Fire may require 20 feet.

- Dedicated turn around spaces with adequate back-out room are required in any dead end of rows of parking.  Label the striped out turn around space and MUTCD standard NO PARKING sign on the plan.

- Bollards are needed for vehicular protection for any proposed doors that swing into the proposed drive aisles around the proposed building.  Details for the bollards need to be shown on the plans.

- Show truck movements on the plan.

- Provide a maintenance of traffic plan for all work proposed in the public right-of-way…Currently the MOT plan on sheet C35 only includes TTC-4.2 for the widening of Scott Road. MOT plan will need to consider the Waterline, Sanitary sewer, and storm sewer work proposed to cross Scott Road. MOT will also need to consider work on Aberdeen Street and at the intersection of Aberdeen Street & Athens Avenue

- Improvements along ... (State Route ...) must be approved by the Department of Transportation.

- A note needs to be included on the plans indicating: “A traffic signal exists at the intersection of 			 and 		           	. The contractor shall contact the Traffic Engineering Signal Shop at (804) 727-8303 with any questions pertaining to the signal. A Miss Utility ticket shall be called in to field locate traffic control equipment and cables at least 72 hours prior to beginning work on or adjacent to the right-of-way within 500 feet of the intersection. The contractor or developer will be responsible for the cost of repair or replacement of any damaged traffic control equipment.”

- A note needs to be included on the plans indicating: “If there are any Henrico County maintained signs within the construction limits that the contractor feels are in the way, please contact Traffic Engineering at (804) 727-8296 for removal and re-installation.”

- The developer is responsible for all costs associated with modifying any existing traffic signal adjacent to the site.

- A note needs to be included on the plans indicating: “The contractor is responsible for installing all stop signs, directional signs, and striping shown on the plans.”

- A note needs to be included on the plans indicating: “Coordinate in the field with Henrico County Traffic Engineering at 804-727-8282 regarding the signs, striping and arrows on Scott Road before installation."

- Show proposed signs, striping and arrows on the plan for the widening of Scott Road, as applicable.

- Provide evidence that VDOT has reviewed the current scope of work shown on the plan and has no comments regarding the proposed work.

- Additional comments will follow upon review of a subsequent submittal.

ADDITIONAL PLAN COMMENTS:

General:

- According to the DPW’s recently released Draft Bike plan for the County’s 2045 Comprehensive Plan (https://www.henriconext.us/), a shared use path is currently proposed along Scott Road. This path would lead west to the future Fall Line Trail. Please revise sidewalk and install a shared use path according to sheet B-8 found in appendix B of the DPW design manual (https://henrico.us/pdfs/works/design/designmanual/2021_DesignManual_AppendixB.pdf). It appears the path can fit within a majority of the existing right-of-way frontage.

  - Between Scott Road/Athens Avenue’s intersections with Aberdeen Street & (private) Magnolia Terrace Lane, additional right-of-way dedication or easement would need to be dedicated to accommodate the path.

- A VDOT standard CG-9D apron needs to be provided at all private connections to public roads. For each CG-9D, detectable warning surfaces will need to be provided where the sidewalk and traversable slope of the apron meet.

- Provide cross-sections for the widening of Scott Road/Athens Avenue in 25’ intervals.

- Note: The horizontal curve along Scott Road/Athens Avenue should be superelevated at 4%.

Sheet C2 (Existing Conditions and Demolition Plan):

- Per the annotation “Relocate ex. right turn sign” in front of the house at 1000 Scott Road, please clarify where this sign would be relocated… I believe the existing signs are a W1-2r (curve) and W13-1 (advisory speed sign).

Sheet C3 (Overall Plan):

- Clarify if Section 4 will provide access to GPIN: 786-759-0210, abutting I-95 R/W.

Sheet C8 (Layout & Utility Plan [West]):

- Provide a directional VDOT CG-12 ramp at the intersection corner of Aberdeen St & Athens Ave (crossing Aberdeen St).

- For lot 33, place driveway as far as possible from intersecting Scott Road.

Sheet C33 (Site Details):

- In typical section details, revise dimensions to show road to be 36’ wide. Update Scott Road section per comment #51.

  - Clarify if Class V Road section also applies for the short span of widening along Aberdeen Street.

Sheet C35 (Site Details):

- Add following notes to “MAINTENANCE OF TRAFFIC” Notes:

  - Work hours along Scott Road/Athens Avenue shall be 8:00AM-4:30PM, Monday-Friday.

  - The contractor shall be responsible for maintaining access to all affected property owners within the work zone limits.

  - The Contractor is responsible for all notifications made to affected property owners.

  - The Contractor shall coordinate all lane closures with Henrico Police/Fire (501-5000) and Pupil Transportation/ Schools (226-5570).

Please let me know if you have any questions.

Thank you,

Brandon House, E.I.T.

Traffic Review Engineer

County of Henrico - Department of Public Works
P.O. Box 90775 Henrico, VA 23273-0775

804.501.4661 phone | 804.501.7470 fax

hou018@henrico.us | www.henrico.us/works/traffic/