The Department of Public Works has completed its review of the above referenced project and has the following comments:

- Trees and/or shrubs cannot be planted in any County maintained drainage easement. Shrubs in the drainage easement between structure 105 and 104 must be moved out of the drainage easement

- No plantings above 30 inches in height above the curb line are allowed in the public right-of-way.

- A maintenance agreement must be provided from the developer to the County for any plantings, irrigation work, lighting work, etc. located in the right-of-way.

- Henrico County is not liable or responsible for any damage or destruction of plantings, lighting, irrigation systems, etc. in the right-of-way or public easement resulting from maintenance of the drainage systems, right-of-way, and/or roadway.

- Provide underdrains along the rear of the curb and gutter any public right-of-way or in any islands/medians in the public right-of-way if an irrigation system is proposed.

- Provide sight distance information at all entrances and intersections.  Please show sight distance lines on sheet L8.0

- Lighting poles/fixtures are not permitted over any storm sewer (public or private) or in public drainage easements.

- Trees/shrubs cannot be planted below the water quality volume elevation in the BMP.

- Trees/shrubs cannot be planted on the fill section of any dams.

- Mulch cannot be placed below the water quality volume elevation in the BMP.

- Plantings, lighting poles/fixtures, and/or fences around BMPs must be placed so that access is not blocked to any inlet/outlet structures.

- NO COMMENTS

ADDITIONAL COMMENTS:

Reviewed by:	Alex Gruendl / gru018@henrico.us / 804-501-4033

Date:	23 May 2022