# PLANNING COMMISSION RECOMMENDATION:

The Traffic Engineering Section:

can recommend approval of this project to the Planning Commission.

cannot recommend approval of this project to the Planning Commission because:

- The modifications to the ring road need to consider bike accommodations (comment #51)

- Dedicated on-street parking shall not obstruct sight distance (comment #34)

# ROAD IMPROVEMENT COMMENTS:

- Road improvements and/or right-of-way dedication is required.

Right-of-way dedication to outline the limits of the adjacent ring-road section is required. Dedication will need to be called out on the plans. Dedication should match area shown in email exhibit (of sheet C2.3) received on October 11, 2021.

Property/right-of-way lines at roadway intersections shall be a chord/tangent. The beginning and ending points of the right-of-way tangent are determined by measuring back from the right-of-way extended PI (point of intersection). The ends of the tangent line shall be minimum 25 feet from the right-of-way extended PI (in each direction) for residential streets and 30 feet for non-residential streets.

Road widening with Henrico County curb & gutter to ... feet from centerline is required along ...

Road widening to ... feet from centerline and a --- feet wide shoulder is required along .....................

Minimum improvements required, including 6’ stabilized shoulders and associated ditch

work for adequate drainage along ............................

- Show dimensions, right-of-way centerlines, curb return radii, and right-of-way widths of all roads (both sides) and intersections on the plans. Show dimensions on the plans according to email exhibit received on October 11, 2021.

- The minimum allowable centerline radii for curves is … feet along ... Centerline lengths shall be minimum 100’ long.

- All roads intersecting another road shall do so at an angle of 90 degrees for a minimum distance of 60 feet measured from the near edge of pavement/face of curb of the thru lane of the intersecting road in all directions. "Road" shall mean public road, private road, multifamily access, alley, and commercial access.

- The minimum access point spacing (measured from the near edge of pavement of existing road to centerline of new road) is … feet along….

# STANDARD PLAN COMMENTS:

- Provide the vehicle trips per weekday, AM peak hour weekday trip generation (enter/exit) and PM peak hour weekday trip generation (enter/exit) on the plan cover sheet. There is a newer POD cover sheet that needs to be used that is available at http://henrico.us/works/design/.

- Show the minimum queue length for drive thru lanes.

- Henrico County standard curb and gutter is required around all interior driveways and around all parking areas.

- Henrico County standard independent curb is required.

- Raised, landscaped islands with a minimum width of 9 feet are required at the ends of all rows of parking to separate parking areas from driveways.

- Label driveway widths, curb radii, and typical parking space dimensions on the plans.

- Curb radii adjacent to parking spaces need to be a minimum of 4.5 feet.

- There may be no more than 50 single-family lots on a single point of access.

- There may be no more than 82 multi-family units on a single point of access.

- Final grading details need to be shown in order to determine the need for guardrail or other accepted vehicular protection.

- MASH (Manual for Assessing Safety Hardware) standard guardrail and proper end treatments are required along public roadways where the appropriate clear zone is not provided. Refer to current VDOT GRIT (Guardrail Installation Training) Manual. The approximate locations of the guardrail and end treatments need to be shown on the plan within the right-of-way or an easement.

- In private developments, guardrail or other accepted vehicular protection is required along drive aisles, parking lots or internal private roads adjacent to a BMP, or where a 7.5 feet wide clear zone having a graded 6:1 or flatter shelf from face of curb or near edge of pavement is not provided. When there is a water hazard with a depth of 2 feet or more, the minimum clear zone increases to 10 feet.  The approximate locations of the guardrail or other accepted vehicular protection need to be shown on the plans.

- Per Public Works policy, a Henrico County sidewalk with a 4 feet wide utility strip (measured between the back of curb and near edge of sidewalk) is required along the Virginia Center Commons Ring Road for the entire frontage of the property. Sidewalk shall include a minimum 1’ shelf beyond the far edge of the sidewalk (from the roadway) …Per sheet C2.2, carry sidewalk to western property limits. Please also carry sidewalk across PARCEL C frontage. Provide CG-12 ramps where needed.

- All sidewalks must be located within right-of-way or a permanent easement. Easement should be specified as a “pedestrian access” easement. Easement shall encompass the entire sidewalk plus a minimum 1’ shelf beyond the far edge of the sidewalk… In this circumstance, the property owner should be responsible for the maintenance of the sidewalk, lighting, and landscaping proposed along the ring road.

- Pedestrian passing areas are needed in sidewalk.

- Sidewalks that run along the end of parking spaces are required to be 5 feet wide exclusive of the width of curbing.

- Wheel stops are required in any proposed handicap parking spaces and any regular parking spaces adjacent to the ramps.  Provide handicap parking signs, R7-8, in front of handicap parking spaces

- The maximum length of road segment is 1320 feet.

- Show standard Henrico County end of road barricades.

- A standard R1-1 Stop Sign and 24 inch white stop bar are required at all points of egress from this development.

- Recommend standard R1-1 Stop Signs and 24 inch white stop at all internal intersections within the proposed development

- Provide and show the locations of the subdivision street name signs. The street name signs must meet the specifications in the Department of Public Works Design Manual (Section 2-38). Signs for public roads shall display a green background with white lettering while signs for private roads shall display a white background with black lettering.

- Provide and show the locations of the subdivision speed limit signs and Stop signs.

- Specify the proposed type of posts for subdivision street name signs, stop signs, speed limit signs, etc. in the public right-of-way.  If not using the standard green u-channel, square wood or square metal posts in the public right-of-way, provide a Henrico County Right-of-Way Maintenance Agreement prior to plan approval. Any non-standard sign post must be approved by the Traffic Engineer prior to plan approval.  Provide a catalog cut of any proposed non-standard sign post.

- Within subdivisions, bump-outs are required on public residential roadways with a speed limit of 25 mph or less. Bump-outs are curb extensions that reduce the travel lanes along a roadway. They are predominantly located at intersections to reduce pedestrian crossing distances but may be installed at a mid-block section of roadway. Bump-outs are also used as a traffic calming measure. Locations of bump-outs should be coordinated with Traffic Engineering. Traffic Engineering will provide an example of bump-outs upon request.

- No on-street parking will be permitted for this development on the adjacent public roads now or in the future.

- Provide intersection sight distance lines to scale on the plan for all access points onto the public right-of-way.  Provide a profile of the roadway along with the driver’s line of sight.  Show sight distance 14.5 feet from edge of travel lane.  Adequate sight distance must be demonstrated prior to Public Works’ approval of this plan… Sight lines need to be verified prior to PC approval.

- Sight Distance easements will be required for the proposed access points where the sight distance line is outside the proposed right-of-way. All easements need to be shown and identified on the plans.

- Sight Distance lines and easements shall remain free of all structures, trees, shrubbery, and signs that are higher than 30” above the ground where the sight distance originates, except utility poles, fire hydrants, and traffic control signs…Reference made to on street parking and the street trees proposed along the ring road per landscape plans. Dedicated on-street parking spaces shall not obstruct the sight lines looking onto the public road.

- For developments with more than one business or greater than 82 units, a minimum of 150 feet to the first point of conflict is required at the proposed entrances from a public street.

- All two-way drive aisles need to be a minimum of 24 feet wide and a maximum of 30 feet wide.  Call out the dimensions on the southern, east-west running drive aisle on plans.

- All one-way drive aisles need to be a minimum of 18 feet wide.  Henrico County Division of Fire may require 20 feet.

- Dedicated turn around spaces with adequate back-out room are required in any dead end of rows of parking.  Label the striped out turn around space and NO PARKING sign on the plan.

- Bollards are needed for vehicular protection for any proposed doors that swing into the proposed drive aisles around the proposed building.  Details for the bollards need to be shown on the plans.

- Show truck movements on the plan…On the plans, provide truck movements for the loading dock to the southwest of the property according to email attachment Traffic Engineering received on 2/23/22. I believe the detail was originally sent to Planning on 2/18/22.

- Provide a maintenance of traffic plan for all work proposed in the public right-of-way.

- Improvements along ... (State Route ...) must be approved by the Department of Transportation.

- A note needs to be included on the plans indicating: “A traffic signal exists at the intersection of 			 and 		           	. The contractor shall contact the Traffic Engineering Signal Shop at (804) 727-8303 with any questions pertaining to the signal. A Miss Utility ticket shall be called in to field locate traffic control equipment and cables at least 72 hours prior to beginning work on or adjacent to the right-of-way within 500 feet of the intersection. The contractor or developer will be responsible for the cost of repair or replacement of any damaged traffic control equipment.”

- A note needs to be included on the plans indicating: “If there are any Henrico County maintained signs within the construction limits that the contractor feels are in the way, please contact Traffic Engineering at (804) 727-8296 for removal and re-installation.”

- The developer is responsible for all costs associated with modifying any existing traffic signal adjacent to the site.

- A note needs to be included on the plans indicating: “The contractor is responsible for installing all stop signs, directional signs, and striping shown on the plans.”

- A note needs to be included on the plans indicating: “Coordinate in the field with Henrico County Traffic Engineering at 804-727-8282 regarding the striping and arrows on the ring road before installation."

- Show proposed striping and arrows on the plan for the ring road. See comment #51 for more detail.

- Provide evidence that VDOT has reviewed the current scope of work shown on the plan and has no comments regarding the proposed work.

- Additional comments may follow upon review of a subsequent submittal.

ADDITIONAL PLAN COMMENTS:

General:

- In pursuit of DPW’s current plan on bike lanes and shared use paths, a neighboring development (Virginia Center Commons Townhomes) is planning to restripe the ring road along its frontage (near this site) to include bike lanes. Presently, the bike striping is planned to carry up to THIS site’s western limits.

  - (3/3/22): Based on this plan and the recently received Virginia Center Commons Conceptual Master Plan, bike accommodations along the ring road are missing. The ring road and bike/pedestrian accommodations need to be clarified and coordinated between the VCC Townhomes project and the overall conceptual master plan for VCC (including this apartment project). Coordinate with VCC Townhomes project engineer: David Ellington regarding bike accommodations. David can be reached at: david.ellington@kimley-horn.com; 804-672-4708.

  - The Director of Public Works has stated that if on-street parking is to be added along this portion of the ring road, a shared use path needs to be provided on the northern side of the ring road.

    - A center turn lane should be provided for the three-lane section of roadway.

Sheet C2.3 (Site Plan):

- Per the VCC Condominium plan (referenced in comment #51), please extend sidewalk to the west enough to provide a curb ramp in alignment with Condominium project’s nearest ramp anticipated on the other side of the ring road. (3/3/22): Call out the ramp on the plans. Show proposed ramp and other improvements across the street to ensure ramps align.

- At the westernmost internal intersection, I am concerned about the proposed alignment and stop conditions. It appears motorists travelling from the internal parking lot to the west (driving SB to the intersection) are given the right-of-way through the oblong intersection. Are motorists traveling west from the eastern half of the intersection intended to stop, then proceed with caution into the intersection? This looks like two intersections being made into one.

Sheet C11.1 (Traffic-MOT):

- Per the note: “ACTIVE WORK ZONE HOURS SHALL BE ACCORDING TO THE PROFFERED RESTRICTIONS REQUIRED FOR THIS PROJECT”. I could not find a proffer specifying restricted work hours. Please clarify where I find this.

- Provide the following notes on the MOT page:

  - Except for emergencies, no lane closures or other traffic restrictions shall be erected during periods of inclement weather.

  - The Contractor shall coordinate all lane closures with Henrico Police/Fire (804-501-5000) and Pupil Transportation/ Schools (804-226-5570).

  - The Contractor is responsible for the maintenance of all signs and posts in the work zone.  This includes, but is not limited to, stop, yield, street name and speed limit signs.  Any sign or post damaged during construction or missing shall be replaced by the Contractor at his expense.

  - The Traffic Engineer (804-727-8282) reserves the right to modify the traffic control as necessary in the interests of public safety and/or convenience.

  - Unless otherwise approved, no equipment or materials are to be left in the County right-of-way after work hours.  Should permission be given to allow equipment and materials in the right-of-way after work hours, group II channelizing devices (plastic barrels with prismatic sheeting) shall be used to delineate the obstacles.  Equipment and materials shall be placed in areas that would have no adverse impact to the property owners and shall not obstruct any sight distances or create any other safety issues.

  - All employees exposed to vehicular traffic shall be provided with and instructed to wear warning vests marked with or made of reflectorized or high visibility materials meeting Class III standards.

- How will TTC-5.2 and TTC-23.2 apply for the work proposed? The existing ring road is 4-lanes, undivided. The current proposed stormwater work looks as though it would require shutting down half (if not more) of the existing roadway.

- A narrative/sequence for the maintenance of traffic plan is needed.

Please let me know if you have any questions.

Thanks,

Brandon House, E.I.T.

Traffic Review Engineer

County of Henrico - Department of Public Works
P.O. Box 90775 Henrico, VA 23273-0775

804.501.4661 phone | 804.501.7470 fax

hou018@henrico.us | www.henrico.us/works/traffic/